|  | United Nations | ECE/TRANS/WP.29/2010/69 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 8 April 2010 English Original: English and French |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-fifty-first session

Geneva, 22 – 25 June 2010

Item 4.2.9 of the provisional agenda

1958 Agreement - Consideration of draft

amendments to existing Regulations

Proposal for Supplement 2 to Regulation No. 89 (Speed limitation devices)

Submitted by the Working Party on Brakes and Running Gear*

The text reproduced below was adopted by the Working Party on Brakes and Running Gear (GRRF) at its sixty-seventh session in order to include vehicles of category M2 in the scope of the Regulation. It is based on ECE/TRANS/WP.29/GRRF/2010/4, not amended (ECE/TRANS/WP.29/GRRF/67, para. 27). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Paragraph 1.1.1., amend to read:

“1.1.1.		Part I: Vehicles of categories 1/ M2, M3, N2 and N3 2/ equipped with an SLD and to vehicles of categories M and N equipped with an adjustable speed limitation device ASLD which have not been separately approved according to Part III of this Regulation, or to vehicles so designed and/or equipped that their component parts can be regarded as totally or partially fulfilling the function of an SLD or ASLD, as appropriate.”

Paragraph 1.1.2., amend to read:

“1.1.2.	Part II: The installation on vehicles of categories M2, M3, N2 and N3 of SLDs and installation on vehicles of categories M and N of ASLD which have been type approved to Part III of this Regulation.”

Paragraph 1.1.3., amend to read:

“1.1.3.	Part III: SLDs which are intended to be fitted to vehicles of categories M2, M3, N2 and N3 and ASLD which are intended to be fitted to vehicles of categories M and N.”

Paragraph 1.2.1., amend to read:

“1.2.1.	A speed limitation device (SLD) or function (SLF) shall limit the maximum speed of vehicles of categories M2, M3, N2 and N3.”

Paragraph 1.2.2., amend to read:

“1.2.2.	When fitted, the adjustable speed limitation device (ASLD) or function (ASLF) shall limit the speed of vehicles of categories M and N to a speed voluntarily set by the driver when it is activated.”

Delete paragraph 1.2.3.

Paragraph 5.1., amend to read:

“5.1.	Requirements for vehicles of categories M2, M3, N2 and N3 equipped with SLF”

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.