| Transmitted by the expert from the Russian Federation | Informal Document No. GRB-51-10 51st GRB, 15-17 February 2010, Agenda Item 2 |
| --- | --- |
|  | ENGLISH Original: RUSSIAN |

COMMENT BY THE RUSSIAN FEDERATION

IN REGARDS TO THE PROPOSAL BY CHINA

FOR THE DRAFT AMENDMENTS TO THE REGULATION No. 28

(document ECE/TRANS/WP.29/GRB/2010/2)

In the framework of check and evaluation of proposal by China in the document TRANS/WP.29/GRB/2010/2, the Technical Service of the Russian Federation has conducted tests of the audible warning devices, primarily made by the Russian and Chinese manufacturers.  The test results have shown:

- The audible warning devices made in the Russian Federation comply with the requirements of the paragraph 6.2.7.1. of the Regulation No.28.

- The audible warning devices made in the European and Asian countries having the type approval in most cases satisfy the requirements of the paragraph 6.2.7.1. of the Regulation No.28, except for the audible warning devices made in China.  However in connection with an uncertainty in what complete set they had been tested for the type approval purpose, such devices also can be considered as complying to the Regulation No.28, once the test results had reached the admissible limit.

- The audible warning devices made in China and not having the type approval in the majority cases were not in compliance with the Regulation No.28.

Taking into account the aforesaid the Russian Federation experts do not see a necessity for amending the paragraph 6.2.7 of the Regulation No.28 reducing thereby the requirements on the level of the sound pressure to the frequency range, which is most perceived by a human ear.  Correctly designed audible warning devices have a double stock on levels in such frequency range in relation to the requirement of 105 dBA which is set in the paragraph 6.2.7.1. of the Regulation No.28.

For the time being the limited number of tests made by our Technical Service, does not allow to draw unequivocal conclusions concerning conformity to the requirements of the Regulation No.28 of the audible warning devices having the official type approval.

A concern of incompliance to the requirements of the Regulation No.28 of the audible warning devices is considered as a concern of the manufacturer not satisfying the conditions for provision of conformity of production.  Such a fact cannot form the basis for modification of the Regulation No.28.

Annex: Test results.

| Test Results of Audible Warning Device for compliance with the requirements of paragraph 6.2.7. of the UNECE Regulations No.28 |
| --- |
| No. of the audible warning device | Country of origin | Availability of approval mark | Nominal Voltage, V | Test Results | Total Sound Pressure Level at 13/26 V (Permissible Level < 118 dB (A)) | Inspection Result |
|  |  |  |  | Sound Pressure Level in the band |  |  |
|  |  |  |  | 1800-3550 Hz (Permissible Level > 105 dB (A)) |  |  |
|  |  |  |  | 11.4/22.8 V | 13.0/26.0 V | 13.8/27.6 V |  |  |
| 1. | Russia | Yes | 12 | 109.6 | 112.7 | 113.5 | 113.8 | Satisfy the requirements |
| 2. | Russia | Yes | 12 | 108.8 | 109.7 | 110.1 | 110.2 | Satisfy the requirements |
| 3. | Russia | Yes | 12 | 107.8 | 110.2 | 111.9 | 111.0 | Satisfy the requirements |
| 4. | Russia | Yes | 12 | 106.0 | 110.5 | 115.9 | 110.7 | Satisfy the requirements |
| 5. | Russia | Yes | 12 | 107.2 | 111.5 | 115.9 | 111.5 | Satisfy the requirements |
| 6. | Russia | Yes | 12 | 107.7 | 109.3 | 109.5 | 109.5 | Satisfy the requirements |
| 7. | Spain | Yes | 24 | 108.4 | 109.9 | 111.6 | 109.9 | Satisfy the requirements |
| 8. | Korea | Yes | 24 | 107.2 | 108.7 | 108.7 | 109.3 | Satisfy the requirements |
| 9. | Korea | Yes | 12 | 109.7 | 111.6 | 111.1 | 111.8 | Satisfy the requirements |
| 10. | China | Yes | 12 | 103.7 | 104.6 | 105.2 | 105.4 | Below limits |
| 11. | China | Yes | 12 | 105.4 | 105.7 | 105.8 | 106.4 | Satisfy the requirements |
| 12. | China | Yes | 12 | 105.5 | 108.2 | 108.7 | 108.6 | Satisfy the requirements |
| 13. | China | Yes | 12 | 104.7 | 105.8 | 105.2 | 105.8 | Below limits |
| 14. | China | Yes | 12 | 79.1 | 100.1 | 99.5 | 100.4 | Below limits |
| 15. | China | Yes | 12 | 106.0 | 105.2 | 105.0 | 105.8 | Satisfy the requirements |
| 16. | China | No | 12 | 93.5 | 98.4 | 100.2 | 104.7 | Below limits |
| 17. | China | No | 12 | 93.0 | 98.4 | 101.5 | 101.9 | Below limits |
| 18. | China | No | 12 | 94.2 | 99.6 | 101.6 | 104.7 | Below limits |
| 19. | China | No | 24 | 101.5 | 105.8 | 106.7 | 106.6 | Below limits |
| 20. | China | No | 24 | 101.3 | 102.6 | 104.6 | 103.2 | Below limits |
| 21. | China | No | 24 | 105.6 | 108.7 | 110.1 | 109.2 | Satisfy the requirements |
| 22. | China | No | 24 | 95.7 | 98.2 | 100.9 | 101.4 | Below limits |
| 23. | China | No | 24 | 92.5 | 96.6 | 98.3 | 103.3 | Below limits |
| 24. | China | No | 24 | 95.1 | 98.9 | 101.1 | 104.4 | Below limits |

Audible Warning Device No.1

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 81.9 112.7 101.0 Sound Level, dB (A) 113.8 Sound Level , dB (L) 112.2 |
| --- | --- |

Audible Warning Device No.2

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 83.7 109.7 99.5 Sound Level, dB (A) 110.2 Sound Level , dB (L) 109.2 |
| --- | --- |

Audible Warning Device No.3

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 82.3 110.2 104.8 Sound Level, dB (A) 111.0 Sound Level , dB (L) 110.2 |
| --- | --- |

Audible Warning Device No.4

|  | Sound Pressure Level, dB (A)) f<1800 Hz (1800- 3550) Hz f>3550 Hz 87.0 110.5 95.8 Sound Level, dB (A) 110.7 Sound Level , dB (L) 109.8 |
| --- | --- |

Audible Warning Device No.5

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 81.1 111.5 95.2 Sound Level, dB (A) 111.5 Sound Level , dB (L) 110.4 |
| --- | --- |

Audible Warning Device No.6

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 84.8 109.3 96.0 Sound Level, dB (A) 109.5 Sound Level , dB (L) 108.3 |
| --- | --- |

Audible Warning Device No.7

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 88.0 109.9 99.9 Sound Level, dB (A) 110.3 Sound Level , dB (L) 109.3 |
| --- | --- |

Audible Warning Device No.8

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 81.1 108.7 100.6 Sound Level, dB (A) 109.3 Sound Level , dB (L) 108.4 |
| --- | --- |

Audible Warning Device No.9

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 87.1 111.6 97.1 Sound Level, dB (A) 111.8 Sound Level , dB (L) 110.8 |
| --- | --- |

Audible Warning Device No.10

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 74.7 104.6 97.3 Sound Level, dB (A) 105.4 Sound Level , dB (L) 104.7 |
| --- | --- |

Audible Warning Device No.11

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 79.2 105.7 98.0 Sound Level, dB (A) 106.4 Sound Level , dB (L) 105.6 |
| --- | --- |

Audible Warning Device No.12

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 79.8 108.2 98.5 Sound Level, dB (A) 108.6 Sound Level , dB (L) 107.8 |
| --- | --- |

Audible Warning Device No.13

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 84.2 105.0 97.5 Sound Level, dB (A) 105.8 Sound Level , dB (L) 105.2 |
| --- | --- |

Audible Warning Device No.14

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 78.3 100.1 88.5 Sound Level, dB (A) 100.4 Sound Level , dB (L) 99.8 |
| --- | --- |

Audible Warning Device No.15

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 84.7 105.2 97.3 Sound Level, dB (A) 105.8 Sound Level , dB (L) 105.2 |
| --- | --- |

Audible Warning Device No.16

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 103.3 98.4 90.7 Sound Level, dB (A) 104.7 Sound Level , dB (L) 104.4 |
| --- | --- |

Audible Warning Device No.17

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 99.2 98.4 82.4 Sound Level, dB (A) 101.9 Sound Level , dB (L) 101.7 |
| --- | --- |

Audible Warning Device No.18

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 103.0 99.6 86.5 Sound Level, dB (A) 104.7 Sound Level , dB (L) 104.7 |
| --- | --- |

Audible Warning Device No.19

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 97.3 105.8 93.3 Sound Level, dB (A) 106.6 Sound Level , dB (L) 105.8 |
| --- | --- |

Audible Warning Device No.20

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 88.8 102.6 92.6 Sound Level, dB (A) 103.2 Sound Level , dB (L) 102.7 |
| --- | --- |

Audible Warning Device No.21

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 97.5 108.7 96.3 Sound Level, dB (A) 109.2 Sound Level , dB (L) 108.4 |
| --- | --- |

Audible Warning Device No.22

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 98.3 98.2 84.6 Sound Level, dB (A) 101.4 Sound Level , dB (L) 101.2 |
| --- | --- |

Audible Warning Device No.23

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 102.2 96.6 85.3 Sound Level, dB (A) 103.3 Sound Level , dB (L) 103.4 |
| --- | --- |

Audible Warning Device No.24

|  | Sound Pressure Level, dB (A) f<1800 Hz (1800- 3550) Hz f>3550 Hz 102.9 98.9 85.6 Sound Level, dB (A) 104.4 Sound Level , dB (L) 104.4 |
| --- | --- |

-----