Proposal for Corrigendum 3 to Supplement 18 to the 01 series of amendments to Regulation No. 6 (Direction indicators)

The modifications to the existing text of the Regulation are marked in bold characters.

I.	Proposal

Annex 1, amend to read:

“………

Category 1a:	for use at a distance greater than 20 mm but less than 40 mm from the dipped-beam headlamp and/or the front fog lamp;

Category 1b: 	for use at a distance less than or equal to 20 mm from the dipped-beam headlamp and/or the front fog lamp.

………”

II.	Justification

In Regulation No. 6, any front direction indicator lamp used at a distance less than 20 mm from dipped-beam headlamp and/or front fog lamp is defined as Category 1b and also greater than 20mm but less than 40mm is defined as Category 1a. A distance of 20 mm isn’t included in neither Category 1b nor Category 1a. Meanwhile, in Regulation No. 48, a distance of 20mm is included in Category 1b. Hence, the requirement of Regulation No. 6 should be aligned with the one of Regulation No. 48.