|  |  | Comments to GTR Draft SGS-10-13 | Status: 11.10.2010 |
| --- | --- | --- | --- |
| AI | Paragraph/figure/table | Recommendation | Comment/Justification |
| 15 | B5.1.4.1. + Remark B.5.2.4. | The localized fire test is needed for hydrogen storage containers (both CGH2 and LH2) whose concept for protection from overpressure is based on thermally activated PRD’s. For hydrogen storage containers with pressure activated PRD’s the bonfire test has to be performed and no localized fire test is needed. | Since this is a special issue of thermally activated PRD’s, the localized fire test should only be mandatory for hydrogen storage containers (both CGH2 and LH2) which are equipped only with a thermally activated PRD. |
|  |  |  | Cryogenic tanks always have a mechanical PRD (safety valve). |
| Rem | B.6.1.2.6. b Page 57 | Delete list of materials. | Requirements for material compatibility should be defined, but no design restrictive list of materials (hinders development of new concepts). |