|  | United Nations | ECE/TRANS/WP.29/2011/112 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 2 August 2011 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on General Safety Provisions

One-hundred-and-fifty-fifth session

Geneva, 15–18 November 2011

Item 4.7.7 of the provisional agenda

1958 Agreement – Consideration of draft amendments 
to existing Regulations submitted by GRSG

Proposal for Supplement 6 to Regulation No. 121 (Identification of controls, tell-tales and indicators)

Submitted by the Working Party on General Safety Provisions *

The text reproduced below was adopted by the Working Party on General Safety Provisions (GRSG) at its 100th session. It is based on ECE/TRANS/WP.29/GRSG/2011/8 as amended by para. 33 of the report (ECE/TRANS/WP.29/GRSG/79, para. 33). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

I.	Proposal

Table 1, amend to read:

"

| 2. | Headlamp passing beams | 1/, 6/, 13/ | Control | No | - |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Tell-tale | Yes | Green |
| 3. | Headlamp driving beams |  | Control | No | - |
|  |  | 1/ 13/ | Tell-tale | Yes | Blue |

"

Paragraph 2.5., amend to read:

"2.5.	"Tell-tale" means an optical signal that, when alight, indicates the actuation or deactivation of a device, a correct or defective functioning or condition, or a failure to function."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.