|  | INF. 9 |
| --- | --- |
| Economic Commission for Europe Inland Transport Committee Working Party on the Transport of Dangerous Goods Joint Meeting of Experts on the Regulations annexed to the European Agreement concerning the International Carriage of Dangerous Goods by Inland Waterways (ADN) (ADN Safety Committee) Twentieth session Geneva, 23-27 January 2011 Item 4 (b) of the provisional agenda Proposed amendments to the Regulations annexed to ADN: Other proposals | 8 November 2011 |

2.2.2.2.2

Transmitted by the Government of the Netherlands

I.	 Introduction

1.	Article 3.2.3 of Table C contains a list of substances which are allowed to be carried in tank vessels. One of the entries in Table C is 9000 Ammonia, deeply refrigerated.

2. 	However, article 2.2.2.2.2 states that the following substances and mixtures shall 		not be accepted for carriage: "Refrigerated liquefied gases which cannot be assigned to 		classification codes 3A, 3O or 3F". Ammonia cannot be assigned to one of these three 		categories.  As a consequence ammonia is prohibited from carriage.

II.	Proposal for amendment

On this basis, the following amendment is proposed:

2.2.2.2.2 fourth indent, amend to read:

	"Refrigerated liquefied gases which cannot be assigned to classification codes 3A, 3O or 3F, with the exception of substance identification number 9000 AMMONIA, DEEPLY REFRIGERATED of classification code 3TC in tank vessels."