Table 1: The sub-categories suggestion from China (Chinese Style)

| Vehicle Category | Sub-category | Limit value (Phase 1st) | Limit value (Phase 2nd) |
| --- | --- | --- | --- |
| M1* | GVM≤2 500kg | 72 | 71 |
|  | GVM＞2 500kg | 73 | 72 |
| M2** | GVW≤3 500 kg | 74 | 73 |
|  | GVW>3 500 kg | 76 | 75 |
| M3** | Vehicle length≤7 500mm | 78 | 76 |
|  | 7 500mm ＜Vehicle length ≤ 10 000mm | 80 | 79 |
|  | Vehicle length>10 000mm | 81 | 80 |
| N1* | Front axle drive | 72 | 71 |
|  | Rear or two axles drive | 74 | 73 |
| N2** | GVW≤7 500 kg | 78 | 77 |
|  | GVW>7 500 kg | 79 | 78 |
| N3** | GVW≤17 000 kg | 81 | 80 |
|  | GVW>17 000 kg | 82 | 81 |

Additional items (All the three additional items upwards can be accumulated.):

1. Increased by 1 dB(A) for M1, M2（GVW≤3.5t）and N1 equipped with a compression-ignition and directinjection internal combustion engine;

2. Increased by 1 dB(A) for M1 categories vehicles with the PMR values higher than 120 kW/t, and increased by 2dB(A) with the PMR values higher than 160 kW/t.

3. Increased by 1 dB(A) for M1 and N1 categories with rear axle drive or more than one drive axle;

4. ** Increased by 1 dB(A) for M2, M3, N2, N3 with more than one drive axle;

5. Increased by 1 dB(A) for All vehicle categories with more than two axles.

Table 2: The sub-categories suggestion from China (Chinese Style)

| Vehicle Category | Sub-category | Limit value (Phase 1st) | Limit value (Phase 2nd) |
| --- | --- | --- | --- |
| M1* | Front axle drive | 72 | 71 |
|  | Rear or two axles drive | 73 | 72 |
| M2** | GVW≤3 500 kg | 74 | 73 |
|  | GVW>3 500 kg | 76 | 75 |
| M3** | Vehicle length≤7 500mm | 78 | 76 |
|  | 7 500mm ＜Vehicle length ≤ 10 000mm | 80 | 79 |
|  | Vehicle length>10 000mm | 81 | 80 |
| N1* | Front axle drive | 72 | 71 |
|  | Rear or two axles drive | 74 | 73 |
| N2** | GVW≤7 500 kg | 78 | 77 |
|  | GVW>7 500 kg | 79 | 78 |
| N3** | GVW≤17 000 kg | 81 | 80 |
|  | GVW>17 000 kg | 82 | 81 |

Additional items (All the three additional items upwards can be accumulated.):

1. Increased by 1 dB(A) for M1, M2（GVW≤3.5t）and N1 equipped with a compression-ignition and directinjection internal combustion engine;

2. Increased by 1 dB(A) for M1 categories vehicles with the PMR values higher than 120 kW/t, and increased by 2dB(A) with the PMR values higher than 160 kW/t.

3. ** Increased by 1 dB(A) for M2, M3, N2, N3 with more than one drive axle;

4. Increased by 1 dB(A) for All vehicle categories with more than two axles.

Table 3: The sub-categories suggestion from China (European or Japanese Style)

(Not recommended but still can accept)

| Vehicle Category | Sub-category | Limit value (Phase 1st) | Limit value (Phase 2nd) |
| --- | --- | --- | --- |
| M1* | PMR ≤ 120 kW/t | 72 | 71 |
|  | 120 < PMR ≤ 160 kW/t | 73 | 72 |
|  | PMR > 160 kW/t | 74 | 73 |
| M2** | GVW≤3 500 kg | 74 | 73 |
|  | GVW>3 500 kg | 76 | 75 |
| M3** | Pn≤110kW | 78 | 76 |
|  | 110＜Pn≤180kW | 80 | 79 |
|  | Pn ＞180kW | 81 | 80 |
| N1* | GVM≤2 500kg | 72 | 71 |
|  | GVM＞2 500kg | 73 | 72 |
| N2** | Pn≤75 kW | 78 | 77 |
|  | Pn ＞75kW | 79 | 78 |
| N3** | Pn≤225 kW | 81 | 80 |
|  | Pn＞225 kW | 82 | 81 |

Additional items (All the three additional items upwards can be accumulated.):

1. Increased by 1 dB(A) for M1, M2（GVW≤3.5t）and N1 equipped with a compression-ignition and directinjection internal combustion engine;

2. * Increased by 1 dB(A) for M1 and N1 categories with rear axle drive or more than one drive axle;

3. ** Increased by 1 dB(A) for M2, M3, N2, N3 with more than one drive axle;

4. Increased by 1 dB(A) for All vehicle categories with more than two axles.

The limit value for different vehicle categories of Chinese suggestions

| Limit value dB（A） | Vehicle categories |
| --- | --- |
|  | M1 | N1 | M2 | N2 | M3 | N3 |
| 72 |  |  |  |  |  |  |
| 73 |  |  |  |  |  |  |
| 74 |  |  |  |  |  |  |
| 75 |  |  |  |  |  |  |
| 76 |  |  |  |  |  |  |
| 77 |  |  |  |  |  |  |
| 78 |  |  |  |  |  |  |
| 79 |  |  |  |  |  |  |
| 80 |  |  |  |  |  |  |
| 81 |  |  |  |  |  |  |
| 82 |  |  |  |  |  |  |
| 83 |  |  |  |  |  |  |
| 84 |  |  |  |  |  |  |

What has been considered for the limit value of China？：

- Data base of ECE R51 / 03 series

- Data base of ECE R51 / 02 series

- The implement of ECE R 51 / 02 series

- The relationship between the 02 and 03 series

- The relationship between different vehicle categories within the limit values system of 03 series we have built up.

The limit value for different vehicle categories of Japan (GRB-56-01)

| Limit value dB（A） | Vehicle categories |
| --- | --- |
|  | M1 | N1 | M2 | N2 | M3 | N3 |
| 72 |  |  |  |  |  |  |
| 73 |  |  |  |  |  |  |
| 74 |  |  |  |  |  |  |
| 75 |  |  |  |  |  |  |
| 76 |  |  |  |  |  |  |
| 77 |  |  | ----- |  |  |  |
| 78 |  |  |  |  |  |  |
| 79 |  |  |  |  |  |  |
| 80 |  |  |  | ----- |  |  |
| 81 |  |  |  |  |  |  |
| 82 |  |  |  |  |  |  |
| 83 |  |  |  |  |  |  |
| 84 |  |  |  |  |  | ----- |

The difference between method A and method B

The database of China (168 vehicles included)

The database of Europe (from the TNO report)