|  | United Nations | ECE/TRANS/WP.29/GRPE/2012/11/Rev.1 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 27 April 2012 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on Pollution and Energy

Sixty-fourth session

Geneva, 5–8 June 2012

Item 3(c) of the provisional agenda

Light vehicles: Regulation No. 83

(emissions of M1 and N1 vehicles)

Proposal for draft amendments to the 06 series of amendments to Regulation No. 83

Submitted by the expert from the International Organization of Motor Vehicle Manufacturers*

The text reproduced below was prepared by the expert from the International Organization of Motor Vehicle Manufacturers (OICA) in order to incorporate the content of Regulation (EU) 566/2011 into the 06 series of amendments to Regulation No. 83. This document is based on Informal document GRPE-63-16, distributed at the sixty-third session of the Working Party on Pollution and Energy (GRPE) and updated as indicated in ECE/TRANS/WP.29/GRPE/63, paragraphs 26-27. The modifications to the original English text are marked using track changes. The same modifications in the French and Russian versions are marked in bold for new or strikethrough for deleted characters.

I.		Proposal

Paragraph 2.4., amend to read:

"2.4.	…

(d)	C1H1.86O0.005 for diesel (B5)

(f)	C1H2,61O0,329 for ethanol (E75)."

Insert a new paragraph 2.27., to read:

"2.27.		In the context of in use performance ratio monitoring (IUPRM), "cold start" means an engine coolant temperature (or equivalent temperature) at engine start of less than or equal to 35 °C and less than or equal to 7 K higher than ambient temperature (if available) at engine start."

Paragraph 5.2.3., Table A, amend to read:

Table A. Requirements

Application of test requirements for type approval and extensions

|  | Vehicles with positive ignition engines including hybrids | Vehicles with C.I. engines including hybrids |
| --- | --- | --- |
|  | Mono fuel | Bi fuel1 | Flex fuel1 | Flex fuel | Mono fuel |
| Reference fuel | Petrol (E5) | LPG | NG/ Biomethane | Hydrogen | Petrol (E5) | Petrol (E5) | Petrol (E5) | Petrol (E5) | Diesel (B5) | Diesel (B5) |
|  |  |  |  |  | LPG | NG/ Biomethane | Hydrogen | Ethanol (E85) | Biodiesel |  |
| Gaseous pollutants (Type I test) | Yes | Yes | Yes |  | Yes (both fuels) | Yes (both fuels) | Yes (petrol only) 2 | Yes (both fuels) | Yes (B5 only)2 | Yes |
| Particulate mass (Type I test) | Yes direct injection only | - | - |  | Yes direct injection only (petrol only) | Yes direct injection only (petrol only) | Yes direct injection only (petrol only) 2 | Yes direct injection only (both fuels) | Yes (B5 only)2 | Yes |
| Particulate number (Type I test) |  |  |  |  | - | - | - | - | Yes (B5 only)2 | Yes |
| Idle emissions (Type II test) | Yes | Yes | Yes |  | Yes (both fuels) | Yes (both fuels) | Yes (petrol only) 2 | Yes (both fuels) | - | - |
| Crankcase emissions (Type III test) | Yes | Yes | Yes |  | Yes (petrol only) | Yes (petrol only) | Yes (petrol only) 2 | Yes (petrol) | - | - |
| Evaporative emissions (Type IV test) | Yes | - | - |  | Yes (petrol only) | Yes (petrol only) | Yes (petrol only) 2 | Yes (petrol) | - | - |
| Durability (Type V test) | Yes | Yes | Yes |  | Yes (petrol only) | Yes (petrol only) | Yes (petrol only) (2) | Yes (petrol) | Yes (B5 only)2 | Yes |
| Low temperature emissions (Type VI test) | Yes | - | - |  | Yes (petrol only) | Yes (petrol only) | Yes (petrol only) 2 | Yes (both fuels)3 | - | - |
| In-service conformity | Yes | Yes | Yes |  | Yes (both fuels) | Yes (both fuels) | Yes (petrol only) 2 | Yes (both fuels) | Yes (B5 only)2 | Yes |
| On-board diagnostics | Yes | Yes | Yes |  | Yes | Yes | Yes | Yes | Yes | Yes |

1	When a bi fuel vehicle is combined with a flex fuel vehicle, both test requirements are applicable.

2	This provision is temporary, further requirements for biodiesel and hydrogen shall be proposed later on.

3	The E75 test reference fuel specified in Annex 10 shall be used.

Paragraph 5.3.7.3., the table, the text in the fourth row of the first column, amend to read:

"(a)	for petrol (E5) 1.89

(b)	for LPG 2.53

(c)	for NG/biomethane 4.0

(d)	for ethanol (E85) 2.74

(e)	for ethanol (E75) 2.61"

Paragraph 5.3.7.3., the table, the text in the sixth row of the first column, amend to read:

"(a)	for petrol (E5) 0.016

(b)	for LPG 0.0

(c)	for NG/biomethane 0.0

(d)	for ethanol (E85) 0.39

(e)	for ethanol (E75) 0.329"

Paragraph 9.1., amend to read:

"9.1.		Introduction

This paragraph sets out the tailpipe emissions and OBD (including IUPRM) in-service conformity requirements for vehicles type approved to this Regulation."

Paragraph 9.2.5.4., amend to read:

"9.2.5.4.	Where appropriate, the list of vehicle types covered within the manufacturer's information, i.e., for tailpipe emissions, the in-service family group in accordance with paragraph 9.2.1. and, for OBD and IUPRM, the OBD family, in accordance with Appendix 2 to Annex 11;"

Paragraph 9.2.5.11., amend to read:

"9.2.5.11.	The results from the manufacturer's in-service conformity procedure, including:

(a)	Identification of the vehicles included in the programme (whether tested or not). The identification shall include the following:

(i)	Model name;

(ii)	Vehicle identification number (VIN);

(iii)	Vehicle registration number;

(iv)	Date of manufacture;

(v)	Region of use (where known);

(vi)	Tyres fitted (tailpipe emissions only).

(b)	The reason(s) for rejecting a vehicle from the sample;

(c)	Service history for each vehicle in the sample (including any re-works);

(d)	Repair history for each vehicle in the sample (where known);

(e)	Test data, including the following:

(i)	Date of test/download;

(ii)	Location of test/download;

(iii)	Distance indicated on vehicle odometer;

for tailpipe emissions only;

(iv)	Test fuel specifications (e.g. test reference fuel or market fuel);

(v)	Test conditions (temperature, humidity, dynamometer inertia 	weight);

(vi)	Dynamometer settings (e.g. power setting);

(vii)	Test results (from at least three different vehicles per family);

and for IUPRM only;

(viii)	All required data downloaded from the vehicle;

(ix)	For each monitor to be reported the in-use performance ratio IUPRM."

Insert a new paragraph 9.2.5.13., to read:

"9.2.5.13.	for IUPRM sampling, the following:

(a)	the average of in-use-performance ratios IUPRM of all selected vehicles for each monitor according to paragraphs 7.1.4 and 7.1.5 of Appendix 1 to Annex 11;

(b)	the percentage of selected vehicles, which have an IUPRM greater or equal to the minimum value applicable to the monitor according to paragraphs 3.1.4 and 3.1.5 of Appendix 1 to Annex 11."

Paragraph 9.3.1., amend to read:

"9.3.1.		The information gathered by the manufacturer shall be sufficiently comprehensive to ensure that in-service performance can be assessed for normal conditions of use as defined in paragraph 9.2. The manufacturer's sampling shall be drawn from at least two Contracting Parties with substantially different vehicle operating conditions. Factors such as differences in fuels, ambient conditions, average road speeds, and urban/highway driving split shall be taken into consideration in the selection of the Contracting Parties.9.3.1. .

For OBD IUPRM testing only, vehicles fulfilling the criteria of paragraph 2.2.1. of Appendix 3 shall be included in the test sample."

Paragraph 9.3.2., amend to read:

"9.3.2.		In selecting the Contracting Parties for sampling vehicles, the manufacturer may select vehicles from a Contracting Party that is considered to be particularly representative. In this case, the manufacturer shall demonstrate to the Approval Authority which granted the type approval that the selection is representative (e.g. by the market having the largest annual sales of a vehicle family within the applicable Contracting Party). When a family requires more than one sample lot to be tested as defined in paragraph 9.3.5., the vehicles in the second and third sample lots shall reflect different vehicle operating conditions from those selected for the first sample."

Insert new paragraph 9.3.5., to read:

"9.3.5.		Sample lots"

Paragraph 9.3.5. (former), renumber as paragraph 9.3.5.1. and amend to read:

"9.3.5.1	When applying the statistical procedure defined in Appendix 4 (i.e. for tailpipe emissions), the number of sample lots shall depend on the annual sales volume of an in-service family in the territories of a regional organization (e.g. European Community), as defined in the following table:

| Registrations per calendar year | Number of sample lots |
| --- | --- |
| Up to 100,000 | 1 |
| 100,001 to 200,000 | 2 |
| Above 200,000 | 3 |

"

Insert a new paragraph 9.3.5.2., to read:

"9.3.5.2.	For IUPR, the number of sample lots to be taken is described in the table in paragraph 9.3.5.1 and is based on the number of vehicles of an OBD family that are approved with IUPR (subject to sampling).

For the first sampling period of an OBD family, all of the vehicle types in the family that are approved with IUPR shall be considered to be subject to sampling. For subsequent sampling periods, only vehicle types which have not been previously tested or are covered by emissions approvals that have been extended since the previous sampling period shall be considered to be subject to sampling.

For families consisting of fewer than 5,000 registrations that are subject to sampling within the sampling period, the minimum number of vehicles in a sample lot is six. For all other families, the minimum number of vehicles in a sample lot to be sampled is fifteen.

Each sample lot shall adequately represent the sales pattern, i.e. at least high volume vehicle types (≥ 20 per cent of the family total) shall be represented."

Paragraph 9.4., amend to read:

"9.4.		…

(d)	Decide that the in-service conformity of a vehicle type, that is part of an in-service family, is unsatisfactory and proceed to have such vehicle type tested in accordance with Appendix 3.

If, according to the IUPRM audit, the test criteria of paragraph 6.1.2. point (a) or (b) of Appendix 3 are met for the vehicles in a sample lot, the type-approval authority must take the further action described in point (d) of this paragraph."

Appendix 3, paragraph 2., amend to read:

"2.	Selection criteria

The criteria for acceptance of a selected vehicle are defined for tailpipe emissions in paragraphs 2.1. to 2.8. of this appendix and for IUPRM in paragraphs 2.1. to 2.5 of this Appendix. Information is collected by vehicle examination and an interview with the owner/driver."

Appendix 3, insert a new paragraph 2.2.1., to read:

"2.2.1.	For checking IUPRM, the test sample shall include only vehicles that:

(a)	have collected sufficient vehicle operation data for the monitor to be tested.

For monitors required to meet the in-use monitor performance ratio and to track and report ratio data pursuant to paragraph 7.6.1 of Appendix 1 to Annex 11 sufficient vehicle operation data shall mean the denominator meets the criteria set forth below. The denominator, as defined in paragraphs 7.3 and 7.5 of Appendix 1 to Annex 11 for the monitor to be tested must have a value equal to or greater than one of the following values:

(i)	75 for evaporative system monitors, secondary air system monitors, and monitors utilising a denominator incremented in accordance with paragraph 3.3.2 points (a), (b) or (c) of Appendix 1 to Annex 11 (e.g. cold start monitors, air conditioning system monitors, etc.); or

(ii)	25 for particulate filter monitors and oxidation catalyst monitors utilising a denominator incremented in accordance with paragraph 3.3.2(d) of Appendix 1 to Annex 11; or

(iii)	150 for catalyst, oxygen sensor, EG R, VVT, and all other component monitors;

(b)	have not been tampered with or equipped with add-on or modified parts that would cause the OBD system not to comply with the requirements of Annex 11."

Appendix 3, insert a new paragraph 6.1., to read:

"6.1.	The Approval Authority must request the manufacturer to submit a plan of remedial measures to remedy the non-compliance when:"

Appendix 3, Paragraph 6.1. (former), renumber as paragraph 6.1.1. and amend to read:

"6.1.1.		For tailpipe emissions more than one vehicle is found to be an outlying emitter that meets either of the following conditions:

(a)	the conditions of paragraph 3.2.3. of Appendix 4 and where both the Approval Authority and the manufacturer agree that the excess emission is due to the same cause; or

(b)	the conditions of paragraph 3.2.4. of Appendix 4 where the Approval Authority has determined that the excess emission is due to the same cause.

The Approval Authority must request the manufacturer to submit a plan of remedial measures to remedy the non-compliance."

Appendix 3, insert a new paragraph 6.1.2., to read:

"6.1.2.		For IUPRM, of a particular monitor M the following statistical conditions are met in a test sample, the size of which is determined according to paragraph 9.3.5:

(a)	For vehicles certified to a ratio of 0.1 in accordance with paragraphs 7.1.4. and 7.1.5 of Appendix 1 to Annex 11, the data collected from the vehicles indicate for at least one monitor M in the test sample either that the test sample average in-use-performance ratio is less than 0.1 or that 66 per cent or more of the vehicles in the test sample have an in-use monitor performance ratio of less than 0.1.

(b)	For vehicles certified to the full ratios in accordance with paragraphs 7.1.4 and 7.1.5. of Appendix 1 to Annex 11 the data collected from the vehicles indicate for at least one monitor M in the test sample either that the test sample average in-use performance ratio in the test sample is less than the value Testmin (M) or that 66 per cent or more of the vehicles in the test sample have an in-use performance ratio of less than Testmin (M).

The value of Testmin(M) shall be:

(i)	0. 230 if the monitor M is required to have an in-use ratio of 0,26;

(ii) 	0.460 if the monitor M is required to have an in-use ratio of 0,52;

(iii) 	0.297 if the monitor M is required to have an in-use ratio of 0,336;

according to paragraph 7.1.4. of Appendix 1 to Annex 11."

Appendix 6, paragraph 6.2., amend to read:

"6.2.	The manufacturer shall demonstrate that use of these sensors, and any other sensors on the vehicle, results in the activation of the driver warning system as referred to in paragraph 3., the display of a message indicating an appropriate warning (e.g. "emissions too high – check urea", "emissions too high – check AdBlue", "emissions too high – check reagent"), and the driver inducement system as referred to in paragraph 8.3., when the situations referred to in paragraph 4.2., 5.4. or 5.5. occur.

For the purposes of this point these situations are presumed to occur, if the applicable NOx, emission limit of Table I of section 5.3.1.4. of this Regulation, multiplied by a factor of 1.5, is exceeded. NOx emissions during the test to demonstrate compliance with these requirements shall be not more than 20 per cent higher than the values referred to in the first sentence."

Appendix 6, paragraph 7.1., amend to read:

"7.1.		Where reference is made to this paragraph, a non-erasable Parameter Identifier (PID) shall be stored identifying the reason for and the distance travelled by the vehicle during the inducement system activation. The vehicle shall retain a record of the PID for at least 800 days or 30,000 km of vehicle operation. The PID shall be made available via the serial port of a standard diagnostic connector upon request of a generic scan tool according to the provisions of paragraph 6.5.3.1 of Appendix 1 to Annex 11 to this Regulation. The information stored in the PID shall be linked to the period of cumulated vehicle operation, during which it has occurred, with an accuracy of not less than 300 days or 10,000 km."

Annex 4a, paragraph 6.6.2., amend to read:

"6.6.2.	…

For ethanol (E85) (C1H2,74O0.385)	d = 0.932 g/l

For Ethanol (E75) (C1H2,61O0,329)		d = 0.886 g/l

In the case of nitrogen oxides (NOx):	d = 2.05 g/1"

Annex 4a, paragraph 6.6.4., amend to read:

"6.6.4.	…

for Ethanol (E85)	(5d)

for Ethanol (E75)	(5e)

In these equations:

…"

Annex 10, paragraph 2., amend to read:

"2.		…

Type: Ethanol (E75)

| Parameter | Unit | Limits1 | Test method2 |
| --- | --- | --- | --- |
|  |  | Minimum | Maximum |  |
| Research octane number, RON |  | 95 | - | EN ISO 5164 |
| Motor octane number, MON |  | 85 | - | EN ISO 5163 |
| Density at 15 °C | kg/m3 | report | EN ISO 12185 |
| Vapour pressure | kPa | 50 | 60 | EN ISO 1 30 16-1 (DVPE) |
| Sulphur content3, 4 | mg/kg | - | 10 | EN ISO 20846 EN ISO 20884 |
| Oxidation stability | minutes | 360 | - | EN ISO 7536 |
| Existent gum content (solvent washed) | mg/100ml | - | 4 | EN ISO 6246 |
| Appearance shall be determined at ambient temperature or 15 °C whichever is higher. |  | Clear and bright, visibly free of suspended or precipitated contaminants | Visual inspection |
| Ethanol and higher alcohols7 | % (V/V) | 70 | 80 | EN 1601 EN 13132 EN 1451 7 |
| Higher alcohols (C 3 - C8) | % (V/V) | - | 2 |  |
| Methanol |  | - | 0,5 |  |
| Petrol5 | % (V/V) | Balance | EN 228 |
| Phosphorus | mg/l | 0,306 | EN 15487 ASTM D 3231 |
| Water content | % (V/V) | - | 0,3 | ASTM E 1064 EN 15 489 |
| Inorganic chloride content | mg/1 | - | 1 | ISO 6227 - EN 15492 |
| pHe |  | 6,50 | 9 | ASTM D 6423 EN 15490 |
| Copper strip corrosion (3h at 50 °C) | Rating | Class I |  | EN ISO 2160 |
| Acidity (as acetic acid CH3COOH) | % (m/m) |  | 0,005 | ASTM 0161 3 EN 15491 |
|  | mg/1 |  | 40 |  |
| Carbon/hydrogen ratio |  | report |  |
| Carbon/oxygen ratio |  | report |  |
| 1 The values referred to in the specifications are "true values". When establishing the value limits, the terms of ISO 4259 Petroleum products - Determination and application of precision data in relation to methods of test were applied. When fixing a minimum value, a minimum difference of 2R above zero was taken into account. When fixing a maximum and minimum value, the minimum difference used was 4R (R = reproducibility). Notwithstanding this procedure, which is necessary for technical reasons, fuel manufacturers shall aim for a zero value where the stipulated maximum value is 2R and for the mean value for quotations of maximum and minimum limits. Where it is necessary to clarify whether fuel meets the requirements of the specifications, the ISO 4259 terms shall be applied. 2 In cases of dispute, the procedures for resolving the dispute and interpretation of the results based on test method precision, described in EN ISO 4259 shall be used. 3 In cases of national dispute concerning sulphur content, either EN ISO 20846 or EN ISO 20884 shall be called up similar to the reference in the national annex of EN 228. 4 The actual sulphur content of the fuel used for the Type 6 test shall be reported. 5 The unleaded petrol content may be determined as 100 minus the sum of the percentage content of water and alcohols. 6 There shall be no intentional addition of compounds containing phosphorus, iron, manganese, or lead to this reference fuel. 7 Ethanol to meet specification of EN 15376 is the only oxygenate that shall be intentionally added to this reference fuel. |

"

Annex 11, paragraph 3.3.5., amend to read:

"3.3.5.	Manufacturers may demonstrate to the approval authority that certain components or systems need not be monitored if, in the event of their total failure or removal, emissions do not exceed the emission limits given in paragraph 3.3.2.

A particulate trap however, where fitted as a separate unit or integrated into a combined emission control device, shall be monitored at least for total failure or removal if the latter resulted in exceeding the applicable emission limits. it shall also be monitored for any failure that would result in exceeding the applicable OBD threshold limits."

Annex 11, paragraph 4.2.1., amend to read:

"4.2.1.	The authority will not accept any deficiency request that includes the complete lack of a required diagnostic monitor or of mandated recording and reporting of data related to a monitor."

Annex 11, Appendix 1, paragraphs 7.1.6. and 7.1.7., amend to read:

"7.1.6.	The manufacturer shall demonstrate to the approval authority that these statistical conditions are satisfied all monitors required to be reported by the OBD system according to paragraph 7.6. of this Appendix not later than 18 months thereafter. For this purpose, for OBD families consisting of more than 1000 registrations in the European Union or non-EU Contracting Party, that are subject to sampling within the sampling period, the process described in Annex 11 shall be used without prejudice to the provisions of paragraph 7.1.8 of this Appendix.In addition to the requirements set out in Annex 11 and regardless of the result of the audit described in paragraph 9.2., the authority granting the approval shall apply the in-service conformity check for IUPR described in Appendix I to Annex 11 in an appropriate number of randomly determined cases. "In an appropriate number of randomly determined cases" means, that this measure has a dissuasive effect on non-compliance with the requirements of Section 3 of this Annex or the provision of manipulated, false or non-representative data for the audit. If no special circumstances apply and can be demonstrated by the type-approval authorities, random application of the in-service conformity check to 5 per cent of the type approved OBD families shall be considered as sufficient for compliance with this requirement. For this purpose, type-approval authorities may find arrangements with the manufacturer for the reduction of double testing of a given OBD family as long as these arrangements do not harm the dissuasive effect of the type approval authority's own in-service conformity check on non-compliance with the requirements of Section 3 of this Annex. Data collected by EU-member States during surveillance testing programmes may be used for in-service conformity checks. Upon request, type-approval authorities shall provide data on the audits and random in-service conformity checks performed, including the methodology used for identifying those cases, which are made subject to the random in-service conformity check, to the European Commission and other type-approval authorities.

7.1.7.		For the entire test sample of vehicles the manufacturer must report to the relevant authorities all of the in-use performance data to be reported by the OBD system according to paragraph 7.6. of Appendix 1 to Annex 11 in conjunction with an identification of the vehicle being tested and the methodology used for the selection of the tested vehicles from the fleet. Upon request, the type-approval authority granting the approval shall make these data and the results of the statistical evaluation available to the European Commission and other approval authorities."

Annex 11, Appendix 1, insert a new paragraph 7.3.2., to read:

"7.3.2.	Without prejudice to requirements for the increment of denominators of other monitors the denominators of monitors of the following components shall be incremented if and only if the driving cycle started with a cold start:

(i) 	liquid (oil, engine coolant, fuel, SCR reagent) temperature sensors;

(ii) 	clean air (ambient air, intake air, charge air, inlet manifold) temperature sensors;

(iii) 	exhaust (EGR recirculation/cooling, exhaust gas turbo-charging, catalyst) temperature sensors;

The denominators of monitors of the boost pressure control system shall be incremented if the all of the following conditions are met:

(i) 	the general denominator conditions arc fulfilled;

(ii) 	the boost pressure control system is active for a time greater than or equal to 15 seconds."

Paragraphs 7.3.2. (former) to7.3.3, renumber as paragraphs 7.3.3. to 7.3.4.

Annex 11, paragraph 7.6.2., amend to read:

"7.6.2.	For specific components or systems that have multiple monitors, which are required to be reported by this paragraph (e.g. oxygen sensor bank 1 may have multiple monitors for sensor response or other sensor characteristics), the OBD system shall separately track numerators and denominators for each of the specific monitors except those monitoring for short circuit or open circuit failures and report only the corresponding numerator and denominator for the specific monitor that has the lowest numerical ratio. If two or more specific monitors have identical ratios, the corresponding numerator and denominator for the specific monitor that has the highest denominator shall be reported for the specific component."

II.		Justification

1.	The transposition of the Euro 5 requirements into Regulation 83 could not take account of the first series of amendments within the European Union as these amendments were still in discussion at the time.  These amendments have now been published in Regulation (EU) 566/2011 and, therefore, can now be transposed into Regulation 83 and return parity between the two legislations.

2.	In response to questions from the expert from Poland during the sixty-third GRPE, clarity has been introduced to the definition of "cold start".

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.