Regulation No. 13H - Status of Supplements

| Status of document | Date of entry into force | WP.29 Session (date) | Adopted document ECE/TRANS/WP.29/... | Content | Transitional provisions & Lead time | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| Suppl.6 to 00 | 15.10.08 | 144 (Mar 08) | 2008/3 + para. 33 of the report | List of vehicle data for the purpose of R90 approval | No | The latest supplement before introduction of ESC |
| Suppl.7 to 00 | 22.07.09 | 146 (Nov 08) | 2008/81 + Corr.1 | Introduction of ESC (Annex 9) | Yes 01.01.11 - national type approvals 01.11.13 - first national registration | Are those transitional provisions needed? |
| Suppl.8 to 00 | 24.10.09 | 147 (Mar 09) | 2009/6 | Reference to R64 | No |  |
| Suppl.9 to 00 | 17.03.10 | 148 (June 09) | 2009/64 | Introduction of BAS (same Annex 9) | Yes 01.01.11 - national type approvals 01.11.13 - first national registration | Are those transitional provisions needed? |
| Suppl.10 to 00 | 09.12.10 | 150 (Mar 10) | 2010/4 + Corr.1 | Activation of the emergency braking signal | No |  |
| Suppl.11 to 00 | 30.01.11 | 151 (June 10) | 2010/65 | Electric regenerative braking systems - activation of the signal | Yes 36 months - till 30.01.14 | Guidelines: “Until … months after the date of entry into force of the Supplement XX to the original version of this Regulation, Contracting Parties applying this Regulation can continue to grant UNECE type approvals to the un-amended Regulation.” |
| Suppl.12 to 00 | 28.10.11 | 153 (Mar 11) | 2011/5 | Alignment of R13H & R90 to identify replacement brake disks and drums | Yes 12 months - till 28.10.12 |  |
| Suppl.13 to 00 | [13.04.12] | 154 (June 11) | 2011/59 | Alignment of R13H & FMVSS 126 in regards to ESC malfunction tell-tale + provisions for PTI | No |  |

| Transitional provisions R13H/Rev.2 + R13H/Rev.2/Amend.1 | Source / Remark |
| --- | --- |
| 12.1. As from 1 November 2011, Contracting Parties applying this Regulation may refuse to grant national or regional type approval if the vehicle type does not meet the requirements of this Regulation as amended by Supplement 9 or Supplement 10 or Supplement 11 and is not fitted with an Electronic Stability Control System and a Brake Assist System, both meeting the requirements of Annex 9 to this Regulation. | R13H/Rev.2 |
| 12.2. As from 1 November 2013, Contracting Parties applying this Regulation may refuse first national registration of a vehicle which does not meet the requirements of this Regulation as amended by Supplement 9 or Supplement 10 or Supplement 11 and is not fitted with an Electronic Stability Control System and a Brake Assist System, both meeting the requirements of Annex 9 to this Regulation. | R13H/Rev.2 |
| 12.3. As from the official date of entry into force of the Supplement 11 (30 January 2011) to the original version of this Regulation, no Contracting Party applying this Regulation shall refuse to grant ECE approval under this Regulation as amended by Supplement 11. | R13H/Rev.2 |
| 12.4. Contracting Parties applying this Regulation shall continue to grant approvals to those types of vehicles which comply with the requirements of this Regulation as amended by Supplement 10 to the original version of this Regulation during the 36 months period which follows the date of entry into force of Supplement 11. | R13H/Rev.2 |
| [12.5. Contracting Parties applying this Regulation may continue to grant approvals to those types of vehicles which comply with the requirements of this Regulation as amended by Supplement 6 to the original version of this Regulation.] | Lost? It is allowed to grant UNECE type approval to vehicle types not fitted with ESC and BAS (“if fitted” requirement) |
| 12.6. As from the official date of entry into force of the Supplement 11 to the original version of this Regulation, no Contracting Party applying this Regulation shall refuse to grant ECE approval under this Regulation as amended by Supplement 11. | ECE/TRANS/WP.29/2010/65 Not included in R13H/Rev.2 |
| 12.7. Contracting Parties applying this Regulation shall continue to grant approvals to those types of vehicles which comply with the requirements of this Regulation as amended by Supplement 10 to the original version of this Regulation during the 36 months period which follows the date of entry into force of Supplement 11. | ECE/TRANS/WP.29/2010/65 Not included in R13H/Rev.2 |
| 12.8. As from the official date of entry into force of the Supplement 12 to the original version of this Regulation, no Contracting Party applying this Regulation shall refuse to grant approval under this Regulation as amended by Supplement 12 to the original version of this Regulation. | R13H/Rev.2/Amend.1 |
| 12.9. Contracting Parties applying this Regulation shall continue to grant approvals to those types of vehicles which comply with the requirements of this Regulation as amended by Supplement 11 to the original version of this Regulation during the 12 month period which follows the date of entry into force of supplement 12 to the original version of this Regulation. | R13H/Rev.2/Amend.1 |
| 12.10. Contracting Parties applying this Regulation shall not refuse to grant extensions of approval according to this Regulation as amended by Supplement 11 to the original version of this Regulation. | R13H/Rev.2/Amend.1 |