## Slide 1: DTP14 and GTR Drafting Progress Report
66th GRPE
6th June 2013
Informal document No. GRPE-66-36
66th GRPE, 3-7 June 2012
agenda item 3(a)
Transmitted by WLTP-DTP

## Slide 2: Overview
Good progress made since last GRPE
2 DTP meetings in Tokyo and Geneva
3 phone conferences
Several meetings of the sub-groups
On-going drafting group meetings (audio/web or f2f)
Inf. Doc GRPE-66-02: Draft GTR WLTP

## Slide 3: Sub-Group Reports
PM/PN subgroup has closed all open issues and concentrates its work on drafting.
AP subgroup has completed the work on N20 and NO2-measurement. EtOh-, NH3- and Aldehyde measurement will be added at a later stage.
EV subgroup has closed all major open issues for Phase 1 except Utility Factor (will be determined on a regional basis). Some issues still depend on the outcome of the confirmation phase. All vehicles will be classified as Class 3.
ICE subgroup has completed the new test mass approach (the method is however not yet fully validated), but still has to deal with some minor open issues.

## Slide 4: Remaining Open Issues from DTP 14
  RCB correction for low-voltage battery
  Table of running resistances
  Comparison of RLD methods
  Vehicle warm-up procedure
  Speed trace violation
  Definition of predominant mode for multimode gearboxes
  Ambient temperature for coastdown
  Temperature correction for regional representativeness

## Slide 5: 1. RCB Correction
  Issue:
  The SoC of the low voltage battery has an impact on fuel consumption. This impact shall be considered appropriately.
  Proposal:
  SoC will be monitored via OBD data for a worst case family member.
  The definition of such a family is still an open issue. Correction of fuel consumption if delta RCB> [0,5 %] on the basis Willans factors.
  Decision:
  The principles of this proposal is agreed. TÜV Nord and VW will cover the open issue of family criteria and validation procedure and present a paper to the next LabProcICE meeting.
Notes: C

## Slide 6: 2. Table of Running Resistances (red)
  Issue:
  Default values for dyno settings may be applied if the Road Load of a vehicle cannot be determined (for example via coastdown).
  Proposal:
  Default values will be calculated on the basis of Cw*A and vehicle mass. The default values should orient towards worst case.
  Decision:
  A new proposal from TNO and RDW, which is based on a physical model to determine the road load and which applies an additional 3kW margin is estimated to be a promising approach. The group agrees to continue the RLD based approach. However additional data is requested. LabProc ICE is asked to continue to work on this approach until August. At least the principle approach/procedure has to be agreed until August in order to bring it into the GTR. Parameter definition could be postponed to November – if Steering Group agrees.
  As a fallback solution there will be regional default tables.
Notes: C

## Slide 7: 3. Comparison of RLD Methods
  Issue:
  Apart from the coastdown there are other methods to determine the road load (torque meter, wind tunnel measuring)
  Proposal:
  The new RLD methods should be allowed, if the equivalency and accuracy of the new methods can be shown.
  The torque meter method has been proven to be equivalent to the coastdown method.
  Decision:
  Torque meter and coastdown methods will be included in the GTR. Wind tunnel method can become a subject at a later stage.

## Slide 8: 4. Warm-Up Procedure (red)
  Issue:
  Preconditioning of the vehicle for RLD and for dyno load setting.
  Proposal:
  The majority of the LabProcICE experts are in favour of defining stable vehicle conditions as a recommendation for warm-up. Japanese experts prefer a dedicated warm-up procedure.
  Decision:
  LabProcICE experts presented a new approach based on a WLTC warm-up cycle for dyno load setting; LabProcICE is asked to work out this approach and to provide a document before August.
Notes: C

## Slide 9: 5. Speed Trace Violation
  Issue:
  Deviations occuring outside the prescribed tolerances when following the speed trace of the test cycle.
  Proposal:
  The LabProcICE proposal is in principle accepted, but values have to be confirmed. It is still unclear how to deal with vehicles which cannot follow the cycle.
  Decision:
  The proposal is welcomed by the group. India proposes to allow 1 % time deviation instead 10 deviations. The DHC Secretary accepted to introduce a common proposal on the basis of the LabProcICE work. This proposal will also take into consideration vehicles that cannot follow the cycle.
Notes: C

## Slide 10: 6. Definition of Predominant Mode
  Issue:
  Vehicles with multi-mode gearboxes shall be tested in the predominant mode. Therefore, a stable definition is needed.
  Proposal:
  LabProcICE has worked out a definition. NL still has reservations and is asked to come up with an improved definition.
  Decision:
  Despite the fact that the wording of the definition of the predominant mode is not perfect, the DTP group agrees to accept the current definition of the predominant mode.
Notes: C

## Slide 11: 7. Ambient Temperature for coastdown
  Issue:
  Definition of an allowed temperature range for coastdown.
  Proposal:
  EU proposes 5-35°C; India proposes 5-45°C. If no agreement can be found, the temperature range could be defined on a regional basis.
  Decision:
  A compromise proposal by India to restrict the temperature range up to 40°C could be acceptable by contracting parties. This could be accepted by EU-COM with the addition, that deviations of +/- 5°C are allowed. OICA has reservations of possible disharmonisation.

## Slide 12: 8. Temperature Correction for Regional Representative Conditions
  Issue:
  Supplemental test for determination of CO2 under representative regional conditions.
  Proposal:
  Additional vehicle test under representative conditions for a representative family. The details of such a concept still have to be worked out.
  Decision:
  The principles of such an additional test are accepted. OICA will present a stable test procedure as well as a family concept and a validation program by the end of July.
  The procedure still has to be validated. EVs shall also be taken into account.
Notes: C

## Slide 13
GTR available as an informal document on the GRPE site
GTR uploaded regularly to the UNECE website
Formation of drafting group consisting of representatives of the subgroups PM/PN, additional pollutants, electrified vehicles, lab procedures, steering group, contracting parties
Purpose, scope, application: covers only mono-fuel, ICE and EV vehicles
Drafting Overview

## Slide 14
Road and dynamometer load
  Masses
  Vehicle selection
  Tyre selection
Vehicle warming up
Tyre slip on dyno
Running resistance table
Symbols and abbreviations: too extensive in current GTR
Latest cycle and shifting recommendation material to be integrated
Major Open Drafting Points

## Slide 15
Before end of June: Results from this GRPE to be analysed and incorporated into the GTR
End of June: f2f drafting group meeting in Brussels
Early July: Draft to be sent to WLTP members with comments expected no later than July 19
July 19 to last week of July: Incorporation of comments received above
Last week of July: Drafting group meeting (either f2f or audio/web)
August 1 - 21: Finalisation of draft
August 22: Last date for submitting a Working Document to the UN for the November 67th GRPE meeting.
November 14: 67th GRPE meeting
Mid-December: Last date for submitting a Working Document to the UN for the March meeting of WP.29/AC.3
March 2014: Possible vote on the WLTP-GTR in WP.29/AC3
Drafting Deadlines

## Slide 16
A. Statement of technical justification | B. Text of Regulation | Annexes
 | B. Text of Regulation | 1. Cycles
 | B.1. Purpose | 2. Shifting
 | B.2. Scope/Application | 3. Fuels
 | B.3. Definitions | 4. Road and dyno load
 | B.4. Symbols, abbreviations | 5. Equipment
 | B.5. General requirements | 6. Calculations
 | B.6. Performance requirements | 7. System equivalence
 | B.7. Test procedure | 
 | B.8. Electrified vehicles | 
New GTR Structure

## Slide 17: Next DTP-Meetings
Web/Phone Conference 25.7.2013 9h30-12h00 CET
Further Web/Phone conferences possible later