Japanese position for the warning requirements of AEBS

The warning requirements shall be based on the AEBS/LDWS 19-02.

- The warning requirements shall be prescribed at least 0.8 seconds as requirements for the stationary target scenario and the moving target scenario.

- The optical warning has less effect on the driver of the low wakefulness.

However, Japan is open and receptive to the following requirements as a compromise proposal, considering the early development of AEBS regulation.

Paragraph 6.4.2.1., amend to read:

“6.4.2.1.          At least one haptic or acoustic warning mode shall be provided no later than the value specified in Table I Column B of Annex 3, before the start of the emergency braking phase.

In the case of the vehicles referred to in Table I, row 1 of Annex 3, the warning shall be haptic or acoustic.

In the case of the vehicles referred to in Table I, row 2 of Annex 3, the warning shall be haptic, acoustic or optical”

Paragraph 6.5.2.1.

“6.5.2.1.	At least one haptic or acoustic warning mode shall be provided no later than the value specified in Table I Column E of Annex 3, before the start of the emergency braking phase.