| Submitted by the expert from Italy | Informal document GRSG-105-29 (105th GRSG, 8-11 October 2013 Agenda item 9.) |
| --- | --- |

Proposal to amend UN Regulation No. 110 (CNG vehicles)
(01 series of amendments)

A. Proposal

Insert a new paragraph 23.3., to read:

"23.3.	Type approvals of components other than fuel rail, as defined in paragraph 2.28., granted according to original versions of this Regulation, shall remain valid and may be used for the purpose of paragraph 23.4."

Former paragraphs 23.3. to 23.6., renumber as paragraphs 23.4 to 23.7.

B. Justification

The 01 series of amendments of UN Regulation No. 110 introduces the new fuels rail component as well as its definition, requirements and tests.

The new series of amendments does not introduce additional requirements for existing components which, without clarification, would be subject to a new type approval procedure.

Since the provisions of all other existing components remain unchanged, it should be clarified that they can continue to be fitted in vehicles pursuant to the installation requirements of UN Regulation No. 110-01 series of amendments.