|  | United Nations | ECE/TRANS/WP.15/2014/18 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 22 August 2014 English Original: French |

Economic Commission for Europe

Inland Transport Committee

Working Party on the Transport of Dangerous Goods

Ninety-seventh session

Geneva, 3–7 November 2014

Item 6 (b) of the provisional agenda

Proposals for amendments to Annexes A and B of ADR:

Miscellaneous proposals

Guideline for the certificate of approval under 9.1.3 of ADR

Transmitted by the Government of France

Summary

Executive summary: The purpose of this document is to establish a guideline for filling in the certificate of approval under 9.1.3 of ADR.

Action to be taken: Add this guideline to the website under ADR, Guidelines.

Reference documents: ECE/TRANS/WP.15/224, paragraphs 13 and 14.

Introduction

1.	At its May 2014 session, during the discussion of informal document INF.15 submitted by Ireland, the Working Party confirmed that the guidelines contained in annex 4 of the report of WP.15 of May 2001 (document ECE/TRANS/165) on how to fill in the certificate of approval for vehicles remained valid.

2.	Noting that some references had become outdated, the Working Party expressed the wish to update the guidelines and make them more visible on the Web.

Proposal

3.	Add to the website, under ADR, Guidelines, the following guideline:

Guideline for the certificate of approval under 9.1.3 of ADR

The numbered boxes on the printed version of the certificate of approval for vehicles transporting certain dangerous goods, a model of which appears in 9.1.3.5, should be filled in as follows:

1.	Certificate No.

The number should be indicated by the issuing service.

2.	Vehicle manufacturer

See the registration certificate(s).

3.	Vehicle Identification No.

See the registration certificate(s) and check the number(s) on the vehicle(s).

4.	Registration number

See the registration certificate(s). If the vehicle has still not been registered on the date of issue of the certificate of approval, leave this box blank pending registration of the vehicle.

5.	Name and business address of carrier, operator or owner

6.	Description of vehicle

In accordance with footnote 1 of the certificate, descriptions should follow the0 definitions for power-driven vehicles and for trailers of categories N and O, as defined in paragraph 2 of the Consolidated Resolution on the Construction of Vehicles (R.E.3) or in Directive 2007/46/EC.

Description of power-driven vehicles in accordance with R.E.3

| Maximum mass (Mm) | Power-driven vehicles of category N | Véhicules à moteur de catégorie N | Kraftfahrzeuge der Klasse N |
| --- | --- | --- | --- |
| Mm < 3.5t | Category N1 | Catégorie N1 | Klasse N1 |
| 3.5t < Mm < 12t | Category N2 | Catégorie N2 | Klasse N2 |
| Mm > 12t | Category N3 | Catégorie N3 | Klasse N3 |

Description of power-driven vehicles in accordance with Directive 2007/46/EC

| Maximum mass (Mm) | Motor vehicles of category N | Véhicules à moteur de catégorie N | Kraftfahrzeuge der Klasse N |
| --- | --- | --- | --- |
| Mm < 3.5t | Lorry N1 | Camion N1 | Lastkraftwagen N1 |
| 3.5t < Mm < 12t | Lorry N2 | Camion N2 | Lastkraftwagen N2 |
| Mm > 12t | Lorry N3 | Camion N3 | Lastkraftwagen N3 |
| Mm < 3.5t | Tractor N1 | Tracteur N1 | Zugmaschine N1 |
| 3.5t < Mm < 12t | Tractor N2 | Tracteur N2 | Zugmaschine N2 |
| Mm > 12t | Tractor N3 | Tracteur N3 | Zugmaschine N3 |
| Mm < 3.5t | Tractor for semi-trailer N1 | Tracteur de semi-remorque N1 | Sattelzugmaschine N1 |
| 3.5t < Mm < 12t | Tractor for semi-trailer N2 | Tracteur de semi-remorque N2 | Sattelzugmaschine N2 |
| Mm > 12t | Tractor for semi-trailer N3 | Tracteur de semi-remorque N3 | Sattelzugmaschine N3 |

Description of trailers

| Maximum Mass | Trailers | Remorques | Anhänger |
| --- | --- | --- | --- |
| Mm ≤ 0.75t | Drawbar trailer O1/ Full trailer O1* | Remorque à timon d'attelage O1 | Deichselanhänger O1 |
| 0.75t < Mm ≤ 3.5t | Drawbar trailer O2/ Full trailer O2* | Remorque à timon d'attelage O2 | Deichselanhänger O2 |
| 3.5t < Mm ≤ 10t | Drawbar trailer O3/ Full trailer O3* | Remorque à timon d'attelage O3 | Deichselanhänger O3 |
| Mm > 10t | Drawbar trailer O4/ Full trailer O4* | Remorque à timon d'attelage O4 | Deichselanhänger O4 |
| Mm ≤ 0.75t | Semi-trailer O1 | Semi-remorque O1 | Sattelanhänger O1 |
| 0.75t < Mm ≤ 3.5t | Semi-trailer O2 | Semi-remorque O2 | Sattelanhänger O2 |
| 3.5t < Mm ≤ 10t | Semi-trailer O3 | Semi-remorque O3 | Sattelanhänger O3 |
| Mm > 10t | Semi-trailer O4 | Semi-remorque O4 | Sattelanhänger O4 |
| Mm ≤ 0.75t | Centre-axle trailer O1 | Remorque à essieu central O1 | Zentralachsanhänger O1 |
| 0.75t < Mm ≤ 3.5t | Centre-axle trailer O2 | Remorque à essieu central O2 | Zentralachsanhänger O2 |
| 3.5t < Mm ≤ 10t | Centre-axle trailer O3 | Remorque à essieu central O3 | Zentralachsanhänger O3 |
| Mm > 10t | Centre-axle trailer O4 | Remorque à essieu central O4 | Zentralachsanhänger O4 |

*  “Full trailer” is the term used in R.E.3.

In accordance with 9.1.3.3, the certificate of approval for a vacuum-operated waste tank-vehicle should bear the remark: “vacuum-operated waste tank-vehicle”.

7.	Vehicle designation(s) according to 9.1.1.2 of ADR

To avoid any unauthorized tampering with the certificate, all non-conforming designations should be struck out.

It is possible to have several designations for a single vehicle. For example, a vehicle that meets the requirements for FL vehicles automatically meets the requirements for AT vehicles. In such cases both designations should appear on the certificate.

The information under number 7, together with the information under number 10, determines what goods can be transported by the vehicle.

8.	Endurance braking system

The entry “Not applicable” should be checked on certificates of vehicles for which the provisions relating to endurance braking systems do not apply owing to their low maximum mass or the low mass of their trailers, pursuant to note (b) of the table in 9.2.1.

In other cases, the second line of number 8 should be checked and the correct value indicated. In some countries the registration/in-service maximum permissible mass may exceed 44 tonnes, but under ECE Regulation No. 13, annex 5, section 2.3.1.5, the value of 44 tonnes may be considered to be sufficient, even if the overall total maximum mass is greater than 44 tonnes (see footnote 4 of the certificate).

Example: The maximum mass of a whole unit is 50 tonnes (according to the national legislation). The performance of the endurance braking system is sufficient for a maximum permissible mass of 44 tonnes. In accordance with ECE Regulation No. 13, annex 5, section 2.3.1.5, the unit may be operated with up to 50 tonnes.

9.	Description of the fixed tank(s)/battery-vehicle

See the type approval of the tank, the latest inspection report of the tank or the plate of the tank.

10.	Dangerous goods authorized for carriage

No information is required under number 10 for vehicles other than EX/II and EX/III vehicles, those fitted with a fixed tank or battery-vehicles. Such vehicles (for example, drawing vehicles of semi-trailers) may be used to transport goods with the designation appearing under number 7.

10.1	In accordance with 9.3.7.3, which relates to the electrical installation in the load compartment of  EX/II and EX/III vehicles, protection degree IP 65 is required for vehicles transporting explosives of Compatibility Group J. For other explosives, the electrical installation in the load compartment should have protection degree IP 54.

10.2	For tank-vehicles and battery-vehicles, one of the following two possibilities should be selected. Either:

A reference to the tank code under number 9.5 and to any possible special provisions TC or TE under number 9.6; or

The list of goods by Class, UN number, and if necessary packing group and proper shipping name.

11.	Remarks

Space for remarks (for example, date of the next inspection of the tank).

12.	Valid until

Indicate the expiry date and the place and date of issue. The certificate should be stamped and signed by the issuing service.

13.	Extensions of validity

As for number 12, above.

# Footnotes

The present document is submitted in accordance with paragraph 1 (c) of the terms of reference of the Working Party, as contained in document ECE/TRANS/WP.15/190/Add.1, which provides a mandate to “develop and update the European Agreement concerning the International Carriage of Dangerous Goods by Road (ADR)”.