|  | United Nations | ECE/TRANS/WP.15/222/Corr.1 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 26 May 2014 English Original: English and French |

Economic Commission for Europe

Inland Transport Committee

Working Party on the Transport of Dangerous Goods

European Agreement concerning the International Carriage of Dangerous Goods by Road (ADR)

Draft amendments to annexes A and B of ADR

Corrigendum

1.	Page 2, amendment to Part 1, Chapter 1.1, 1.1.3.6.3, in the second indent

After compressed gases insert , adsorbed gases

2.	Page 2, amendment to Part 1, Chapter 1.1, 1.1.3.6.5

For and 1.1.3.9 read , 1.1.3.9 and 1.1.3.10

3.	Page 6, amendment to Part 1, Chapter 1.6, new transitional measure 1.6.2.13

For the existing text, substitute

1.6.2.13	Bundles of cylinders manufactured before 1 July 2013 which are not marked in accordance with 6.2.3.9.7.2 and 6.2.3.9.7.3 applicable from 1 January 2013 or 6.2.3.9.7.2 applicable from 1 January 2015 may be used until the next periodic inspection after 1 July 2015.

4.	Page 6, amendment to Part 1, Chapter 1.6, new transitional measure 1.6.3.44

For the existing text, substitute

1.6.3.44	Fixed tanks (tank-vehicles) and demountable tanks intended for the carriage of UN Nos. 1202, 1203, 1223, 3475 and aviation fuel classified under UN Nos. 1268 or 1863, equipped with additive devices designed and constructed before 1 July 2015 in accordance with national provisions, but which do not, however, conform to the construction, approval and testing requirements of special provision 664 of Chapter 3.3 applicable as from 1 January 2015, may continue to be used until their first intermediate or periodic inspection after 31 December 2015. After this date, they shall only be used with the agreement of the competent authorities in the countries of use.

5.	Page 9, amendment to Part 1, Chapter 1.8, 1.8.6.8

Not applicable to English

6.	Page 20, amendment to Part 3, Chapter 3.2, Table A, UN No. 1408

For AP4 AP5 read AP3 AP4 AP5

7.	Page 21, amendments to Part 3, Chapter 3.2, Table A, UN No. 3170 (packing group II) and UN No. 3170 (packing group III)

For AP4 AP5 read AP2

8.	Page 27, amendment to Part 3, Chapter 3.3, SP594

For the existing text, substitute

SP 594	Amend to read as follows:

"594	The following articles, manufactured and filled according to the provisions applied in the country of manufacture, are not subject to the requirements of ADR:

(a)	UN No. 1044 fire extinguishers provided with protection against inadvertent discharge, when:

–	they are packaged in a strong outer packaging; or

–	they are large fire extinguishers which meet the requirements of special packing provision PP91 of packing instruction P003 in 4.1.4.1;

(b)	UN No. 3164 articles, pressurized pneumatic or hydraulic, designed to withstand stresses greater than the internal gas pressure by virtue of transmission of force, intrinsic strength or construction, when they are packaged in a strong outer packaging.

NOTE:	"Provisions applied in the country of manufacture" means the provisions applicable in the country of manufacture or those applicable in the country of use.".

9.	Page 32, amendment to Part 3, Chapter 3.3, new special provision SP663, after the third indent under “Scope”

Insert

–	Radioactive material; nor

10.	Page 32, amendment to Part 3, Chapter 3.3, new special provision SP664, at the beginning, in the second indent after “Additive devices:”

For emptying device read discharge device

11.	Page 38, amendment to Part 4, Chapter 4.1, 4.1.4.1, packing instruction P200, new paragraph (13), sub-paragraph 1.3, after the third indent

Insert

–	EN ISO 7866; or

12.	Page 41, amendment to Part 4, Chapter 4.1, 4.1.4.1, packing instruction P203

For in front of the existing provision and add read . Add

13.	Page 64, amendment to Part 5, Chapter 5.5, new paragraph 5.5.3.1.5, last sentence

Delete

14.	Page 66, last amendment to Part 6, Chapter 6.2, 6.2.2.1.1

For the existing text, substitute

For ISO 7866:1999, in the column "Applicable for manufacture", add "Until 31 December 2020" and for all the other standards, in the column "Applicable for manufacture", add "Until further notice".

15.	Amendments to Part 6, Chapter 6.2, 6.2.2.10, 6.2.2.11, 6.2.3.6.1, 6.2.4.1 and 6.2.4.2, in the French text

Not applicable to English

16.	Page 70, amendment to Part 6, Chapter 6.2, 6.2.3.9.7

For the existing text, substitute

6.2.3.9.7	Amend to read as follows:

"6.2.3.9.7	Marking of bundles of cylinders

6.2.3.9.7.1	Individual cylinders in a bundle of cylinders shall be marked in accordance with 6.2.3.9.1 to 6.2.3.9.6.

6.2.3.9.7.2	Marking of bundles of cylinders shall be in accordance with 6.2.2.10.2 and 6.2.2.10.3, except that the United Nations packaging symbol specified in 6.2.2.7.2 (a) shall not be applied.

6.2.3.9.7.3	In addition to the preceding marks, each bundle of cylinders that meets the periodic inspection and test requirements of 6.2.4.2 shall be marked indicating:

(a)	The character(s) identifying the country authorizing the body performing the periodic inspection and test, as indicated by the distinguishing sign of motor vehicles in international traffic3. This marking is not required if this body is approved by the competent authority of the country approving manufacture;

(b)	The registered mark of the body authorised by the competent authority for performing periodic inspection and test;

(c)	The date of the periodic inspection and test, the year (two digits) followed by the month (two digits) separated by a slash (i.e. "/"). Four digits may be used to indicate the year.

The above marks shall appear consecutively in the sequence given either on the plate specified in 6.2.2.10.2 or on a separate plate permanently attached to the frame of the bundle of cylinders.".

The text of footnote 3 read as follows: "3	Distinguishing signs for motor vehicles in international traffic prescribed in the Vienna Convention on Road Traffic (1968).".

17.	Page 70, amendment to Part 6, Chapter 6.2, 6.2.4.1, new entry for standard "EN ISO 3807:2013", in column (2), after the title of the standard

Insert

NOTE:	Fusible plugs shall not be fitted.

18.	Page 70, before the amendment to Part 6, Chapter 6.2, 6.2.4.1, concerning the insertion of standard "EN ISO 11120:1999 + A1:2013"

Insert

–	For standard "EN ISO 11120:1999", in column (4), replace "Until further notice" by "Between 1 July 2001 and 30 June 2015".

–	For standard "EN ISO 11120:1999", in column (5), add the following new text: "31 December 2015 for tubes marked with the letter "H" in accordance with 6.2.2.7.4 (p)".

19.	Page 73, second amendment to Part 6, Chapter 6.4, 6.4.6.4 (starting with "In (a) and (b)…")

For the existing text, substitute

6.4.6.4		In (a) and (b) delete "The packages are designed".

6.4.6.4		In (a), add "and/or" at the end and in (b), replace "or" by "and/or".

20.	Page 81, amendment to Part 6, Chapter 6.5, 6.5.2.2.2, in the introductory text before the figures

For Figure 6.5.2.2.1 or Figure 6.5.2.2.2 read Figure 6.5.2.2.2.1 or Figure 6.5.2.2.2.2

21.	Page 84, amendment to Part 6, Chapter 6.8, 6.8.2.2.3

Not applicable to English

22.	Amendment to Part 6, Chapter 6.8, 6.8.2.6.1, 6.8.2.6.2, 6.8.3.6, 6.8.4 TA4 and TT9

Not applicable to English

23.	Pages 86 and 87, amendments to Part 7, Chapter 7.3, 7.3.3.2.1 and 7.3.3.2.7, additional provision AP2

For the existing text, substitute

AP2	Vehicles and containers shall have adequate ventilation.

24.	Page 86, amendment to Part 7, Chapter 7.3, 7.3.3.2.3, before additional provision AP3

Insert

AP2	Vehicles and containers shall have adequate ventilation.

25.	Page 89, amendment to Part 9, Chapter 9.2, 9.2.2.5.1 (a)

Delete and renumber accordingly the footnotes in Chapter 9.2