|  | United Nations | ECE/TRANS/WP.29/2014/17 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 18 December 2013 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

162nd session

Geneva, 11-14 March 2014

Item 4.9.5 of the provisional agenda

1958 Agreement – Consideration of draft amendments

to existing Regulations submitted by GRE

Proposal for Supplement 6 to the 04 series of amendments to Regulation No. 19 (Front fog lamps)

Submitted by the Working Party on Lighting and Light-Signalling *

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its seventieth session (ECE/TRANS/WP.29/GRE/70, para. 49). It is based on ECE/TRANS/WP.29/GRE/2013/66, not amended. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee AC.1 for consideration.

Paragraph 14.2., amend to read:

"14.2.		As from the date of entry into force of Supplement 2 to the 04 series of amendments, Contracting Parties applying this Regulation shall refuse to grant approvals for new types of Class B front fog lamps. However, Contracting Parties applying this Regulation shall continue to issue approvals for Class B front fog lamps on the basis of the 02, 03 and 04 series of amendments provided that these front fog lamps are only intended as replacements for fitting to vehicles in use."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2012–2016 (ECE/TRANS/224, para. 94 and ECE/TRANS/2012/12, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.