|  | United Nations | ECE/TRANS/WP.29/GRE/2014/13 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 17 January 2014 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on Lighting and Light-Signalling

Seventy-first session

Geneva, 31 March–03 April 2014

Item 12(d) of the provisional agenda
Other business – Any other business

Proposal for amendments to Regulation No. 48 (Installation of lighting and light-signalling devices)

Submitted by the expert from the European Association of Automotive Suppliers*

The text reproduced below was prepared by the expert from the European Association of Automotive Suppliers (CLEPA). The modifications to the existing text of the Regulation are marked in bold for new and strikethrough for deleted characters.

I.	Proposal

Paragraph 2.17.6.4., amend to read:

"2.17.6.4.	Retro-Reflecting materials approved as Class D or E or F according to Regulation No. 104 and used for other purposes in compliance with national requirements, e.g. advertising."

II.	Justification

1.	Introduction of new class F marking materials designed with alternate stripe pattern to be applied to special utility vehicles or trailers not regularly covered by standard contour marking materials requires amending the definitions.

2.	This amendment ensures that this new "F" class of materials does not conflict with the mandatory requirements of existing class "C".

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2012–2016 (ECE/TRANS/224, para. 94 and ECE/TRANS/2012/12, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate