| Transmitted by the expert from IMMA (International Motorcycle Manufacturers Association) | Informal document GRE-73-16 (73rd GRE, 14-17 April 2015, agenda item 9) |
| --- | --- |

Proposal for Supplement XX to Regulation No. 50 (Position, stop, direction indicators lamps for mopeds and motorcycles)

The modifications to the existing Regulation are marked in bold for new or strikethrough for deleted characters.

- Proposal

Annex 5, item 3, amend to read:

"3. 	Angle of incidence

The manufacturer of the illuminating device shall specify one or more or a field of positions in which the device is to be fitted in relation to the space for the registration plate; when the lamp is placed in the position(s) specified by the manufacturer the angle of incidence of the light on the surface of the plate does not exceed 82° at any point of the surface to be illuminated, this angle being measured from the mid-point of the edge of the illuminating surface of the device which is furthest from the surface of the plate. If there is more than one illuminating device, the foregoing requirement shall apply only to the part of the plate intended to be illuminated by the device concerned.

The device shall be so designed that no light is emitted directly towards the rear, with the exception of red light if the device is combined or grouped with a rear lamp."

- Justification

- The angle of incidence was developed to ensure plate was illuminated.  However, with new technologies (example: LED) the performance requirements noted in Annex 5, item 1 “Space to be illuminated” and Annex 5, item 5 “Photometric characteristics” sections can be met without the need to maintain the angle of incidence.

- This proposal will NOT change performance of illumination on the plate.

- This proposal allows for design packaging flexibility only.