## Slide 1: Status of the IWG on gaseous fuelled vehicles (GFV) and specific concerning the status of the HDDF retrofit regulation
GRPE June 9th 2016
Geneva
Informal document GRPE-73-28
73rd GRPE, 6-10 June 2016, agenda item 8

## Slide 2
Overview
A new regulation is developed which includes the requirements for the type approval of retrofit systems intended to be fitted on a heavy duty diesel vehicle to enable its operation either in diesel mode or in dual-fuel mode.
Only Euro V and EEV vehicles were included.

## Slide 3: Issues to be considered
Regulation for type approval of systems for retrofitting diesel vehicles to dual fuel operation, but it references to R49: type approval of engines
Tension between retrofit conversion effort/costs and environmental impact/benefit
Level playing field for both retrofit system manufacturers and engine/vehicle manufacturers
Euro IV, V and EEV diesel engines have limited diagnostic functionality and no NOX closed loop control (difference with R115 for LDV’s)

## Slide 4: Progress since Jan 2016 GRPE
Concerns raised by the German delegation and the legal department of DG-GROWTH of the European Commission were discussed and solved
Draft was finalised
Discussions about CO/NMHC derogations
5 tele/web meetings
1 face to face meeting (2 days)
Working document submitted to GRPE

## Slide 5: Changes since Jan 2016 GRPE
Concerns from the German delegation and from the legal department of DG-GROWTH of the European Commission;
  Removed possibility to perform retrofit system type approval on a non compliant demonstration engine (even when the retrofitted engine would be compliant on DF operation)
  Removed simplified engine test bench and chassis dyno tests and provisions for increased CO emissions
  Improvements in other parts of the document

## Slide 6: Changes since Jan 2016 GRPE
Retrofit system parts information system introduced for the retrofit system plate
Administrative provisions were finalised
Installation- and user manual requirements were finalised
Fuel related requirements introduced
  reference fuels vs market fuels
  composed representative fuels (if market fuel cannot be acquired)
  universal fuel approval vs fuel range restricted approval

## Slide 7: Proposal for a new Regulation of Heavy Duty Dual-Fuel Engine Retrofit Systems (HDDF-ERS) ECE/TRANS/WP.29/GRPE/2016/12
Structure:
  I - Preamble and guidance
  II - Requirements and specifications
    Annex 1 - Information documents
      Appendix 1 - Essential characteristics of the (parent) retrofit system and of the demonstration engine
      Appendix 2 - Essential characteristics of the engine retrofit system family and of the application range
    Annex 2 - (Reserved)
    Annex 3 - Information document regarding the actual applications
      Appendix 1 - List of actual applications

## Slide 8: HDDF Engine Retrofit Systems (HDDF-ERS) regulation
    Annex 4 - Arrangement of the dual-fuel engine retrofit system type approval mark
    Annex 5 - Communication concerning the approval or extension or refusal or withdrawal of approval or production definitively discontinued of a type of an engine retrofit system (HDDF-ERS) pursuant to Regulation No. XXX
    Annex 6 - Dual-fuel engine retrofit systems intended to be fitted on road vehicles – requirements and tests

## Slide 9
Emission tests
Type-approval extension
For a type approval extension, the emissions may be measured with a (retrofit specific) test procedure using a Portable Emission Measurement System mounted on a vehicle equipped with the retrofit system.
Back-to-back comparison between a test in diesel mode and a test in dual-fuel mode (measurement of BSFC emissions is not feasible)
Measurement in accordance with the type approval test procedure (against the emission limits on an engine test bench) or back-to-back on the road at the choice of the manufacturer.

## Slide 10
Emission tests
Type-approval extension
The working principle has always been that the pollutant emissions of a retrofitted dual-fuel engine shall be lower than or equal to those of the original diesel engine
A derogation for CH4 emissions is already implemented (GHG neutral)
Diesel engines may show NMHC and/or CO emissions far below the emission limits
System manufacturers raised concerns not to be able to meet those emission levels in dual-fuel mode
Manufacturers desire derogations for CO and NMHC emissions

## Slide 11: Vehicle certification / Vehicle approval after the retrofit conversion
The (re-)certification of a retrofitted vehicle including all the quality requirements should be handled in national and/or CP legislation
The check that the Vehicle Retrofit System is approved for the engine/vehicle combination and is installed in line with the installation manual
Safety check of the conversion in line with R67 and R110 (including check of the used components)
Specific attention for the installation of the cylinders and the safety devices.