Proposal for amendments to working document GRRF/2016/29

The modifications to the existing text are marked in bold for new or double strikethrough for deleted characters.

I.	Proposal

“Paragraph 5.3.4., renumber as paragraph 5.3.5. and amend to read:

"5.3.45. A statement of the characteristic performance values …”

Paragraph 5.3.4.1., renumber as paragraph 5.3.5.1 and amend to read:

"5.3.45.1.	The characteristic performance values shall be at least equal to those requirement values, determined according to Annex 8 of this regulation applicable to applying the maximum permissible towing vehicle, trailer and combination masses, determined according to Annex 8 of this regulation."

.

II.	Justification

- The text of the GRRF/2016/29 has a linguistic form that implicates that limiting masses are calculated using the formulae of Annex 8. Rather limiting forces are used calculating required performance values applying the formulae in Annex 8.

- The text of the GRRF/2016/29 implicates renumbering of the paragraphs concerned. However the numbering in the Rev 2 of UNRCE R55 already is renumbered appropriately.