## Slide 1: “Pre Study for the discussion on Reversing Alarm System" -Japanese current situations-
Feb/2017
Noise Subcommittee/JASIC
Japan Automobile Standards Internationalization Center
http://www.jasic.org
Transmitted by the expert from Japan
Informal document GRB-65-06
(65th GRB, 15-17 February 2017,
agenda item 2)

## Slide 2
1. Technical Standard and History in Japan
2. Reversing alarm standard for unit ( JASO D901)
3. The attachment rate of the reversing alarm
System for new Vehicles and sound pressure level
4. Questionnaire Research ( Truck & Bus users )
Contents

## Slide 3
1. Technical Standard and History in Japan
* To equip reversing alarms is not mandatory.
It is allowed to be equipped.
Reversing Alarm equipment is available for Retrofit
* In 1963, a Japanese company succeeded in developing the
world’s first reversing alarm system.
* JASO (Japanese Automobile Standards Organization)
established D901 "Reverse buzzer standard" in 1975.

## Slide 4
JASO :
Japanese Automobile Standards Organization

## Slide 5
2. Reversing alarm standard for unit
: JASO D901
D901 : Main requirements
1. Sound pressure level : 75 - 95 dB
Distance from the buzzer to microphone 1m,
measured in anechoic chamber
2. Fundamental frequency : 400 - 4000 Hz
（no fluctuation)
3. The intermittence number per minute
: 60 - 120 count/min

## Slide 6
3. The attachment rate of the reversing alarm
system for new Vehicles
All new motor vehicles sold in Japan of categories N2, N3, and M3 are equipped with reversing alarms (beep type).
Categories | Company A | Company B | Company C | Company D
M3 | － | 100% | 100% | 100%
N3 | 100% | 100% | 100% | 100%
N2 | 100% | 100% | 100% | 100%

## Slide 7: Measuring Point same as Germany Proposal
７ｍ
0.5～1.5ｍ
Measuring Point:
Distance from the end of the vehicle: 7m
Maximum sound level during microphone height: 0.5 ～1.5ｍ

## Slide 8: Measurement results of SPL
・N3 : 59.9～75.0ｄBA (Ave. 67.4dBA) ・M3 : 56.9～69.1ｄBA (Ave. 62.6dBA)
・N2：71.2～78.9ｄBA (Ave. 75.6dBA)
N3 Ave. 67.4
M3 Ave. 62.6
N2 Ave. 75.6

## Slide 9: 4. Questionnaire Research (Truck & Bus users)
 | Trucking Association (JTA) | Road Contractors Association (JRCA) | Bus Association (NBA) | Sum
Responded Company | 159 | 98 | 49 | 307
Total Owned Vehicle Number | about 5,800 | about 1,900 | about 2,500 | about 10,200
How many vehicle does your company have?
Number of company which responded our questionnaire
JRCA
JTA
NBA

## Slide 10
What is a major vehicle type at your workplace?
Japan Trucking Association (JTA) & Japan Road Contractors Association (JRCA)
Nihon Bus Association (NBA)
No. of cases. (%)
No. of cases. (%)

## Slide 11
Are your Main owned Vehicles Equipped with Reversing Alarms?
JTA
(n=157)
JRCA
(n=95)
NBA
(n=45)
Almost all companies own vehicles equipped with reversing alarms.
One bus company answered "None", however all the buses owned by the company are equipped with reversing camera.

## Slide 12
Do you think motor vehicles need reversing alarms?
 | JTA |  | JRCA |  | NBA | 
Necessary for all motor vehicles | 141 | (88.7) | 91 | (92.9) | 43 | (87.8)
Necessary for certain types of motor vehicles | 11 | (6.9) | 5 | (5.1) | 2 | (4.1)
Not necessary for any motor vehicles | 3 | (1.9) | 1 | (1.0) | 2 | (4.1)
Others | 2 | (1.3) | 1 | (1.0) | 0 | (0)
No answer | 2 | (1.3) | 0 | (0) | 2 | (4.1)
Total | 159 | (100) | 98 | (100) | 49 | (100)
No. of cases. (%)
A lot of companies answered that reversing alarm is necessary for all motor vehicles.
5 of 6 companies who answered “not necessary for any” own vehicles equipped with reversing camera.

## Slide 13
Daytime
Night
JTA
n=145
JRCA
n=94
Just right
Somewhat quiet
Too quiet
Somewhat loud
Too loud
NBA
n=41
JTA
n=132
JRCA
n=92
NBA
n=37
Just right
Somewhat loud
Too loud
Too quiet
Somewhat quiet

## Slide 14
Daytime
Night
JTA
n=41
JRCA
n=31
NBA
n=6
JTA
n=40
JRCA
n=32
NBA
n=9
Too loud
Just right
Just right

## Slide 15
Have Local Residents Ever Complained
About Reversing Alarms?
JTA
n=157
JRCA
n=97
NBA
n=49
JTA
n=36
JRCA
n=30
NBA
n=8
Yes
in the last 12 month
Yes, but not
in the last 12 month
Never
Don’t Know
Don’t have any motor vehicles with reversing alarms

## Slide 16
 | JTA | JRCA | JBA
Reversing cameras | 82.9 | 52.7 | 100.0
Rear sonars | 2.4 | 7.3 | 12.5
Directional microphones | 0.0 | 0.0 | 50.0
Someone guiding while reversing | 19.5 | 47.3 | 18.8
Others | 2.4 | 10.9 | 0.0
To ensure safety while reversing the vehicle, do you use any equipment or take any measures other than reversing alarms? (Multiple answers allowed)
Many companies use several equipment (especially reversing cameras) other than reversing alarms, to ensure safety while reversing the vehicle. 'Directional microphones' are used in Bus association only

## Slide 17
All new motor vehicles sold in Japan of categories N2, N3, and M3 are equipped with reverse alarms (beep type), which are in fairly high demand from operation managers of automotive transport companies who own trucks and buses.
- Though differing somewhat depending on the vehicle category, the sound level of reverse alarms commonly used in Japan is typically 60–78 dB (measured by the method proposed by Germany).
- Most operation managers feel the sound level of reverse alarms (60–78 dB) is just right in the daytime, but a majority feel it is too loud at night.
- Regarding the use of reverse alarms, roughly half of operation managers have received complaints from local residents.
- In addition to reverse alarms, most motor vehicles of categories N2, N3, and M3 are equipped with reverse cameras to ensure safety while reversing. In some cases, even further measures are taken such as sonars, microphones, and someone guiding while reversing.
Outline of the results of the survey