## Slide 1: Tyres in Europe Tightening of tyre limits and further suggestions for improvement
Johan Sliggers (Ministry of Infrastructure and Environment)
Erik de Graaff (M+P)
Transmitted by the expert from the Netherlands
Informal document GRB-66-01-Add.1
(66th GRB, 4-6 September 2017,
agenda item 6)

## Slide 2: Tyre Limits
2014: On the agenda GRB: GRB-59-11
2015: Proposals for Noise limits (stage 3): GRB-61-03, GRB-62-11
2016: Proposal for all three tyre limits (stage 3): GRB-62-11-REV.1 (at GRB-64)
2017: Revised proposal for all three tyre limits (stage 3 and 4): GRB-66-03

## Slide 3: Statistics of C1 label values and (suggested) stages of limit values

## Slide 4: Statistics of C2 label values and (suggested) stages of limit values

## Slide 5: Statistics of C3 label values and (suggested) stages of limit values

## Slide 6: Developments
Rapid improvements tyres (noise) 2007-2013
Premium tyres are dominant in the market (>90% in OEM) (>50% in replacement)
Premium OEM tyres perform (much) better than aftersales tyres
Updated Stage 3 limits at 50 Percentile of 2016 data
New stage 4 limits at 20 Percentile of 2016 data

## Slide 7: Rolling Resistance coefficient (N/kN)
Tyre type | Current limit | GRB-62-11-Rev.1 | Stage 3 | Stage 4
C1 | 10.5 | 9.0 | 9.0 | 8.0
C2 | 9.0 | 8.0 | 8.0 | 7.0
C3 | 6.5 | 6.0 | 6.0 | 5.5

## Slide 8: Wet Grip index (G)
Tyre type | Current limit | GRB-62-11-Rev.1 | Stage 3 | Stage 4
C1 | 1.1 | 1.4 | 1.45 | 1.6
C2 | 0.95 | 1.25 | 1.25 | 1.35
C3 | 0.80 | 1.1 | 1.1 | 1.2

## Slide 9: Noise (rolling sound emissions dB(A))
Tyre type | Current limit | GRB-62-11-Rev.1 | Stage 3 | Stage 4
C1 | 70-74 | 67-71 | 69-73 | 67-71
C2 | 72 | 70 | 71 | 70
C3 | 73 | 69 | 71 | 69

## Slide 11: Potential benefits Stage 3, 4 and Proper tyre pressure in the EU
 | Stage 4 limits | Stage 3 limits | Proper pressure
Fuel savings [billion l/yr] | 17 | 8 | 5
CO2 reduction [Mt/yr] | 42 | 21 | 12
Reduced # of fatalities | 2567 | 1300 | 140
Reduced # of slight/ serious injuries | 19631/ 12353 | 10000/ 6000 | 1100/ 7000
Reduced # of annoyed people [millions] | 13 | 6 | 1.5
Reduced # of sleep disturbed people [mill.] | 6 | 3 | 0.6
Cost savings [billion €/y] | 34 | 17 | 6

## Slide 12: Potential benefits A label tyres for fuel efficiency equivalent Stage 4 (incl. proper tyre pressure)
Vehicle type | Km/year | Fuel savings/year [l] | Cost savings/year [€]
Passenger car (Petrol) | 17.000 | 84 (19) | 121 (27)
Passenger car (Diesel) | 35.000 | 138 (31) | 151 (34)
Delivery van (D) | 35.000 | 183 (41) | 201 (45)
Delivery truck (D) | 60.000 | 388 (70) | 427 (78)
Heavy duty truck (D) | 130.000 | 2150 (414) | 2365 (456)
Bus (D) | 50.000 | 789 (155) | 868 (171)

## Slide 13: Clean Vehicle Directive: Potential benefits for car fleets
Potential benefits | Dutch National Road Authority (RWS) | Amsterdam | Rotterdam
Number of vehicles | 1575 | 781 | 1097
Vehicle average [ km/yr ] | 26.000 | 17.200 | 17.300
Fuel savings (correct pressure) [thousands ltr/yr] | 153.000 (26.500) | 147.000 (33.000) | 200.000 (45.000)
CO2 reduction [ton/yr] | 388 (66) | 379 (86) | 514 (116)
Cost savings [€/yr] | 237.500 (42.000) | 224.000 (51.000) | 303.000 (69.000)
Cost savings per vehicle [€/yr] | 150 (36) | 287 (65) | 277 (63)

## Slide 14: Tyre pressure
60% of cars have underinflated tyres
Tyres deflate 3-5% a month
User manuals prescribe: ‘inflate when cold’
  Frequency?
  Warm tyres? What then?

## Slide 17: Tyre pressure monitoring systems (TPMS)

## Slide 18: Tyre wear
In NLs 1 kg per capita, in EU 0.5 Mton/yr
40% of total microplastics emissions
30% under inflation increases wear by 50%
No standards/limits for tyre wear
Wear/Durability/Abrasion rate on tyre label?
Wheel alignment in periodic road worthiness tests?

## Slide 19: Tyre quality NL 2015 (8 million cars)
Passenger cars with at least one tyre | Percentage | Total NLs (million)
Irregular wear or damage | 41 | 3.35
Damage | 25 | 2.04
Irregular wear | 10 | 0.82
(Ageing) little cracks or tear | 26 | 2.12
Danger to traffic safety | 9 | 0.74
Underinflation | >60 | 5

## Slide 20: Tyre label
Label lacks information
Not fit for all season and winter tyres
Market surveillance
Stakeholder consultation EU on Tyre label Regulation, September

## Slide 24: Interaction tyres with roads

## Slide 25: Thank you for your attention !