## Slide 1: UN-Regulation No. 80 Additional Information to GRSP-62-35
May 2018
Submitted by the expert from Germany
Informal document GRSP-63-32
(63rd GRSP, 14 - 18 May 2018,
agenda item 14)

## Slide 2: UN-Regulation No. 80
The current UN-Regulation No. 80 allows to approve large passanger vehicle seats and their anchorage according to two different test procedures.
Appendix 1 (dynamic)
sled test with 50%ile Dummy (HII or HIII), 30-32km/h, 8-12g
Test 1 (without belt)
Test 2 (with belt)
Appendix 5 (static)
defined forces applied to the backrest at two locations
or
ax
ax
F1
F2

## Slide 3: Testmatrix
Seat | Test procedure | Belt | Test-No. | Remarks
A | Dynamic (Appendix 1) | unbelted | R-80_17_01 | 
 |  | unbelted | R80-1-1-01 | 
 |  | 2-point belt | R80-1-2-02 | 
 |  | Seat only | R-80_17_02 | not part of R80
 |  | Seat only | R80-1-1-05 | not part of R80
 | Static (Appendix 5) | - | R-80-d-17_01 | 
 |  | - | 179421190_002 | 
B | Dynamic (Appendix 1) | unbelted | R80-1-1-03 | 
 |  | unbelted | R80-1-1-04 | 
 | Static (Appendix 5) | - | 179421190_001 | 
C | Dynamic (Appendix 1) | unbelted | R-80_17_03 | 
 | Static (Appendix 5) | - | R-80-d-17_02 | 
Tests have been conducted
  according to test procedure R80 Appendix 1 (dynamic) and Appendix 5 (static)
  different seats
  at different labs.
All seats are equipped with quick clamping systems

## Slide 4: Testmatrix
Seat | Test procedure | Belt | Test-No. | Remarks
A | Dynamic (Appendix 1) | unbelted | R-80_17_01 | 
 |  | unbelted | R80-1-1-01 | 
 |  | 2-point belt | R80-1-2-02 | 
 |  | Seat only | R-80_17_02 | not part of R80
 |  | Seat only | R80-1-1-05 | not part of R80
 | Static (Appendix 5) | - | R-80-d-17_01 | 
 |  | - | 179421190_002 | 
B | Dynamic (Appendix 1) | unbelted | R80-1-1-03 | 
 |  | unbelted | R80-1-1-04 | 
 | Static (Appendix 5) | - | 179421190_001 | 
C | Dynamic (Appendix 1) | unbelted | R-80_17_03 | 
 | Static (Appendix 5) | - | R-80-d-17_02 | 
Videos shown as comparision of test method in GRSP-62-35
Additional videos presented in this presentation for clarification

## Slide 5: Are these test methods equivalent?
UN-Regulation No. 80
Seat B
Test 179421190_001
Seat A
Test R80-1-2-02
Videos from GRSP-62-35

## Slide 6: Seat of Concern
UN-Regulation No. 80
Seat A
Test R-80-d-17_01
Seat A
Test R80-1-2-02
Seat A

## Slide 7: Seat of Concern
UN-Regulation No. 80
Seat A
179421190_002

## Slide 8
Seat A Quick Clamping System
UN-Regulation No. 80

## Slide 9: Results – Static Test
179421190_002 – Seat A
Tested according to R80 – Appendix 5
Observations:
  Seat stays in place, no failure
  The maximum displacement at F1 is below the threshold of 400mm
  The minimum displacement at F1/ F2 is above the threshold of 100/50mm




## Slide 10: Results – Dynamic Test 1
R80-1-1-01 - Seat A
Tested according to R80 – Appendix 1, Test 1 (unbelted)
Observations:
  Auxiliary seat slides 600mm (but still in seat track)
  Test seat slides without any load of the dummies completely out of the seat track
   seat mountings are not strong enough to hold the seat in place
   Occupants are not restrained by the test seat
  Dummy values are below the thresholds but serious injuries are likely
Sliding distance of auxiliary seat
Post-test
Pre-test

## Slide 11: Results – Dynamic Test 2
R80-1-2-02 - Seat A
Tested according to R80 – Appendix 1, Test 2 (belted)
Observations:
  Auxiliary seat detaches completely from the seat track
  Test seat slides without any load of the dummies completely out of the seat track
   seat mountings are not strong enough to hold the seat in place
   Occupants are not restrained by the test seat
  Dummy values are below the thresholds
  but serious injuries are likely
Post-test -Dummies
Pre-test
Post-test - overview

## Slide 12: Conclusion
The statically (appendix 5) tested seats, when tested according to the dynamic test, collapsed in the dynamic tests
  Goal of UN Regulation No. 80 is not achieved when tested statically
Proposal: delete static test according to Appendix 5

## Slide 13: Outlook
In addition it has been observed that
the static test procedure:
does not consider dynamic effects like:
  oscillation
  inertia
    mass and mass distribution of the seat
    detaching of accessories
    detaching/sliding/failure of clamp connection and locking
does only partially take into account the different installation situation of the seat (lateral and vertical offset of seats, etc.).
the dynamic test procedure:
Does not limit the sliding of the seat anchorage

## Slide 14: Thank you for your attention!

## Slide 15: Results - Summary
Seat | Test procedure | Belt | Test-No. | Resistance of seat/seat mountings | Occupants restraint | Occupant load
A | Dynamic (Appendix 1) | unbelted | R-80_17_01 | test seat slides ~240mm and detaches partly; auxiliary seat slides ~100mm*) | excursion below threshold | values above threshold
 |  | unbelted | R80-1-1-01 | test seat slides out of seat track; auxiliary seat slides ~600mm | not restrained | values below threshold
 |  | 2-point belt | R80-1-2-02 | test seat slides out of seat track; auxiliary seat detaches | not restrained | values below threshold
 | Other | Seat only | R-80_17_02 | seat slides ~655mm | - | -
 |  | Seat only | R80-1-1-05 | seat slides ~665mm | - | -
 | Static (Appendix 5) | - | R-80-d-17_01 | seat slides ~20mm | correctly restrained | sufficient deformation
 |  | - | 179421190_002 | seat does not move | correctly restrained | sufficient deformation
B | Dynamic (Appendix 1) | unbelted | R80-1-1-03 | test seat slides ~39mm | Dummy excursion below threshold | values below threshold
 |  | unbelted | R80-1-1-04 | test seat slides ~16mm | excursion below threshold | values below threshold
 | Static (Appendix 5) | - | 179421190_001 | Seat does not move | correctly restrained | sufficient deformation
C | Dynamic (Appendix 1) | unbelted | R-80_17_03 | test seat slides (~340mm) | excursion below threshold | values below threshold
 | Static (Appendix 5) | - | R-80-d-17_02 | seat does not move | correctly restrained | sufficient deformation
*) seat sliding influenced due to tape on seat track