| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/GRE/2005/36/Corr.1 26 January 2006 Original: ENGLISH ENGLISH AND FRENCH ONLY |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Lighting and Light-Signalling (GRE)

(Fifty-sixth session, 4-7 April 2006,

agenda item 17.1.)

PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 48 */

(Installation of lighting and light-signalling devices)

Transmitted by the expert from the Working Party "Brussels 1952" (GTB)

Corrigendum

PROPOSAL

Page 2, inserted new paragraph 2.7.10.1., correct to read:

"2.7.10.1.	"Principal dipped beam" means the dipped beam produced without the contribution of infrared (IR) emitter and/or additional light sources for bend lighting."

Page 2, paragraph 6.2.8., correct to read:

"6.2.8.	Tell-tale

6.2.8.1.	Tell-tale optional.

6.2.8.2.	An operational tell-tale is mandatory:

-	in the case where the whole beam or the kink of the elbow of the cut-off is moved to produce bend lighting;

-	if one or more LED modules are used to produce the principal dipped-beam.

##### It shall be a flashing warning light which comes on:

-	in the event of a malfunction of the displacement of the kink of the elbow of the cut-off, or

-	in case of a failure of any one of the LED module(s) producing the principal dipped-beam."

Page 3, paragraph 6.2.9., correct to read:

"6.2.9.	.… to dipped-beam headlamps.

Dipped-beam headlamps with a light source or LED module(s) having a total objective luminous flux which exceeds 2,000 lumen shall only be installed in conjunction …."

- - - - -