#### UNITED

# NATIONS

Distr.

# GENERAL

# TRANS/WP.15/AC.1/2001/26

# 19 March  2001

# ENGLISH

Original: ENGLISH and FRENCH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of the RID Safety Committee and the

Working Party on the Transport of Dangerous Goods

(Bern, 28 May – 1 June 2001)

PARTS 7 to 9

### Note by the Secretariat */

This document contains proposed amendments to Parts 7 and 9 of the restructured RID/ADR for harmonization with the 12th revised edition of the United Nations Recommendations on the Transport of Dangerous Goods, Model Regulations, on the basis of the decisions of the Committee of Experts on the Transport of Dangerous Goods at its twenty-first session, (Geneva, 4-13 December 2000) (See ST/SG/AC.10/27 and addenda 1 and 2).

_______

*/    Circulated by the Central Office  for International Carriage by Rail (OCTI) under the symbol OCTI/RID/GT/III/2001/26.

PART 7

Chapter 7.2

7.2.4		For V8 (1):

Replace "Organic peroxides and self-reactive substances" by "substances stabilized by temperature control".

Add a NOTE as follows:

"NOTE:

[This provision V8 is indicated in Table A of Chapter 3.2 for all substances the proper shipping name of which contains the word "STABILIZED". However it is not applicable] [This provision V8 does not apply to substances referred to in 3.1.2.6] when substances are stabilized by the addition of chemical inhibitors such that the SADT is greater than 50 °C. In this latter case, temperature control may be required under transport conditions where the temperature may exceed 55 °C.".

[Add "V8" in Table A of Chapter 3.2 for all substances the proper shipping name of which include the word "STABILIZED".]

Chapter 7.5

7.5.2.1	In the table:

Add "c" in the intersection of row "1.4" and column "9" and column "1.4" and row "9", and add at the end of the table a new "c" as follows:

"c	Mixed loading permitted between air bag inflators, or air bag modules, or seat-belt pretensioners of Division 1.4, compatibility group G, (UN 0503) and air bag inflators or air bag modules or seat-belt pretensioners of Class 9 (UN 3268).

Add "d" in the intersection of row "1" and column "5.1" and column "5.1" and row "1", and add at the end of the table a new "d" as follows:

"d	Mixed loading permitted between blasting explosives (except UN 0083 Explosive, blasting, type C) and ammonium nitrate and inorganic nitrates of Class 5.1 (UN Nos. 1942 and 2067) provided the aggregate is treated as blasting explosives under Class 1 for the purposes of placarding, segregation, stowage and maximum permissible load."

PART 8

Chapter 8.5

For S4 add a NOTE as follows:

"NOTE:

[This provision S4 is indicated in Table A of Chapter 3.2 for all substances the proper shipping name of which contains the word "STABILIZED". However it is not applicable] [This provision S4 does not apply to substances referred to in 3.1.2.6] when substances are stabilized by the addition of chemical inhibitors such that the SADT is greater than 50 °C. In this latter case, temperature control may be required under transport conditions where the temperature may exceed 55 °C.".

[Add "S4" in Table A of Chapter 3.2 for all substances the proper shipping name of which include the word "STABILIZED".(ADR only)].

PART 9

Chapter 9.6

Amend the title to read: "ADDITIONAL REQUIREMENTS  CONCERNING COMPLETE OR COMPLETED VEHICLES INTENDED FOR THE CARRIAGE OF TEMPERATURE CONTROLLED SUBSTANCES"

9.6.1	Replace "self-reactive substances of Class 4.1 and organic peroxides of Class 5.2" with "substances".

-----------------------------------

# Text boxes

E

Economic and Social

Council