#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2002/44

8 April 2002

# ORIGINAL: ENGLISH

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

(Twenty-first session, 1-10 July 2002,

agenda item 8(b))

## LISTING AND CLASSIFICATION

## Correct assignment of UN Numbers to substances and solutions

with respect to physical state (liquid or solid)

Transmitted by the experts from the Netherlands and Germany

#### Background

## In July 2001 the Sub-Committee discussed a joint paper from the Netherlands and Germany (ST/SG/AC.10/C.3/2001/14) concerning the assignment of substances and solutions to the correct UN number in relation to the physical state (liquid/solid). The principle to create separate entries for a solid and the solution thereof  was adopted as well as the principle to create separate entries for those substances for which due to the different composition of isomers the entry can be both liquid or solid, see paragraphs 71 to 75 of  report ST/SG/AC.10/C.3/38.

Furthermore in December 2002 the Sub-Committee was informed about the provisional results of the consequential work concerning the correct assignment of UN numbers, proper shipping names and packing instructions to substances with respect to their physical state (UN/SCETDG/20/INF.17), see paragraphs 62 and 63 of report ST/SG/AC.10/C.3/40.

Based upon the outcome of the discussion whether it is necessary to create new UN numbers in all cases and comments received intersessionally from the United Kingdom and further study of the regulations and consultation of the database of the BAM in Berlin, a list of all entries concerned was compiled (see the Annex to this document).

GE.02-

A further point concerns those substances for which due to different composition of isomers the entry can be both a liquid or solid. In those cases no additional entries for the solution are included.

As a consequence the principles adopted, the text of 3.1.2.4 should be deleted. In order to make things clear for the user it is proposed to use this paragraph with the following text:

“Many substances have an entry for both the liquid and solid state or for the solid and solution. These are allocated separate UN entries which are not necessarily adjacent to each other. Details are provided in the alphabetical index, e.g.

NITROXYLENES, LIQUID UN 1965

NITROXYLENES, SOLID UN XXXX

In this way special provisions as suggested in UN/SCETDG/20/INF.17 can be avoided

Also in the process the following errors were found:

- UN 2511, 2-CHLOROPROPIONIC ACID, SOLID does not exist as it has a melting point of  -12 °C (source: BAM Database and BIG Database)

- UN 3207, delete in column (9) special provisions B2 and B4 as special provisions B2 and B4 are not applicable to IBC instruction IBC01 and IBC02

## Proposal

- To adopt all proposed entries mentioned in the Annex which appear in the solid and in the liquid state together with the consequential amendments and to amend Chapter 3.2 and the INDEX accordingly.

- To adopt the proposed amendment of 3.1.2.4;

Replace current text 3.1.2.4 by:

“Many substances have an entry for both the liquid and solid state or for the solid and solution. These are allocated separate UN entries which are not necessarily adjacent to each other. Details are provided in the alphabetical index, e.g.

NITROXYLENES, LIQUID UN 1965

NITROXYLENES, SOLID UN XXXX

- To adopt the found errors with regard to UN 2511 and UN 3207 and to amend Chapter 3.2 accordingly;

Delete  the entry for UN 2511, 2-CHLOROPROPIONIC ACID, SOLID and delete for UN 3207 in column (9) the special provisions B2 and B4 for PG II and  PG III entry respectively

#### Annex

The attached annex lists all entries, which may appear in the solid and in the liquid state  in one (or more)  of the international regulations (UN Recommendations, IMDG-Code, RID/ADR and also CFR)  together with the consequential amendments.

The existing UN number is used for the case described in the present regulations. A new UN number is proposed for the substance in the other aggregation state. In this list the consequential amendments are indicated. Consequential amendments are based on the rationalised approach of the issue concerned.

Annex

New entries and amendments to DGL (12th ed.)) concerning “LIQUID/SOLID/SOLUTION”-problem

Based upon ST/SG/AC.10/C.3/2001/14 - Annex 1

The information given in the columns (6) to (11) for the new entries are based upon the ‘’Rationalized Approach” for packagings, RID/ADR and IMDG Code.

Where for  solid entries in column (10) and (11) a T-code and/or TP-code is found between square brackets ( [..]), this means that the 12th edition of the ‘Orange Book’ indicates a T-Code and/or TP-code for the concerned solid entry. However that for the final allocation of a T-Code and/or TP-code the Sub-Committee is requested to await the outcome of the discussion on transport of solids in portable tanks.

Note: “a new entry” = a solid, liquid or solution entry which has not been mentioned in the ‘Orange Book’ by means of the applicable packing instruction, column (8) (e.g. in ‘Orange Book’ an existing entry for a liquid/P001 ( ‘new entry’ + new UN No. will be the solid/P002, etc.); or: the second mentioned entry under an existing entry with the same UN No. will become the ‘new entry’.

| UN No. | Name and description | Class or Division | Subsidiary risk | UN packing group | Special provisions | Limited quantities | Packagings and IBCs | Portable tanks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Packing instruction | Special provisions | Portable tank instructuions | Portable tank special instructions |
| (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) |
| 1389 | ALKALI METAL AMALGAM, LIQUID | 4.3 |  | I | 182 | NONE | P402 |  | - |  |
| ABCD | ALKALI METAL AMALGAM, SOLID | 4.3 |  | I | 182 | NONE | P403 |  | - |  |
| 1392 | ALKALINE EARTH METAL AMALGAM, LIQUID | 4.3 |  | I | 183 | NONE | P402 IBC04 | B1 | - |  |
| BCDE | ALKALINE EARTH METAL AMALGAM, SOLID | 4.3 |  | I` | 183 | NONE | P403 |  | - |  |
| 1420 | POTASSIUM METAL ALLOYS, LIQUID | 4.3 |  | I |  | NONE | P402 IBC04 | B1 | - |  |
| XXXX | POTASSIUM METAL ALLOYS, SOLID | 4.3 |  | I |  | NONE | P402 |  | - |  |
| 1422 | Potassium sodium alloys, liquid | 4.3 |  | I |  | NONE | P402 IBC04 | B1 | T9 | TP3, TP7, TP31 |
| XXXX | Potassium sodium alloys, SOLID | 4.3 |  | I |  | NONE | P403 |  |  |  |
| 1445 | BARIUM CHLORATE, SOLID | 5.1 | 6.1 | II |  | 1 kg | P002 IBC06 | B2 | [T4] | [TP1] |
| XXXX | BARIUM CHLORATE, SOLUTION | 5.1 | 6.1 | II |  | 500 ml | P504 IBC02 |  | T4 | TP1 |
| XXXX | BARIUM CHLORATE, SOLUTION | 5.1 | 6.1 | III |  | 1l | P001 IBC02 |  | T4 | TP1 |
| DEFG | BARIUM PERCHLORATE, SOLUTION | 5.1 | 6.1 | II |  | 500ml | P504 IBC02 |  | T4 | TP1 |
| XXXX | BARIUM PERCHLORAE, SOLUTION | 5.1 | 6.1 | III |  | 1l | P001 IBC02 |  | T4 | TP1 |
| 1447 | BARIUM PERCHLORATE, SOLID | 5.1 | 6.1 | II |  | 1 kg | P002 IBC06 | B2 |  |  |
| EFGH | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE, SOLUTION | 5.1 |  | II |  | 500ml | P504 IBC01 |  | T4 | TP1 |
| EFGH | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE, SOLUTION | 5.1 |  | III |  | 1l | P504 IBC01 |  | T4 | TP1 |
| 1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE, SOLID | 5.1 |  | II |  | 1 kg | P002 IBC08 | B2, B4 |  |  |
| 1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE, SOLID | 5.1 |  | III | 223 | 5 kg | P002 IBC08 LP02 | B3 |  |  |
| 1470 | LEAD PERCHLORATE, SOLID | 5.1 | 6.1 | II |  | 1 kg | P002 IBC06 | B2 |  |  |
| FGHI | LEAD PERCHLORATE, SOLUTION | 5.1 | 6.1 | II |  | 500 ml | P504 IBC02 |  | T4 | TP1 |
| 1577 | CHLORODINITROBENZENES, LIQUID | 6.1 |  | II |  | 100 ml | P001 IBC02 |  | T7 | TP2 |
| XXXX | CHLORODINITROBENZENES, SOLID | 6.1 |  | II | 279 | 500g | P002 IBC08 | B2, B4 | Note: is now an existing entry under UN 1577 |  |
| 1578 | CHLORONITROBENZENES, SOLID | 6.1 |  | II | 279 | 500g | P002 IBC08 | B2, B4 |  |  |
| XXXX | CHLORONITROBENZENES, LIQUID | 6.1 |  | II | 279 | 100 ml | P001 IBC02 |  | T7 | TP2 |
| 1579 | 4-CHLORO-ortho-TOLUIDINE HYDROCHLORIDE, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 |  |  |
| GHIJ | 4-CHLORO-ortho-TOLUIDINE HYDROCHLORIDE, SOLUTION | 6.1 |  | III |  | 5 l | P001 IBC03 |  | - |  |
| 1590 | DICHLOROANILINES, LIQUID | 6.1 |  | II |  | 100 ml | P001 IBC02 |  | T7 | TP2 |
| XXXX | DICHLOROANILINES, SOLID | 6.1 |  | II |  | 500 g | P002 IBC08 | B2, B4 |  |  |
| 1597 | DINITROBENZENES, SOLUTION | 6.1 |  | II |  | 100 ml | P001 IBC02 |  | T7 | TP2 |
| XXXX | DNITROBENZENES, SOLID | 6.1 |  | II |  | 500 g | P002 IBC08 | B2, B4 |  |  |
| 1650 | Beta-NAPHTHYLAMINE, SOLID | 6.1 |  | II |  | 500 g | P002 IBC08 | B2, B4 | - |  |
| XXXX | Beta-NAPHTHYLAMINE, SOLUTION | 6.1 |  | II |  | 100 ml | P001 IBC02 |  | T7 | TP2 |
| 1656 | NICOTINE HYDROCHLORIDE, LIQUID | 6.1 |  | II | 43 | 100ml | P001 IBC02 |  |  |  |
| XXXX | NICOTINE HYDROCHLORIDE SOLUTION | 6.1 |  | II | 43 | 100ml | P001 IBC02 |  | Note: is now an existing entry under UN 1656 |  |
| HIJK | NICOTINE HYDROCHLORIDE, SOLID | 6.1 |  | II | 43 | 500 g | P002 IBC08 | B2, B4 | Note: is now an existing entry under UN 1656 |  |
| 1658 | NICOTINE SULPHATE, SOLUTION | 6.1 |  | II |  | 100 ml | P001 IBC02 |  | T7 | TP2 |
| IJKL | NICOTINE SULPHATE, SOLID | 6.1 |  | II |  | 500 g | P002 IBC08 | B2, B4 | Note: is now an existing entry under UN 1658 |  |
| JKLM | POTASSIUM CYANIDE, SOLUTION | 6.1 |  | I |  | NONE | P001 |  | T14 | TP2 TP13 |
| JKLM | POTASSIUM CYANIDE, SOLUTION | 6.1 |  | II |  | 100 ml | P001 IBC02 |  | T11 | TP2, TP13, TP27 |
| JKLM | POTASSIUM CYANIDE, SOLUTION | 6.1 |  | III |  | 5 l | P001 IBC03 LP01 |  | T7 | TP2, TP13, TP28 |
| 1664 | NITROTOLUENES, LIQUID | 6.1 |  | II |  | 100ml | P001 IBC02 |  | T7 | TP2 |
| XXXX | NITROTOLUENES, SOLID | 6.1 |  | II |  | 500g | P002 IBC08 | B2, B4 | Note: is now an existing entry under UN 1664 |  |
| 1665 | NITROXYLENES, LIQUID | 6.1 |  | II |  | 100 ml | P001 IBC02 |  | T7 | TP2 |
| XXXX | NITROXYLENES, SOLID | 6.1 |  | II |  | 500 g | P002 IBC08 | B2, B4 | Note: is now an existing entry under UN 1665 - | - |
| 1680 | POTASSIUM CYANIDE, SOLID | 6.1 |  | I |  | NONE | P002 IBC07 | B1 | - | - |
| MNOP | SODIUM CYANIDE, SOLUTION | 6.1 |  | I |  | NONE | P001 |  | T14 | TP2 TP13 |
| MNOP | SODIUM CYANIDE SOLUTION | 6.1 |  | II |  | 100 ml | P001 IBC02 |  | T11 | TP2 TP13 TP27 |
| MNOP | SODIUM CYANIDE SOLUTION | 6.1 |  | III | 223 | 5 l | P001 IBC03 LP01 |  | T7 | TP2 TP13 TP28 |
| 1689 | SODIUM CYANIDE, SOLID | 6.1 |  | I |  | NONE | P002 IBC07 |  | - | - |
| NOPQ | SODIUM FLUORIDE, SOLUTION | 6.1 |  | III |  | 5 l | P001 IBC03 LP01 |  | T4 | TP1 |
| 1690 | SODIUM FLUORIDE, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 |  |  |
| 1693 | TEAR GAS SUBSTANCE, LIQUID, N.O.S. | 6.1 |  | I | 274 | NONE | P001 |  |  |  |
| 1693 | TEAR GAS SUBSTANCE, LIQUID, N.O.S. | 6.1 |  | II | 274 | NONE | P001 IBC02 |  |  |  |
| OPQR | TEAR GAS SUBSTANCE, SOLID, N.O.S. | 6.1 |  | I | 274 | NONE | P002 |  | Note: is now an existing entry under UN 1693 |  |
| OPQR | TEAR GAS SUBSTANCE, SOLID, N.O.S. | 6.1 |  | II | 274 | NONE | P002 IBC08 | B2, B4 | Note: is now an existing entry under UN 1693 |  |
| 1694 | Bromobenzyl cyanides, liquid | 6.1 |  | I | 138 | NONE | P001 |  | T14 | TP2 TP13 |
| PQRS | Bromobenzyl cyanides, solid | 6.1 |  | I | 138 | NONE | P002 |  | Note: is now an existing entry under UN 1694 |  |
| QRST | CHLOROACETOPHENONE, LIQUID | 6.1 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1697 | CHLOROACETOPHENONE, SOLID | 6.1 |  | II |  | NONE | P002 IBC08 | B2, B4 |  |  |
| 1699 | DIPHENYLCHLOROARSINE, LIQUID | 6.1 |  | I |  | NONE | P001 |  |  |  |
| RSTU | DIPHENYLCHLOROARSINE, SOLID | 6.1 |  | I |  | NONE | P002 IBC07 | B1 | Note: is now an existing entry under UN 1699 |  |
| 1701 | XYLYL BROMIDE, LIQUID | 6.1 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| XXXX | XYLYL BROMIDE, SOLID | 6.1 |  | II |  | NONE | P002 IBC08 | B2, B4 |  |  |
| 1708 | Toluidines, liquid | 6.1 |  | II | 279 | 100 ml | P001 IBC02 |  | T7 | TP2 |
| STUV | Toluidines, SOLID | 6.1 |  | II | 279 | 500 g | P002 IBC08 | B2, B4 | Note: is now an existing entry under UN 1708 [T7] | [TP2] |
| TUVW | 2,4-TOLUYLENEDIAMINE, SOLUTION | 6.1 |  | III |  | 500 ml | P001 IBC03 LP01 |  | T4 | TP1 |
| 1709 | 2,4-TOLUYLENEDIAMINE, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 |  |  |
| 1729 | ANISOYL CHLORIDE, LIQUID | 8 |  | II |  | 1 l | P001 IBC02 |  | T7 | TP2 |
| UVWX | ANISOYL CHLORIDE, SOLID | 8 |  | II |  | 1 kg | P002 IBC08 | B2, B4 |  |  |
| 1711 | XYLIDINES, LIQUID | 6.1 |  | II |  | 100ml | P001 IBC02 |  | T7 | TP2 |
| XXXX | XYLIDINES, SOLID | 6.1 |  | II |  | 500g | P002 IBC08 | B2, B4 | Note: is now an existing entry under UN 1711 [T7] | [TP2] |
| 1742 | BORON TRIFLUORIDE ACETIC ACID COMPLEX, LIQUID | 8 |  | II |  | 1 l | P001 IBC02 |  | T8 | TP2 TP12 |
| VWXY | BORON TRIFLUORIDE ACETIC ACID COMPLEX, SOLID | 8 |  | II |  | 1 kg | P002 IBC08 | B2, B4 |  |  |
| 1743 | BORON TRIFLUORIDE PROPIONIC ACID COMPLEX, LIQUID | 8 |  | II |  | 1 l | P001 IBC02 |  | T8 | TP2 TP12 |
| WXYZ | BORON TRIFLUORIDE PROPIONIC ACID COMPLEX, SOLID | 8 |  | II |  | 1 kg | P002 IBC08 | B2, B4 |  |  |
| ZABC | POTASSIUM HYDROGENDIFLUORIDE, SOLUTION | 8 | 6.1 | II |  | 1 l | P001 IBC02 |  | T7 | TP2 |
| 1801 | POTASSIUM HYDROGENDIFLUORIDE, SOLID | 8 | 6.1 | II |  | 1 kg | P002 IBC08 | B2, B4 |  |  |
| 1805 | PHOSPHORIC ACID, SOLUTION | 8 |  | III |  | 5 l | P001 IBC03 LP01 |  | T4 | TP1 |
| XXXX | PHOSPHORIC ACID, SOLID | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | Note: is now an existing entry under UN 1805 |  |
| ZBCD | POTASSIUM FLUORIDE, SOLUTION | 6.1 |  | III |  | 5 l | P001 IBC03 LP01 |  | T4 | TP1 |
| 1812 | POTASSIUM FLUORIDE, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 |  |  |
| 1835 | TETRAMETHYLAMMONIUM HYDROXIDE, SOLUTION | 8 |  | II |  | 1 l | P001 IBC02 |  | T7 | TP2 |
| XXXX | TETRAMETHYLAMMONIUM HYDROXIDE, SOLID | 8 |  | II |  | 1 kg | P002 IBC08 | B2, B4 |  |  |
| 1843 | AMMONIUM DINITRO-o-CRESOLATE, SOLID | 6.1 |  | II |  | 500 g | P002 IBC08 | B2, B4 |  |  |
| XXXX | AMMONIUM DINITRO-o-CRESOLATE, SOLUTION | 6.1 |  | II |  | 100 ml | P001 IBC02 |  | T7 | TP2 |
| 1938 | BROMOACETIC ACID, SOLUTION | 8 |  | II |  | 1 l | P001 IBC02 |  | T7 | TP2 |
| ZCDE | BROMOACETIC ACID, SOLID | 8 |  | II |  | 1 kg | P002 IBC08 | B2, B4 |  |  |
| 2038 | DINITROTOLUENES, LIQUID | 6.1 |  | II |  | 100 ml | P001 IBC02 |  | T7 | TP2 |
| XXXX | DINITROTOLUENES, SOLID | 6.1 |  | II |  | 500 g | P002 IBC08 | B2, B4 | Note: is now an existing entry under UN 2038 [T7] | [TP2] |
| 2074 | ACRYLAMIDE, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 |  |  |
| ZDEF | ACRYLAMIDE, SOLUTION | 6.1 |  | III |  | 5 l | P001 IBC03 LP01 |  | T4 | TP1 |
| 2076 | CRESOLS, LIQUID | 6.1 | 8 | II |  | 100 ml | P001 IBC02 |  | T7 | TP2 |
| XXXX | CRESOLS, SOLID | 6.1 | 8 | II |  | 500 g | P002 IBC08 | B2, B4 | Note: is now an existing entry under UN 2076 [T7] | [TP2] |
| 2077 | alpha-NAPHTHYLAMINE, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 |  |  |
| XXXX | alpha-NAPHTHYLAMINE, SOLUTION | 6.1 |  | III |  | 5 l | P001 IBC03 LP01 |  | T3 | TP1 |
| 2235 | CHLOROBENZYL CHLORIDES, LIQUID | 6.1 |  | III |  | 5 l | P001 IBC03 LP01 |  | T4 | TP1 |
| XXXX | CHLOROBENZYL CHLORIDES, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 |  |  |
| 2236 | 3-CHLORO-4-METHYLPHENYL ISOCYANATE, LIQUID | 6.1 |  | II |  | 100 ml | P001 IBC02 |  |  |  |
| ZEFG | 3-CHLORO-4-METHYLPHENYL ISOCYANATE, SOLID | 6.1 |  | II |  | 500 g | P002 IBC08 | B2, B4 |  |  |
| 2239 | CHLOROTOLUIDINES, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 |  |  |
| XXXX | CHLOROTOLUIDINES, LIQUID | 6.1 |  | III |  | 5 l | P001 IBC03 LP01 |  | T4 | TP1 |
| 2261 | XYLENOLS, SOLID | 6.1 |  | II |  | 500 g | P002 IBC08 | B2, B4 |  |  |
| XXXX | XYLENOLS, LIQUID | 6.1 |  | II |  | 100 ml | P001 IBC02 |  | T7 | TP2 |
| 2306 | NITROBENZOTRIFLUORIDES, LIQUID | 6.1 |  | II |  | 100 ml | P001 IBC02 |  | T7 | TP2 |
| XXXX | NITROBENZOTRIFLUORIDES, SOLID | 6.1 |  | II |  | 500 g | P002 IBC08 | B2, B4 |  |  |
| 2308 | NITROSYLSULPHURIC ACID, LIQUID | 8 |  | II |  | 1 l | P001 IBC02 |  | T8 | TP2 TP12 |
| XXXX | NITROSYLSULPHURIC ACID, SOLID | 8 |  | II |  | 1 kg | P002 IBC08 | B2, B4 | Note: is now an existing entry under UN 2308 [T8] | [TP2, TP12] |
| 2315 | POLYCHLORINATED BIPHENYLS, LIQUID | 9 |  | II | 305 | 1 l | P906 IBC02 |  | T4 | TP1 |
| XXXX | POLYCHLORINATED BIPHENYLS, SOLID | 9 |  | II | 305 | 1 kg | P906 IBC08 |  |  |  |
| 2433 | CHLORONITROTOLUENES, LIQUID | 6.1 |  | III |  | 5 l | P001 IBC03 LP01 |  | T4 | TP1 |
| XXXX | CHLORONITROTOLUENES, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | Note: is now an existing entry under UN 2433 |  |
| 2445 | LITHIUM ALKYLS, LIQUID | 4.2 | 4.3 | I |  | NONE | P400 |  | T21 | TP3 TP7 |
| XXXX | LITHIUM ALKYLS, SOLID | 4.2 | 4.3 | I |  | NONE | P400 |  |  |  |
| 2446 | NITROCRESOLS, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 |  |  |
| XXXX | NITROCRESOLS, LIQUID | 6.1 |  | III |  | 5 l | P001 IBC03 LP01 |  | T4 | TP1 |
| 2511 | 2-CHLOROPROPIONIC ACID, or 2-CHLOROPROPIONIC ACID, SOLUTION | 8 |  | III |  | 5 l | P001 IBC03 LP01 |  | T4 | TP2 |
| ZGHI | HYDROQUINONE, SOLUTION | 6.1 |  | III |  | 5 l | P001 IBC03 LP01 | B3 | T4 | TP1 |
| 2662 | HYDROQUINONE, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 |  |  |
| 2552 | HEXAFLUOROACETONE HYDRATE, LIQUID | 6.1 |  | II |  | 100 ml | P001 IBC02 |  | T7 | TP2 |
| XXXX | HEXAFLUOROACETONE HYDRATE ,SOLID | 6.1 |  | II |  | 500 g | P002 IBC08 | B2, B4 |  |  |
| 2669 | CHLOROCRESOLS, SOLUTION | 6.1 |  | II |  | 100 ml | P001 IBC02 |  | T7 | TP2 |
| XXXX | CHLOROCRESOLS, SOLID | 6.1 |  | II |  | 500 g | P002 IBC08 | B2, B4 |  |  |
| 2730 | NITROANISOLES, LIQUID | 6.1 |  | III | 279 | 5 l | P001 IBC03 LP01 |  | T4 | TP1 |
| XXXX | NITROANISOLES, SOLID | 6.1 |  | III | 279 | 5 kg | P002 IBC08 LP02 | B3 | Note: is now an existing entry under UN 2730 [T4] | [TP1] |
| 2732 | NITROBROMOBENZENES, LIQUID | 6.1 |  | III |  | 5 l | P001 IBC03 LP01 |  | T4 | TP1 |
| XXXX | NITROBROMOBENZENES, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | Note: is now an existing entry under UN 2732 [T4] | [TP1] |
| 2753 | N-ETHYLBENZYLTOLUIDINES , LIQUID | 6.1 |  | III |  | 5 l | P001 IBC03 LP01 |  | T7 | TP1 |
| XXXX | N-ETHYLBENZYLTOLUIDINES , SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | Note: is now an existing entry under UN 2753 [T7] | [TP1] |
| 3052 | ALUMINIUM ALKYL HALIDES, LIQUID | 4.2 | 4.3 | I |  | NONE | P400 |  | T21 | TP2 TP7 TP9 |
| ZHIJ | ALUMINIUM ALKYL HALIDES, SOLID | 4.2 | 4.3 | I |  | NONE | P404 |  | Note: is now an existing entry under UN 3052 |  |
| 2937 | alpha-METHYLBENZYL ALCOHOL, LIQUID | 6.1 |  | III |  | 5 l | P001 IBC03 LP01 |  | T4 | TP1 |
| XXXX | alpha-METHYLBENZYL ALCOHOL, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 |  |  |
| 3052 | ALUMINIUM ALKYL HALIDES, LIQUID | 4.2 | 4.3 | I |  | NONE | P400 |  | T21 | TP2 TP7 TP9 |
| XXXX | ALUMINIUM ALKYL HALIDES, SOLID | 4.2 | 4.3 | I |  | NONE | P404 |  | Note: is now an existing entry under UN 3052 |  |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, LIQUID, N.O.S. | 6.1 |  | I | 210 274 | NONE | P001 |  |  |  |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, LIQUID, N.O.S. | 6.1 |  | II | 210 274 | 100 ml | P001 IBC02 |  |  |  |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, LIQUID, N.O.S. | 6.1 |  | III | 210 223 274 | 5 l | P001 IBC03 LP01 |  |  |  |
| ZIJK | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 |  | I | 210 274 | NONE | P002 IBC07 | B1 | Note: is now an existing entry under UN 3172 |  |
| ZIJK | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 |  | II | 210 274 | 500 g | P002 IBC08 | B2, B4 | Note: is now an existing entry under UN 3172 |  |
| ZIJK | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 |  | III | 210 223 274 | 5 kg | P002 IBC08 | B3 | Note: is now an existing entry under UN 3172 |  |
| 3203 | PYROPHORIC ORGANOMETALLIC COMPOUND, LIQUID, WATER-REACTIVE, N.O.S. | 4.2 | 4.3 | I | 274 | NONE | P400 |  | T21 | TP2 TP7 TP9 |
| ZJKL | PYROPHORIC ORGANOMETALLIC COMPOUND, SOLID, WATER-REACTIVE, N.O.S. | 4.2 | 4.3 | I | 274 | NONE | P404 | Note: is now an existing entry under UN 3203 | T21 | TP2 TP7 TP9 |
| [3245 | GENETICALLY MODIFIED ORGANISMS | 9 |  |  | 219 | NONE | P904 IBC99] | Note: UN 3245 not to be split |  |  |
| [ |  |  |  |  |  |  | ] |  |  |  |
| 3276 | NITRILES, TOXIC, LIQUID, N.O.S. | 6.1 |  | I | 274 | NONE | P001 |  | T14 | TP2 TP9 TP13 TP27 |
| 3276 | NITRILES, TOXIC, LIQUID, N.O.S. | 6.1 |  | II | 274 | 100 ml | P001 IBC02 |  | T11 | TP2 TP27 |
| 3276 | NITRILES, TOXIC, LIQUID, N.O.S. | 6.1 |  | III | 223 274 | 5 l | P001 IBC03 LP01 |  | T7 | TP1 TP28 |
| XXXX | NITRILES, TOXIC, SOLID, N.O.S. | 6.1 |  | I | 274 | NONE | P002 IBC07 | B1 |  |  |
| XXXX | NITRILES, TOXIC, SOLID N.O.S. | 6.1 |  | II | 274 | 500 g | P002 IBC08 | B2, B4 |  |  |
| XXXX | NITRILES, TOXIC, SOLID, N.O.S. | 6.1 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 |  |  |
| 3278 | ORGANOPHOSPHOROUS COMPOUND, TOXIC, N.O.S., LIQUID | 6.1 |  | I | 43 274 | NONE | P001 |  | T14 | TP2 TP9 TP13 TP27 |
| 3278 | ORGANOPHOSPHOROUS COMPOUND, TOXIC, LIQUID, N.O.S. | 6.1 |  | II | 43 274 | 100 ml | P001 IBC02 |  | T11 | TP2 TP27 |
| 3278 | ORGANOPHOSPHOROUS COMPOUND, TOXIC, LIQUID, N.O.S. | 6.1 |  | III | 43 223 274 | 5 l | P001 IBC03 LP01 |  | [T7] | [TP1 TP28] |
| ZKLM | ORGANOPHOSPHOROUS COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 | now an existing entry under UN 3278 | I | 43 274 | NONE | P002 IBC07 | B1 | [T14] | [TP2 TP9 TP27] |
| ZKLM | ORGANOPHOSPHOROUS COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 | now an existing entry under UN 3278 | II | 43 274 | 500 g | P002 IBC08 | B2, B4 | [T11] | [TP2 TP27] |
| ZKLM | ORGANOPHOSPHOROUS COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 | now an existing entry under UN 3278 | III | 43 223 274 | 5 kg | P002 IBC08 LP02 | B3 | [T7] | [TP1 TP28] |
| 3280 | ORGANOARSENIC COMPOUND, LIQUID, N.O.S. | 6.1 |  | I | 274 | NONE | P001 |  | T14 | TP2 TP9 TP27 |
| 3280 | ORGANOARSENIC COMPOUND, LIQUID, N.O.S., | 6.1 |  | II | 274 | 100 ml | P001 IBC02 |  | T11 | TP2 TP27 |
| 3280 | ORGANOARSENIC COMPOUND, LIQUID, N.O.S., | 6.1 |  | III | 223 274 | 5 l | P001 IBC03 LP01 |  | T7 | TP1 TP28 |
| ZLMN | ORGANOARSENIC COMPOUND, SOLID, N.O.S., | 6.1 |  | I | 274 | NONE | P002 IBC07 | B1 | now an existing entry under UN 3280 [T14] | [TP2 TP9 TP27] |
| ZLMN | ORGANOARSENIC COMPOUND, SOLID, N.O.S., | 6.1 |  | II | 274 | 500 g | P002 IBC08 | B2, B4 | now an existing entry under UN 3280 [T11] | [TP2 TP27] |
| ZLMN | ORGANOARSENIC COMPOUND, SOLID, N.O.S., | 6.1 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | now an existing entry under UN 3280 [T7] | [TP1 TP28] |
| 3281 | METAL CARBONYLS, LIQUID, N.O.S. | 6.1 |  | I | 274 | NONE | P601 |  | T14 | TP2 TP9 TP13 TP27 |
| 3281 | METAL CARBONYLS, LIQUID, N.O.S. | 6.1 |  | II | 274 | 100 ml | P001 IBC02 |  | T11 | TP2 TP27 |
| 3281 | METAL CARBONYLS, LIQUID, N.O.S. | 6.1 |  | III | 223 274 | 5 l | P001 IBC03 LP01 |  | T7 | TP1 TP28 |
| ZMNO | METAL CARBONYLS, SOLID, N.O.S. | 6.1 |  | I | 274 | NONE | P002 IBC07 | B1 | now an existing entry under UN 3281 [T14] | [TP2 TP9 TP27] |
| ZMNO | METAL CARBONYLS, SOLID, N.O.S. | 6.1 |  | II | 274 | 500 g | P002 IBC08 | B2, B4 | now an existing entry under UN 3281 [T11] | [TP2 TP27] |
| ZMNO | METAL CARBONYLS, SOLID, N.O.S. | 6.1 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | now an existing entry under UN 3281 [T7] | [TP1 TP28] |
| 3282 | ORGANOMETALIC COMPOUND, TOXIC, LIQUID, N.O.S. | 6.1 |  | I | 274 | NONE | P001 |  | T14 | TP2 TP9 TP13 TP27 |
| 3282 | ORGANOMETALIC COMPOUND, TOXIC, LIQUID, N.O.S. | 6.1 |  | II | 274 | 100 ml | P001 IBC02 |  | T11 | TP2 TP27 |
| 3282 | ORGANOMETALIC COMPOUND, TOXIC, LIQUID, N.O.S. | 6.1 |  | III | 223 274 | 5 l | P001 IBC03 LP01 |  | T7 | TP1 TP28 |
| ZNOP | ORGANOMETALIC COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 |  | I | 274 | NONE | P002 IBC07 | B1 | now an existing entry under UN 3282 [T14] | [TP2 TP9 TP27] |
| ZNOP | ORGANOMETALIC COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 |  | II | 274 | 500 g | P002 IBC08 | B2, B4 | now an existing entry under UN 3282 [T11] | [TP2 TP27] |
| ZNOP | ORGANOMETALIC COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | now an existing entry under UN 3282 [T7] | [TP1 TP28] |
| 3283 | SELENIUM COMPOUNDS, SOLID, N.O.S. | 6.1 |  | I |  | NONE | P002 IBC07 | B1 |  |  |
| 3283 | SELENIUM COMPOUNDS, SOLID, N.O.S. | 6.1 |  | II |  | 500 g | P002 IBC08 | B2, B4 |  |  |
| 3283 | SELENIUM COMPOUNDS, SOLID, N.O.S. | 6.1 |  | III | 223 | 5 kg | P002 IBC08 LP02 | B3 |  |  |
| XXXX | SELENIUM COMPOUNDS , LIQUID, N.O.S. | 6.1 |  | I |  | NONE | P001 |  | T14 | TP2 TP9 TP27 |
| XXXX | SELENIUM COMPOUNDS , LIQUID, N.O.S. | 6.1 |  | II |  | 500 ml | P001 IBC02 |  | T11 | TP2 TP27 |
| XXXX | SELENIUM COMPOUNDS , LIQUID, N.O.S. | 6.1 |  | III | 223 | 5 l | P001 IBC03 |  | T7 | TP1 TP28 |
| 3315 | CHEMICAL SAMPLE, TOXIC, LIQUID | 6.1 |  | I | 250 | NONE | P099 |  |  |  |
| ZOPQ | CHEMICAL SAMPLE, TOXIC, SOLID | 6.1 |  | I | 250 | NONE | P099 | now an existing entry under UN 3315 |  |  |

# Text boxes

STSTE

Secretariat