#### UNITED

NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2002/79

21 October 2002

ENGLISH ONLY

# COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

##### Sub-Committee of Experts on the

# Transport of Dangerous Goods

# (Twenty-second session, 2-6 December 2002

agenda item( 4 (b))

# NEW PROPOSALS

New issues

# Dangerous Goods List, Wetted Explosives

## Transmitted by the expert from the International Air Transport Association (IATA)

IATA presented this paper to the ICAO Dangerous Goods Panel working group (WG 02) in Frankfurt, on September 19, 2002. After discussion, IATA was invited to present the paper to the Sub-Committee for consideration.  Some States indicated they had not had sufficient time to consult with the appropriate experts and that they would wish to submit comments.  In order not to unduly delay submission of this paper, it is submitted in the form it was submitted to ICAO and may be revised once comments have been received.

Background:

  - Reference is made to the report of ICAO DGP/18, Appendix C, Amendments to Table 3.1 - Dangerous Goods List. In this report, new UN numbers for Division 4.1 substances (wetted explosives) were added to the Dangerous Goods List. In analyzing the new additions, anomalies were found that are discussed hereafter. As these anomalies stem from the UN Orange book (12 edition) the

  - The wetted explosives under review are indicated in the following table:

| Ref # | Status | UN No. | Name | Class or Division | SP | Passenger Aircraft | Cargo Aircraft |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | PG | PaxPl | Qty | CarPI | Qty |
| 1a | Existing | 0154 | Picric acid, dry or wetted with less than 30% water, by mass | 1.1D |  | Forbidden | Forbidden |
| 1b | New | 3364 | Picric acid, wetted with not less than 10% water, by mass | 4.1 | A40 | I | 416 | 0.5 kg | 416 | 0.5 kg |
| 2a | Existing | 0154 | Trinitrophenol, dry or wetted with less than 30% water, by mass | 1.1D |  | Forbidden | Forbidden |
| 2b | Existing | 1344 | Trinitrophenol, wetted with not less than 30% water, by mass | 4.1 | A40 | I | 416 | 1 kg | 412 | 15 kg |
| 2c | New | 3364 | Trinitrophenol, wetted with not less than 10% water, by mass | 4.1 | A40 | I | 416 | 0.5 kg | 416 | 0.5 kg |
| 3a | Existing | 0155 | Picryl chloride | 1.1D |  | Forbidden | Forbidden |
| 3b | New | 3365 | Picryl chloride, wetted with not less than 10% water, by mass | 4.1 | A40 | I | 416 | 0.5 kg | 416 | 0.5 kg |
| 4a | Existing | 0155 | Trinitrochlorobenzene | 1.1D |  | Forbidden | Forbidden |
| 4b | New | 3365 | Trinitrochlorobenzene, wetted with not less than 10% water, by mass | 4.1 | A40 | I | 416 | 0.5 kg | 416 | 0.5 kg |
| 5a | Existing | 0209 | TNT, dry or wetted with less than 30% water, by mass | 1.1D |  | Forbidden | Forbidden |
| 5b | New | 3366 | TNT, wetted with not less than 10% water, by mass | 4.1 |  | I | 416 | 0.5 kg | 416 | 0.5 kg |
| 6a | Existing | 0209 | Trinitrotoluene, dry or wetted with less than 30% water, by mass | 1.1D |  | Forbidden | Forbidden |
| 6b | Existing | 1356 | Trinitrotoluene, wetted with not less than 30% water, by mass | 4.1 | A40 | I | 416 | 0.5 kg | 416 | 0.5 kg |
| 6c | New | 3366 | Trinitrotoluene, wetted with not less than 10% water, by mass | 4.1 |  | I | 416 | 0.5 kg | 416 | 0.5 kg |
| 7a | Existing | 0214 | Trinitrobenzene, dry or wetted with less than 30% water, by mass | 1.1D |  | Forbidden | Forbidden |
| 7b | Existing | 1354 | Trinitrobenzene, wetted with not less than 30% water, by mass | 4.1 | A40 | I | 416 | 0.5 kg | 416 | 0.5 kg |
| 7c | New | 3367 | Trinitrobenzene, wetted with not less than 10% water, by mass | 4.1 |  | I | 416 | 0.5 kg | 416 | 0.5 kg |
| 8a | Existing | 0215 | Trinitrobenzoic acid, dry or wetted with less than 30% water, by mass | 1.1D |  | Forbidden | Forbidden |
| 8b | Existing | 1355 | Trinitrobenzoic acid, wetted with not less than 30% water, by mass | 4.1 | A40 | I | 416 | 0.5 kg | 416 | 0.5 kg |
| 8c | New | 3368 | Trinitrobenzoic acid, wetted with not less than 10% water, by mass | 4.1 |  | I | 416 | 0.5 kg | 416 | 0.5 kg |
| 9a | Existing | 0234 | Sodium dinitro-o-cresolate dry or wetted with less than 15% water, by mass | 1.3C |  | Forbidden | Forbidden |
| 9b | Existing | 1348 | Sodium dinitro-o-cresolate, wetted with not less than 15% water, by mass | 4.1 & 6.1 (sub risk) | A40 | I | 416 | 1kg | 412 | 15 kg |
| 9c | New | 3369 | Sodium dinitro-o-creosolate, wetted with not less than 10% water, by mass | 4.1 |  | I | 416 | 0.5 kg | 416 | 0.5 kg |
| 10a | Existing | 0220 | Urea nitrate dry or wetted with less than 20% water, by mass | 1.1D |  | Forbidden | Forbidden |
| 10b | Existing | 1357 | Urea nitrate, wetted with not less than 20% water, by mass | 4.1 | A101 | I | 416 | 1kg | 412 | 15 kg |
| 10c | New | 3370 | Urea nitrate, wetted with not less than 10% water, by mass | 4.1 |  | I | 416 | 0.5 kg | 416 | 0.5 kg |

  - In comparing the existing wetted explosives in the 2001-02 ICAO Technical Instructions with the new UN entries mentioned in the DGP/18, the following inconsistencies were found:

- Of the ten (10) new wetted explosives entries, only four (4) had Special Provision A40 assigned, i.e. UN 3364 (Picric acid and Trinitrophenol) and UN 3365 (Picryl chloride and Trinitrophenol). It was also noted in DGP/18, Item 2.4.8.6 that Special Provision A40 (SP 28 in the UNCOE) would be assigned to all the wetted explosive entries. That was not followed through for UN 3366, 3367, 3368, 3369.

- On a similar note, the new entry for Urea nitrate (UN 3370) was not assigned the Special Provision A101 as the similar existing Urea nitrate entry (UN 1357).

- The existing wetted explosive Sodium dinitro-o-cresolate UN 1348 (Ref #9b) requires a water concentration not less than 15% and is classified under Division 4.1 with a toxic sub-risk (6.1). The new entry UN 3369 (Ref #9c) has a water concentration not less than 10% but is classified under 4.1 only. UN 3369 is more concentrated than the existing wetted explosive UN 1348, but does not have the sub-risk 6.1.

- Three (3) new Division 4.1 entries (UN 3366, 3367 and 3368) have identical packing group, packing instruction and quantity limitations for passenger and cargo aircraft as the existing Division 4.1 entries (UN 1356, 1354 and 1355, respectively) with the only difference being the water concentration. The new entries require a water concentration not less than 10% while the existing entries require a water concentration not less than 30%. In addition, the Division 1.1D entries of these substances (UN 0209, 0214 and 0215) require a water concentration less than 30%.

The various water concentrations of the same substance overlap and cause confusion. For example, if one was to ship such a wetted explosive with 35% water concentration, both the new and existing Division 4.1 wetted explosives would apply. However in this case, the packing instructions and quantities would be the same. But if one was to ship a wetted explosive with 20% water concentration, both the new Division 4.1 wetted explosive and the existing Division 1.1D wetted explosive which is completely forbidden would apply. Hence, the need for clarification.

- There are three (3) cases with double nomenclature entries (Ref #1-6). Picric acid (Ref #1) with Trinitrophenol (Ref #2), Picryl chloride (Ref #3) with Trinitrochlorobenzene (Ref #4) and finally TNT (Ref #5) with Trinitrotoluene (Ref #6). Most entries in the Dangerous Goods List make reference to the proper chemical name.

- Trinitrophenol (Ref#2) has three different entries for various water concentrations, however Picric acid (Ref#1), the same substance, has only two entries. The same case applies to TNT (Ref#5) with Trinitrotoluene (Ref#6). It is proposed to add UN 1344 (Ref#2b) as an entry under Picric acid and to add UN 1356 (Ref#6b) as an entry under TNT.

2. PROPOSAL

  - The following proposals are described below to resolve the inconsisties listed above in 1.3.

- Add Special Provision A40 to UN 3366, 3367, 3368 and 3369.

- Add Special Provision A101 to UN 3370.

- Add sub-risk 6.1 to UN 3369.

- It is proposed to amend the water concentration of the new UN wetted explosive entries (UN 3366, 3367 and 3368) and to delete the othername description of the Division 1.1D entries for UN 0209, 0214 and 0215. This would eliminate the water concentration overlap. Please refer to the table below for the proposed modifications:

| Ref # | Status | UN No. | Name | Class or Division | SP | Passenger Aircraft | Cargo Aircraft |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 6a | Existing | 0209 | Trinitrotoluene | 1.1D |  | Forbidden | Forbidden |
| 6b | Existing | 1356 | Trinitrotoluene, wetted with 30% or more water, by mass | 4.1 | A40 | I | 416 | 0.5 kg | 416 | 0.5 kg |
| 6c | New | 3366 | Trinitrotoluene, wetted with not less than 10% but less than 30& water, by mass | 4.1 | A40 | I | 416 | 0.5 kg | 416 | 0.5 kg |
| 7a | Existing | 0214 | Trinitrobenzene | 1.1D |  | Forbidden | Forbidden |
| 7b | Existing | 1354 | Trinitrobenzene, wetted with 30% or more water, by mass | 4.1 | A40 | I | 416 | 0.5 kg | 416 | 0.5 kg |
| 7c | New | 3367 | Trinitrobenzene, wetted with not less than 10% but less than 30& water, by mass | 4.1 | A40 | I | 416 | 0.5 kg | 416 | 0.5 kg |
| 8a | Existing | 0215 | Trinitrobenzoic acid | 1.1D |  | Forbidden | Forbidden |
| 8b | Existing | 1355 | Trinitrobenzoic acid, wetted with 30% or more water, by mass | 4.1 | A40 | I | 416 | 0.5 kg | 416 | 0.5 kg |
| 8c | New | 3368 | Trinitrobenzoic acid, wetted with not less than 10% but less than 30& water, by mass | 4.1 | A40 | I | 416 | 0.5 kg | 416 | 0.5 kg |

After reviewing the proposed changes above, the need for the existing Division 4.1 entries (UN 1356, 1354 and 1355) requires clarification. Their parameters remain the same as the new entries of UN 3366, 3367 and 3368 with the only difference being the new 10% water concentration. A clarification by the UNSCOE explosive experts is required.

- It is proposed that Picric acid, Picryl chloride and TNT refer to their respective proper chemical name. Please see table below for the modifications.

| 1a | Existing | Picric acid, dry or wetted with less than 30% water, by mass, see Trinitrophenol, dry or wetted with less than 30% water, by mass (UN 0154) |
| --- | --- | --- |
| 1b | New | Picric acid, wetted with not less than 10% water, by mass, see Trinitrophenol, wetted with not less than 10% water, by mass (UN 1356) |
| 3a | Existing | Picryl chloride, see Trinitrochlorobenzene (UN 0155) |
| 3b | New | Picryl chloride, wetted with not less than 10% water, by mass, see Trinitrochlorobenzene, wetted with not less than 10% water, by mass (UN 3365) |
| 5a | Existing | TNT, dry or wetted with less than 30% water, by mass, see Trinitrotoluene, dry or wetted with less than 30% water, by mass (UN 0209) |
| 5b | New | TNT, wetted with not less than 10% water, by mass, see Trinitrotoluene, wetted with not less than 10% water, by mass (UN 3366) |

- It is proposed to add the following two entries in Table 3.1:

- Picric acid, wetted  with not less than 30% water by mass (UN 1344); and

- TNT, wetted with not less than 30% water by mass (UN 1356).

|  | Add | Picric acid, wetted with not less than 30% water, by mass, see Trinitrophenol, wetted with not less than 30% water, by mass (UN 1344) |
| --- | --- | --- |
|  | Add | TNT, wetted with not less than 30% water, by mass, see Trinitrotoluene, wetted with not less than 30% water, by mass (UN 1356) |

  - According to the DGP/18 Report, Item 2.4.8.6, the ICAO Secretary was asked to raise the issue of UN 0209, 1356 and 3366 for resolution by the UNSCOE explosive experts. It appears this issue is still pending.

_________________

# Text boxes

Secretariat

STSTE