# UN/SCETDG/21/INF.23

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

(Twenty-first session, 1-10 July 2002,

agenda item 3(b))

EXPLOSIVES, SELF-REACTIVE SUBSTANCES AND ORGANIC PEROXIDES

Classification of ammonium nitrate emulsions, suspensions and gels

Corrigendum to document ST/SG/AC.10/C.3/2002/22

Transmitted by the expert from Japan

This annex replaces the annex of document ST/SG/AC.10/C.3/2002/22.

Annex

Table 1  Test 8(a) : Thermal Stability Test

| Substances | Sample mass (g) | Test T (°C) | Result | Comments |
| --- | --- | --- | --- | --- |
| ANE-J1 Ammonium nitrate 80%, Water 13%, Fuel/emulsifier 7% | 613 | 80 | - | Mass loss 0.1% |
| ANE-J2 Ammonium nitrate 76%, Water 17%, Fuel/emulsifier 7% | 605 | 80 | - | Mass loss 0.3% |
| ANE-J3 Ammonium nitrate 68%, Sodium nitrate 9%, Sodium perchlorate 5%, Water 11%, Fuel/emulsifier 7% | 583 | 80 | - | Mass loss 0.3% |
| ANE-J4 Ammonium nitrate 71%, Sodium nitrate 11%, Water 12%, Fuel/emulsifier 6% | 602 | 80 | - | Mass loss 0.1% |

Table 2  Test 8(b) : ANE Gap Test

| Substances | Density g/cm3 | Gap mm | Result | Comments |
| --- | --- | --- | --- | --- |
| ANE-J1 Ammonium nitrate 80%, Water 13%, Fuel/emulsifier 7% | 1.39 | 70 | - | Tube fragmented. Plate indented. |
| ANE-J2 Ammonium nitrate 76%, Water 17%, Fuel/emulsifier 7% | 1.42 | 70 | - | Tube fragmented. Plate indented. |
| ANE-J3 Ammonium nitrate 68%, Sodium nitrate 9%, Sodium perchlorate 5%, Water 11%, Fuel/emulsifier 7% | 1.41 | 70 | - | Tube fragmented. Plate indented. |
| ANE-J4 Ammonium nitrate 71%, Sodium nitrate 11%, Water 12%, Fuel/emulsifier 6% | 1.40 | 70 | - | Tube fragmented. Plate indented. |
| ANE-J5 (sensitized by microballoons) Ammonium nitrate 71%, Sodium nitrate 5%, Water 18%, Fuel/emulsifier 6% | 1.20 | 70 | + | Tube fragmented. Plate performed. VOD 5.7 km/s |
| ANE-J6 (sensitized by microballoons) Ammonium nitrate 80%, Water 13%, Fuel/emulsifier 7% | 1.26 | 70 | + | Tube fragmented. Plate performed. VOD 6.3 km/s |

Table 3  Test 8(c) : Koenen Test

| Substances | Result | Comments |
| --- | --- | --- |
| ANE-J1 Ammonium nitrate 80%, Water 13%, Fuel/emulsifier 7% | - | Effect type “O” |
| ANE-J2 Ammonium nitrate 76%, Water 17%, Fuel/emulsifier 7% | - | Effect type “O” |
| ANE-J3 Ammonium nitrate 68%, Sodium nitrate 9%, Sodium perchlorate 5%, Water 11%, Fuel/emulsifier 7% | - | Effect type “A” |
| ANE-J4 Ammonium nitrate 71%, Sodium nitrate 11%, Water 12%, Fuel/emulsifier 6% | - | Effect type “A” |

_____________