| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/2002/53 20 August 2002 ENGLISH Original: ENGLISH and FRENCH |
| --- | --- | --- |

##### ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

(One-hundred-and-twenty-eighth session,

12-15 November 2002, agenda item 5.2.5.)

PROPOSAL FOR DRAFT SUPPLEMENT 9 TO REGULATION No. 23

(Reversing lamps)

Transmitted by the Working Party on Lighting

and Light-Signalling (GRE)

Note:  The text reproduced below was adopted by GRE at its forty-eighth session and is transmitted for consideration to WP.29 and AC.1.  It is based on document TRANS/WP.29/GRE/2002/13, as amended (TRANS/WP.29/GRE/48, paras. 40 and 41).

__________

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Paragraph 6.3., amend to read:

"6.3.	The intensity of the light emitted in all directions in which the light can be observed shall not exceed:

300 candelas in directions in or above the horizontal plane;

and, in directions below the horizontal plane:

600 candelas between h-h and 5°D and

8000 candelas below 5°D."

_________