| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/GRRF/2003/30/Corr.1 9 September 2003 ENGLISH ONLY |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Brakes and Running Gear (GRRF)

(Fifty-fourth session, 6-8 October 2003,

agenda item 6.2.)

## PROPOSAL FOR DRAFT AMENDMENTS TO REGULATIONS Nos. 30 and 54

#### Corrigendum 1

(Pneumatic tyres and pneumatic tyres for commercial vehicles)

# Transmitted by the expert from the Russian Federation

The Note of the first page, correct the reference to document "TRANS/WP.29/GRRF/52" to read "TRANS/WP.29/GRRF/53".

____________

_______________

Note: This document is distributed to the Experts on Brakes and Running Gear only.

Part A. (Background), correct to read:

" …… It can be predicted that comparability of the test results could be …… "

Part C (Justification),:

Fourth paragraph, correct to read:

"The main disadvantage of the torque method is that parasitic losses contained in the measurement include rotational test wheel losses as well as tyre spindle losses.  Hence, the parasitic losses are larger than those of the force method and can be of the same order of magnitude as the rolling resistance itself.  In addition, speed-hunting oscillation in the drive motor can introduce errors."

Tables 1 and 2, correct to read:

"

Table 1. Passenger car tyres – Methods of measuring rolling resistance.

Comparison of test conditions

| Standard | Test method | Drum diameter [mm] | Test speed, km/h | Load, % of Max | Inflation pressure, kPa (base) | Warm-up | Temperature sensor distance (cm) |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | speed, km/h | time, minute |  |
| ISO-8767 | Force, Torque, Power, Deceleration | 1500-3000 | 80 | 80 | - 30 | 80. | 30 | 100 |
|  |  |  | 50, 90, 120 | 90 50 | -30, +70 -30, +70 |  |  |  |
| SAE-J1269, SAE-J1270 | Force, Torque, Power | 1708 (most standard) | 80 | 90 | -50, +70 | 80 | 30 | 40 |
|  |  |  |  | 50 | -30, +70 |  |  |  |
| SAE J2452 | Force | 1219-1707 | 80 | 70 | 00 | 80 | 30 | 40 |
|  |  |  | from 115 to 15 | 90 60 30 | -40, +60 -40 +10 |  |  |  |
| ОСТ-4754 (Russian Federation) | Force | 1592, 1707, 2000 | 80 | 80 | +10 +40 | 80 | 60 | 200 |
| ОСТ- 37.001.522 (Russian Federation) | Deceleration | 1592, 1707, 2000 | from max to zero | 80 | -30 | 80 | to stable temp. | 10-15 |

| Standard | Test method | Drum diameter [m] | Test speed, km/h | Load, % of Max | Inflation pressure, % of max | Warm-up | Temperature sensor Distance (cm) |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | speed, km/h | time, minute |  |
| ISO-9948 | Force, Torque, Power, Deceleration | 1.700-3.000 | 80 601) | 85 | 100 | 80. | 90 30 1/ | 100 |
|  |  |  |  | 100 75 50 25 | 100,95 70 120 70 |  |  |  |
| SAE-J1269, SAE-J1270 | Force, Torque, Power | 1708 (most standard) | 80 | 100 75 50 25 | 100,95 70 120 70 | 80 | 90 30 | 40 |
| ОСТ-5513 (Russian Federation) | Force | 1.592, 1.707, 2.000 | 80 601) | 85 | 100 | 80 601) | 60 | 200 |
| ОСТ- 37.001.522 (Russian Federation) | Deceleration | 1.592, 1.707, 2.000 | from max to zero | 85 | 100 | 80 601) | to stable temp. | 10-15 |

Table 2. Truck and bus tyres – Methods of measuring rolling resistance.

Comparison of test conditions"

___________

1/  For tyres for speed category F to J

_____________

# Text boxes

TRANS/WP.29/GRRF/2003/30/Corr.1

page 4

TRANS/WP.29/GRRF/2003/30/Corr.1

page 3