| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL TRANS/WP.5/2005/16/Add.5 29 June 2005 Original: ENGLISH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on Transport Trends and Economics

(Eighteenth session, 15-16 September 2005,

agenda item 3 (b))

MONITORING OF DEVELOPMENTS RELEVANT FOR THE PAN-EUROPEAN TRANSPORT CORRIDORS AND AREAS

Infrastructure bottlenecks and missing links

Transmitted by the Government of Germany

# Bottlenecks in the German E road network

The survey contains statements on all E roads, divided into sections which are comparable in terms of average daily volume of traffic or cross section. The upper limit for the capacity of the cross section was based on the values stated in the questionnaire to which were added the assumed values for six-lane motorways with a capacity of 90,000 vehicles per day or for eight-lane motorways with a capacity of 120,000 vehicles per day, as the case may be. The average volumes of traffic of the road sections relate to the current daily traffic conditions. The selection of the road sections listed is confined to all stretches with a traffic level/capacity ratio exceeding 1.0 (congestion). If the limits are exceeded on 80-120 days, this is classified as a bottleneck.

The table arranged according to E road numbers is divided into two parts: the first part lists the road sections intended for upgrading either as first priority projects or as second priority projects, as defined in the requirement plan for federal trunk roads which came into force on 16 October 2004. There are no plans for increasing the capacity of the road sections listed in the second part of the table.

| E Road | German Motorway No | Section | Capacity [1000 PCU/24 h] | Traffic loading 2005 [1000 PCU/24 h] | Difference | Extent of Action |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Kind | Number of lanes (actual - objective) | Program |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| Upgrade intended |
| E30 | B61 | AD Loehne - AK Bad Oeynhausen | 15 | 40 | -25 | Upgrade | 24 | F |
| E30 | A2 | AK Hannover Ost - Lehrte Ost | 90 | 100 | -10 | Upgrade | 68 | S |
| E30 | A10 | AD Potzdam - AD Nuthetal | 90 | 95 | -5 | Upgrade | 68 | F |
| E31 | A57 | AK Struemp - AK Neuss Sued | 60 | 95 | -35 | Upgrade | 46 | F |
| E31 | A57 | AK Kamp-Lintfort - AK Struemp | 60 | 80 | -20 | Upgrade | 46 | F |
| E31 | A57 | AK Neuss Sued - AK Koeln Nord | 60 | 70 | -10 | Upgrade | 46 | F |
| E331 | A44 | AK Dortmund/Unna - AK Werl | 60 | 65 | -5 | Upgrade | 46 | F |
| E34 | A40 | AK Moers - AK Kaiserberg | 90 | 95 | -5 | Upgrade | 68 | S |
| E34 | A2 | Kamener Kreuz - Oelde | 60 | 65 | -5 | Upgrade | 46 | F |
| E35 | A3 | AK Leverkusen - AD Heumar | 90 | 155 | -65 | Upgrade | 68 | F |
| E35 | A5 | AK Darmstadt - AK Waldorf | 60 | 80 | -20 | Upgrade | 46 | S |
| E35 | A67 | AD Moenchhof - AD Ruesselsheim Ost | 60 | 75 | -15 | Upgrade | 46 | F |
| E35 | A5 | AK Waldorf - AD Karlsruhe | 90 | 100 | -10 | Upgrade | 68 | S |
| E35 | A3 | AK Wiesbaden - AD Moenchhof | 90 | 110 | -20 | Upgrade | 78 | F |
| E37 | A1 | AK Koeln Nord - AK Koeln West | 90 | 110 | -20 | Upgrade | 68 | F |
| E37 | A1 | AK Wuppertal Nord - Wermeskirchen | 60 | 65 | -5 | Upgrade | 46 | F |
| E40 | A4 | AK Koeln Ost - Overath | 60 | 75 | -15 | Upgrade | 46 | S |
| E40 | A4 | AK Aachen - AK Koeln West | 60 | 65 | -5 | Upgrade | 46 | F |
| E40 | B49 | Wetzlar - Gießen | 15 | 40 | -25 | Upgrade | 24 | S |
| E Road | German Motorway No | Section | Capacity [1000 PCU/24 h] | Traffic loading 2005 [1000 PCU/24 h] | Difference | Extent of Action |
|  |  |  |  |  |  | Kind | Number of lanes (actual - objective) | Program |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| E41 | A45 | Westhofener Kreuz - AK Hagen | 60 | 80 | -20 | Upgrade | 56 | F |
| E41 | A81 | AS Boeblingen Ost - AS Herrenberg | 60 | 75 | -15 | Upgrade | 56 | F |
| E45 | A9 | AK Neufahm - AK Muenchen Nord | 90 | 120 | -30 | Upgrade | 68 | F |
| E45 | A7 | AD HH Nordwest - AD HH Suedwest | 90 | 110 | -20 | Upgrade | 68 | F |
| E45 | A99 | AK Muenchen Nord – AK Muenchen Sued | 90 | 110 | -20 | Upgrade | 68 | F |
| E45 | A7 | AD Salzgitter - Friedland | 60 | 70 | -10 | Upgrade | 46 | F |
| E45 | A7 | AD Schweinfurt - AK Biebelried | 60 | 70 | -10 | Upgrade | 46 | S |
| E45 | A9 | AD Holledau - AK Neufahm | 90 | 100 | -10 | Upgrade | 68 | S |
| E45 | A7 | AD Hannover Nord - AD Hannover Sued | 60 | 65 | -5 | Upgrade | 46 | F |
| E451 | A5 | AK Homburg - AK Frankfurt a.M. NW | 30 | 120 | -90 | Upgrade | 68 | F |
| E451 | A5 | AK Gambach - AK Homburg | 90 | 105 | -15 | Upgrade | 68 | F |
| E451 | A67 | AK Darmstadt - AD Viernheim | 90 | 95 | -5 | Upgrade | 68 | F |
| E50 | A6 | AK Viernheim - AK Mannheim | 60 | 75 | -15 | Upgrade | 46 | F |
| E50 | A6 | AS 57 (Schwabach) - AK Nuernberg - Ost | 60 | 75 | -15 | Upgrade | 46 | F |
| E50 | A6 | AD Hockenheim - AK Weinsberg | 60 | 100 | -40 | Upgrade | 46 | F |
| E51 | A9 | AK Nuernberg - AK Nuernberg Ost | 90 | 100 | -10 | Upgrade | 68 | S |
| E52 | A99 | AK Muenchen - Nord - AK Muenchen – Ost | 90 | 120 | -30 | Upgrade | 68 | F |

| E Road | German Motorway No | Section | Capacity [1000 PCU/24 h] | Traffic loading 2005 [1000 PCU/24 h] | Difference | Extent of Action |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Kind | Number of lanes (actual - objective) | Program |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| E52 | A8 | AS Augsburg - West - AS Augsburg – Ost | 60 | 85 | -25 | Upgrade | 46 | F |
| E52 | A99 | AK Muenchen - Ost - AK Muenchen – Sued | 90 | 105 | -15 | Upgrade | 68 | S |
| E52 | A5 | AS Appenweier - AS Baden - Baden | 60 | 65 | -5 | Upgrade | 46 | F |
| E52 | A8 | AD Karlsruhe - AD Leonberg | 60 | 65 | -5 | Upgrade | 46 | F |
| E52 | A8 | AD Leonberg - AS Stuttgart - Degerloch | 90 | 125 | -35 | Upgrade | 78 | S |
| E52 | A8 | AK Muenchen - Sued - AS Holzkirchen | 90 | 100 | -10 | Upgrade | 68 | S |
| E531 | B33 | AS Offenburg - Biberach | 15 | 25 | -10 | Upgrade | 24 | S |
| E533 | B2 | AS Eschenlohe - Kruen | 15 | 25 | -10 | Upgrade | 24 | S |
| E54 | B13 | AS Muenchen - Sendling - AS A95 | 90 | 150 | -60 | Upgrade | 68 | F |
| E54 | B18 | AS Memmingen - AS Stetten | 15 | 25 | -10 | Upgrade | 24 | F |
| E54 | B31 | Ueberlingen - Meersburg | 15 | 20 | -5 | Upgrade | 24 | F |
| E54 | B31 | Meersburg - AS Sigmarszell | 15 | 20 | -5 | Upgrade | 24 | F |
| No upgrade intended |
| E30 | A30 | AK Lotte/Osnabrueck – AK Osnabrueck Sued | 60 | 80 | -20 |  |  |  |
| E30 | A2 | AD Hannover West - AK Hannover Ost | 90 | 105 | -15 |  |  |  |
| E34 | A3 | AK Oberhausen West - AK Oberhausen | 90 | 100 | -10 |  |  |  |
| E34 | A2 | AK Oberhausen - Essen/Gladbeck | 90 | 100 | -10 |  |  |  |
| E35 | A3 | AK Ratingen Ost - AK Hilden | 90 | 135 | -45 |  |  |  |
| E35 | A3 | AK Kaiserberg - AK Breitscheid | 90 | 110 | -20 |  |  |  |
| E35 | A3 | AK Hilden - AK Leverkusen | 90 | 110 | -20 |  |  |  |
| E35 | A3 | AK Oberhausen - AK Oberhausen West | 90 | 105 | -15 |  |  |  |
| E35 | A3 | AK Breitscheid - AK Ratingen Ost | 90 | 105 | -15 |  |  |  |
| E35 | A3 | AK Oberhausen West - AK Kaiserberg | 90 | 100 | -10 |  |  |  |
| E37 | A1 | AK Leverkusen - AK Koeln Nord | 90 | 110 | -20 |  |  |  |
| E37 | A1 | Kamener Kreuz - AK Dortmund/Unna | 90 | 95 | -5 |  |  |  |
| E41 | A81 | AS Ludwigsburg Nord - AS Stuttgart Zuffenhausen | 90 | 120 | -30 |  |  |  |
| E41 | A45 | AK Dortmund NW - AK Dortmund West | 60 | 80 | -20 |  |  |  |
| E41 | A81 | AK Weinsberg - AS Ludwigsburg Nord | 90 | 95 | -5 |  |  |  |
| E41 | A45 | AK Hagen - AS Luedenscheid | 60 | 70 | -10 |  |  |  |
| E41 | A45 | AK Olpe Sued - AS Siegen | 60 | 70 | -10 |  |  |  |
| E41 | A45 | AK Gießen Sued - AK Gambach | 60 | 75 | -15 |  |  |  |
| E45 | A3 | Nuernberg Nord - AK Nuernberg | 90 | 105 | -15 |  |  |  |
| E451 | A5 | AK Frankfurt a.M. NW - AK Frankfurt | 90 | 150 | -60 |  |  |  |
| E451 | A5 | AK Frankfurt - AK Darmstadt | 90 | 120 | -30 |  |  |  |
| E48 | B303 | Troestau - AS Marktredwitz-Nord | 15 | 18 | -3 |  |  |  |
| E52 | A99 | AD Muenchen/Allach - AD Muenchen/Feldmoching | 90 | 100 | -10 |  |  |  |
| E531 | B33 | St.Georgen i.Sch. - AS Donaueschingen | 15 | 20 | -5 |  |  |  |
| E54 | B13 | AS A95 - AS A8 | 90 | 125 | -35 |  |  |  |
| E54 | B34 | AS Lauching - Grenzuebergang | 15 | 20 | -5 |  |  |  |

| Explanations: |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| column 3 | AD/AK | Interchange |  |  |  |  |  |  |
|  | AS | Exit |  |  |  |  |  |  |
| column 7 | Upgrade | Upgrading of existing capacity by adding another lane |  |  |  |  |  |
| column 8 | 24 | Widening from 2 to 4 lanes |  |  |  |  |  |  |
|  | 46 | Widening from 4 to 6 lanes |  |  |  |  |  |  |
|  | 68 | Widening from 6 to 8 lanes |  |  |  |  |  |  |
|  | 78 | Widening from 7 to 8 lanes |  |  |  |  |  |  |
| column 9 | F | First priority project according to the requirement plan for federal trunk roads (started before 2015) |  |  |
|  | S | Second priority project according to the requirement plan for federal trunk roads (after 2015) |  |  |

-----

# Text boxes

TRANS/WP.5/2005/16/Add.5

page 5

TRANS/WP.5/2005/16/Add.5

page 3

TRANS/WP.5/2005/16/Add.5

page 2

TRANS/WP.5/2005/16/Add.5

page 4

TRANS/WP.5/2005/16/Add.5

page 6