| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL TRANS/WP.5/2005/16 7 June 2005 Original: ENGLISH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on Transport Trends and Economics

(Eighteenth session, 15-16 September 2005,

agenda item 2(b))

MONITORING OF DEVELOPMENTS RELEVANT FOR THE PAN-EUROPEAN TRANSPORT CORRIDORS AND AREAS

Infrastructure bottlenecks and missing links

Transmitted by the Governments of Finland, Georgia and Lithuania

FINLAND

Rail bottlenecks in Finland

On the Nordic triangle there are two bottlenecks in the Finnish rail network.

- Section Kerava-Riihimäki

The section is a double track line with mixed traffic. The average number of daily trains in 2003 was 196. Capacity problems exist on weekdays during commuting times. There is a need to increase the number of commuter trains but it cannot be done because the existing infrastructure is in full use (conflict mainly between commuter and long distance passenger trains).

Using the shortcut line Kerava-Lahti in 2006 will partly solve the problem when some of the long distance trains will change their route.

- Section Lahti-Luumäki

This section is also a double track line with mixed traffic. The average number of trains in 2003 was only 65-70 per day but the capacity problem is caused by the alteration of train speeds and unexpected changes in Russian border crossing freight trains. Capacity problems exist mainly during the daytime and partly seasonally.

There is a need to start running fast trains between Helsinki and St. Petersburg (Russian Federation) that is expected to intensify the situation. The Russian side is also extending border crossing freight trains by up to 1,060 metres which will cause extra shunting needs on the Finnish side because of the lack of such long tracks in Finnish yards. At the moment, the needed investments (passing tracks, etc.) are being studied as well as the implementation of PPP-model.

Bottlenecks on Finnish E-roads

Interpreting the word "bottleneck"

"Bottleneck" is a common phrase when referring to shortcomings in the transport system. The definition of the situation behind the word is, however, far from accurate. UNECE documents highlight the difficulties in establishing more clear criteria for bottlenecks.  The item has also been discussed in the relevant organs of the European Commission (DG TREN) and the Commission of European Directors of Roads (CEDR).

Other words used in discussion areas are e.g. "congestion", "lack of capacity" and "deficiency in traffic conditions". How do we understand each expression? Would the grading scale be in connection with the purpose for appraisal? (Daily traffic guidance and information, or needs assessment for major investments.)

In future, there should be more discussion on a European level and harmonization of determinations regarding desired and accepted levels of service in the transport system. The criteria in the questionnaire (and the background paper from 1994) are quite vague and might give too many bottlenecks, provided that bottlenecks are understood as congestions the drivers would like to avoid even when it meant taking a somewhat longer route.

The Finnish answer to the questionnaire (roads) is based on discussions and studies in a working group under CEDR. The theory is briefly described below.

Some theory of capacity related problems - one suggested determination

Once the full capacity of a section of road has been reached, the continuous flow of traffic changes into the "Stop-and-Go" phase and eventually comes to a complete standstill. Over a period of time, this means that vehicles increasingly become a hindrance to each other and the drivers' ability to select their driving speed is limited. These stages of congestion occur with varying regularity and for different lengths of time. The degree of congestion is usually perceived very differently by road users and is always compared with the reference situation of "free-flowing traffic". The loss of time involved is usually considered more serious than can actually be proven.

There is no uniform, generally accepted definition of bottlenecks. It is agreed, however, that bottlenecks are a consequence of some form of congestion, but the definition of the exact traffic conditions involved in traffic congestion has not yet been agreed.

Several factors may cause congestion on the road network. Some are caused by exceptional factors that may be unpredictable. This kind of temporary congestion normally dissolves itself after a short period of time.

Regular congestion refers to capacity-related traffic jams which come about if the traffic demand exceeds - usually temporarily, but regularly - the capacity of a section of road. In principle, this sort of congestion cannot and will not be completely avoided in the future without adding capacity or changing the traffic routes.

The theoretical basis for the identification and evaluation of congestion is the relationship between traffic flow (veh/h) and average speed (km/h) in a cross-section. Once being determined (i.e. measured) for a specific type of road and cross-section, the Flow-Speed-curve can be used to derive reliable information about the quality level of the traffic flow from actual speed data measured later. The relationship between traffic flow and average speed indicates the point at which the traffic flow becomes unstable or comes to a complete standstill.

On motorways, congestion generally occurs when traffic exceeds approximately 1,800 veh/h per lane (urban sections) and 1,900 veh/h per lane (rural sections). The speed of traffic flow drops under 75 km/h.

For 2-lane roads, the driving pattern is different from that of motorways. Overtaking may become difficult even with a rather limited amount of traffic. The indicators can be maximum traffic flow and average speed at maximum flow.

It is important to note, that congestion on 2-lane roads can be caused by many other reasons than traffic flow due to the characteristics of 2-lane roads. The speed first only diminishes slowly as traffic flow builds up. Suggested criteria could be that congestion occurs if the speed falls below 75% of the speed under free flow conditions for 2-lane roads. In Finnish experience the capacity of 2-lane roads is about 1,800-2,100 veh/hour in both directions together. The share of directions could be 30/70.

If, for a specific road section, congestion events over a year exceed a certain determined number of hours per year, the section may be called a bottleneck. One suggested determination for "bottleneck” is a section where the speed of vehicles falls below the threshold value for more than 200 hours per year.

Bottlenecks on the Finnish E-roads

Finland is lucky to have overall moderate traffic volumes on the main road network. Tourist traffic is not a special problem. Most heavy peak hours on roads near urban areas occur when people are travelling to and from work and, in summer rural areas, during weekends when people visit their summer cottages in southern and central Finland.

The length of the E-road network is 4260 km. The network is managed for the Government by the Finnish Road Administration; in addition to this there are some 25 km city streets on E-routes to centres and harbours in Helsinki, Turku and Vaasa.

The E-road network (State owned) consists of:

-	670 km motorway or other 2+2 -lane road

-	3,590 km 2-lane road

No 3-lane roads exist, only extra lanes with limited length for overtaking.

Motorways or other 2 + 2 -roads seldom have bottlenecks. In the Helsinki area only 35 km of these have more than 40,000 veh/day, but less than 60,000 veh/day. The only section worth mentioning is on E18 the Helsinki Ring near the airport, but even there measures alleviating the bottleneck problem will be ready this year (grade separation for at-grade junctions, extra lanes for public transport). There is, however, still some work left for the future.

On a suburban ring road, the daily variation of traffic is quite "flat". On the Helsinki ring the ADT is 54,0000 veh/day. The 200th peak hour in one direction is 5% = 2,700 veh/h, which is quite well managed by a 2-lane carriageway if no at-grade junctions exist.

On 2-lane roads there are, or will become some congestion problems. The lower value in the questionnaire, 8,000 veh/day, seems however not to establish any bottlenecks worth mentioning. Although shoulders on Finnish roads are narrow, the road geometry is mainly good and road side land use on rural sections sparse.

About 230 km of 2-lane roads have traffic of more than 10,000 veh/day. A more regular congestion/lowered speed with slightly over 10,000 volumes may result only if the 200th peak hour is more than 11-12% of ADT and the road geometry is not very good.

When planning programmes for capacity measures on the road network, ADT 8000-12,000 veh/day is a relevant indicator. For daily traffic management and the so-called "regular bottleneck" the ADT should be over 12,000 veh/day unless there are no other causes jamming the traffic. About 125 km of 2-lane E-roads in Finland have traffic of at least 12,000 veh/day. The main objects with experienced problems are:

-	E12 Tampere ring road

-	E18 Turku - Helsinki, middle section Muurla-Lohja

-	E18 Hamina, partly city street.

See more details in the summary table, where these objects are collected under the title "clear bottlenecks today".

Sections with upgrading work taking place this year are excluded.

Even on the following 2-lane sections the ADT is over 12,000. They are close to regional centres with a "flatter" daily traffic curve. The bottlenecks have not yet experienced very tight or longer times. Short congestion peaks appear mostly when going to work before 8 a.m. and going home after 4 p.m. (especially on Fridays in summertime when people go to their summer cottages). In the table, these are under the title "shorter/lighter bottlenecks".

-	E08 north of Turku (Raisio-Masku)

-	E08 north of Pori

-	E08 through Vaasa (Sepänkylä)

-	E63 shortly after Tampere

-	E75 south of Jyväskylä (Vaajakoski)

-	E75 north of Jyväskylä (Tikkakoski).

On the E18 border crossing towards the Russian Federation (Vaalimaa) there is a real bottleneck at least for heavy traffic. It may take hours to cross the border. This depends, however, on border control processes not on road traffic arrangements.  Street connections to Helsinki and Turku/Naantali harbours may also be felt as bottlenecks, but they are not analysed here. (See  "bottleneck on border" in the table.)

In the completed questionnaire table, the column "capacity" refers, on the one hand, to maximum capacity per hour; it depends a.o. the road geometry and density of accessing roads. On the other hand, it is referred to as the threshold value of flowing daily traffic; it depends also on the traffic pattern and known variations at each section.

General questions

As already mentioned, motorways and other 2 -carriageway roads with grade separated interchanges do not establish bottlenecks in Finland. Possible problems close urban areas are/will be solved by extra lanes.

On 2-lane roads the main strategy is to upgrade some roads to motorway or other 2 x 2 -standards. In many cases, problems will be alleviated by adding passing lanes, restriction of minor access roads and some upgrading of road geometry.

In some temporary cases, guiding/recommendation to other routes can be used. No road tolls have been planned. It was not considered necessary to restrict heavy vehicles at certain times.

| State | Mode of transport | Route | Section | Traffic loading | Capacity | Extent of action | Operational by year |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Subject | Kind |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| FINLAND | ROAD TRANSPORT | A. Clear bottlenecks today: |  |  |  |  |  |
|  |  | E 12 | Tampere ring (western by-pass) | 10,000-22,000 veh/day (2-lane road) | 2,100 veh/h 16,000/day | Upgrading to 2 x 2 motorway | 21 km | 2011 |
|  |  | E 18 | Turku-Helsinki, part Muurla-Lohja | 10,500-12,300 veh/day (2-lane road) | 1,800 veh/h 12,000/day | Substituting by new 2 x 2 motorway | 60 km | 2009 |
|  |  |  | Helsinki-Russian border, City of Hamina | 12,000-13,000 veh/day (2-lane road, partly street) | 1,200 veh/h 12 000/day | New by-pass, 2 x 2 motorway | 15 km | 2012 |
|  |  | B. Shorter/lighter bottlenecks: |  |  |  |  |  |
|  |  | E 08 | Turku-Pori, part Raisio-Masku | 12,000-14,000 veh/day (2-lane road) | 2,000 veh/h 13,000/day) | Upgrading to 2 x 2 road | 7 km | > 2010 |
|  |  |  | Pori-Vaasa, nort of Pori | 13,000 veh/day (2-lane road) | 2,100 veh/h 13,000/day | New 2-lane road for trunk traffic | 4 km | > 2010 |
|  |  |  | Vaasa-Oulu north of Vaasa | 15,000 veh/day (2-lane road, traffic lights) | 2,100 veh/h 14,000/day | New by-pass of Sepänkylä | 7 km | 2010 |
|  |  | E 63 | Tampere-Jyväskylä east of Tampere | 13,000-18,000 veh/day (2-lane road) | 2,100 veh/h 14,000/day | Upgrading to 2 x 2 road | 8 km | >2010 |
|  |  | E 75 | Lahti-Jyväskylä south of Vaajakoski | 17,000 veh/day (2-lane road) | 2,000 veh/h 14,000/day | Upgrading to motorway | 3 km | >2010 |
|  |  |  | Jyväskylä-Oulu north of Jyväskylä | 13,000 veh/day (2-lane road) | 2,100 veh/h 13,000/day | Upgrading to 2 x 2 road | 9 km | >2010 |
|  |  | C. Bottleneck on border: |  |  |  |  |  |
|  |  | E 18 | Helsinki-Russian border, Vaalimaa border station | 3,100 veh/day, of which 800 heavy veh | Heavy veh may delay >24 h | Problem is the control procedure. No solution by road investments. |  |  |

| State | Mode of transport | Route | Section | Traffic loading | Capacity | Extent of action | Operational by year |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Subject | Kind |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| FINLAND | INLAND WATERWAYS | E60-11 | The Saimaa Canal/Vyborg – Mälkiä Lock | 2.4 million tons/year |  | Restrictions in the use occur. Canal is closed during mid-winter. | Ice hinders traffic on the canal. | Prolonging of the traffic season is under examination. Decision of the realization has not been made yet. |
|  |  |  | Mälkiä Lock – Kuopio/Straight of Kyrönsalmi in the city of Savonlinna | Approx. 1.5 million tons/year |  | Limited cross-section of the fairway section. | The fairways section does not meet needs of the traffic and the standards. This creates a safety hazard and causes delays to the traffic. | Plans are ready. Decision of the realisation has not been made yet. |

GEORGIA

Intensity of road usage has recently increased in Georgia, leading to traffic congestion on some sectors of the road network of international importance. These sectors are:

- Tbilisi-Khashuri, Zestafoni-Samtredia and Kobuleti-Sarpi of Tbilisi-Poti-Sarpi- Border of Turkey, and

- Tbilisi-Marneuli of Tbilisi-Marneuli-Guguti- Border of Armenia.

Traffic intensity on these sectors at an overnight range is up to 5,000 – 15,000.  Further increases in intensity are foreseen, and road capacity will not be able to meet the capacity of traffic.

Rehabilitation of the above-mentioned road sectors will be financed from the State budget in the near future within existing parameters only. Up to US$ 350 million of investments is required for modernization of these motorways in order to meet growth of traffic volume.

| State | Mode of transport | Route | Section | Traffic loading | Capacity | Extent of action | Operational by year |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Subject | Kind | Finance |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| LITHUANIA | ROAD TRANSPORT | IXB Corridor | Southern by-pass of Vilnius between E85 and E28 | E85 – 25000 E28 – 6500 | 15,000 | Construction of southern by-pass steering aside transit transport | Construction of road 25 km. | €49.2 million | 2010 |
|  |  | A12 (IA Corridor) | Riga–Kaliningrad 180.5 – 187.9 km. | 1,800 | 1,500 | Construction of eastern by-pass of Panemunė | Construction of road with the bridge over the Nemunas river 7.40 km. | €7.2 million | 2010 |
|  |  | A12 (IA Corridor) | Riga – Kaliningrad | 3,800 | 4,000 | Construction of by-pass | Construction of road 18.50 km. | €11.6 million | 2015 |
|  |  | A6 E262 | Kaunas – Zarasai – Daugpils | 5,000 | 4,000 | Construction of Jonava by-pass | Construction of road 13 km. | €8.1 million | 2009 |
|  |  | A6 E262 | Kaunas–Zarasai – Daugpils | 3,800 | 4,000 | Construction of Ukmergė by-pass | Construction of road 8 km. | €5.8 million | 2015 |
|  |  | A6 E262 | Kaunas–Zarasai – Daugpils | 3,000 | 4,000 | Construction of Utena northern by-pass | Construction of road 9 km. | €5.8 million | 2015 |
|  |  | A6 E262 | Kaunas–Zarasai – Daugpils | 1,000 | 1,500 | Construction of Zarasai southern by-pass | Construction of road 7.55 km. | €4.3 million | 2010 |
|  |  | A9 E272 | Panevėžys – Šiauliai | 8,000 | 7,000 | Reconstruction into I category | Construction of second road lane 15.90 km. | €4.3 million | 2009 |
|  |  | A7 E28 (IXD Corridor) | Marijampolė – Kybartai | 1,000 | 1,500 | Construction of Virbalis and Kybartai | Construction of road 10 km. | €9.3 million | 2010 |

| State | Mode of transport | Route | Section | Traffic loading | Capacity | Extent of action | Operational by year |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Subject | Kind | Finance |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| LITHUANIA | RAILWAYS | Corridor IX B | Vilnius – Kaišiadorys | 93 trains/day | 95 +31/51 + 31 | Modernization of the tele-communications, increasing of traffic loading to 115 trains/day | Fibred optical cable system, Transmission system based on SDH including network synchronizations, Telecommunication network management system, PBX’s in a network, telephones and subscribes connection. | €1.6 million | 2002- 2004 |
|  |  |  | Radviliškis – Šiauliai | 64 trains/day | 350 +13/172 + 13 | Modernization of the tele-communications, increasing of traffic loading to 78 trains/day | Fibred optical cable system, Transmission system based on SDH including network synchronizations, Telecommunication network management system, PBX’s in a network, telephones and subscribes connection. |  |  |
|  |  |  | Šiauliai – Klaipeda | 42 trains/day | 21 +6/21 + 6 | Modernization of the tele-communications, increasing of traffic loading to 51 trains/day | Fibred optical cable system, Transmission system based on SDH including network synchronizations, Telecommunication network management system, PBX’s in a network, telephones and subscribes connection. |  |  |
|  |  |  | Šiauliai – Klaipeda | 42 trains/day | 21 +6/21 + 6 | Modernization of Signalling and Power supply, increasing of traffic loading to 51 trains/day | Design, manufacture, installation and commissioning. Will be required to perform all works included in Tender Dossier in connection with modernization of signalling, power supply and telecommunications systems on section. Modern technologies are to be used while implementing the project and the compatibility between existing and new systems is to be ensured including all safety aspects and compliance with requirements for ISPA financed projects. | €28.5 million | 2004- 2006 |

| State | Mode of transport | Route | Section | Traffic loading | Capacity | Extent of action | Operational by year |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Subject | Kind | Finance |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| LITHUANIA | RAILWAYS | Corridor IX B | Kaišiadorys - Radviliškis | 37 trains/day | 31 + 9/31 + 9 | Modernization of power supply, increasing of traffic loading to 45 trains/day | Renovation of 135 km 10/0.4 kV power supplies line. The works also include renovation and installation of 15 diesel power stations, renovation and installation of 29 transformers, construction and installation of one new masonry power station building. All 10kV switchgear and 0.4kV switchboards at the stations shall be replaced with modern equipment using vacuum breaker types in the 10kV switchgear and circuit breakers in the low voltage switchboards to reduce the need for fuses. |  |  |
|  |  |  | Kaišiadorys – Klaipeda | 44 trains/day | 21 + 6/21 + 6 | Elimination of crossings (road overpasses building, increase in traffic loading to 54 trains/day | Elimination of crossings (road overpasses building | €104 million | 2010- 2015 |
|  |  |  | Kaišiadorys –Šiauliai | 49 trains/day | 31 + 9/31 + 9 | Tracks modernization for speed up to 160 km/h, increase in traffic loading to 56 trains/day | Tracks modernization for speed up to 160 km/h | €108 million | 2009- 2015 |

| State | Mode of transport | Route | Section | Traffic loading | Capacity | Extent of action | Operational by year |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Subject | Kind | Finance |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| LITHUANIA | RAILWAYS | Corridor IX B | Kaišiadorys – Radviliškis Palemonas - Gaižiūnai | 37 trains/day 8 trains/day | 31 + 9/31 + 9 26 + 4/26 + 4 | Electrification of sections, increase in traffic loading to 45 trains/day Electrification of sections, increasing in traffic loading to 10 trains/day | Electrification of sections | €70 million | 2010- 2015 |
|  |  |  | Radviliškis – Klaipeda | 48 trains/day | 31 + 9/31 + 9 | Electrification of section, increase in traffic loading to 58 trains/day | Electrification of sections | €77 million | 2010- 2015 |
|  |  | Corridor IX D | Kaišiadorys – Kybartai | 50 trains/day | 27 + 8/27 + 8 | Modernization of Tele-communications, increase in traffic loading to 62 trains/day | Fibred optical cable system, Transmission system based on SDH including network synchronization, Telecommunication network management system, PBX’s in a network, telephones and subscribes connection. | €3.08 million | 2005- 2006 |
|  |  |  | Vilnius – Kybartai | 65 trains/day | 27 + 8/27 + 8 | Elimination of crossings (road overpasses building), increase in traffic loading to 82 trains/day | Elimination of crossings (road overpasses building) | €50 million | 2005- 2008 |

| State | Mode of transport | Route | Section | Traffic loading | Capacity | Extent of action | Operational by year |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Subject | Kind | Finance |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| LITHUANIA | RAILWAYS | Corridor IX D | Kena – Kybartai | 64 trains/day | 27 + 8/27 + 8 | Tracks modernization for speed up to 160 km/h, Increase in traffic loading to 79 trains/day | Tracks modernization for speed up to 160 km/h | €89.7 million | 2005- 2008 |
|  |  | Corridor IXB IXD | Kena – Kybartai, Radviliškis - Šiauliai | 64 trains/day 64 trains/day | 27 + 8/27 + 8 350 + 13/172 + 13 | Modernization of Signalling and Power supply, Increase in traffic loading to 79 trains/day Modernization of signalling and power supply, Increase in traffic loading to 78 trains/day | Modernization of signalling and power supply | €81 million | 2006- 2008 |
|  |  |  |  | 59 trains/day 50 trains/day |  | Extension of tracks length up to 1,050 m, Increase in traffic loading to 73 trains/day on Corridor IXB, 62 trains/day on Corridor IXD | Extension of tracks length up to 1,050 m | €25 million | 2005- 2006 |

| State | Mode of transport | Route | Section | Traffic loading | Capacity | Extent of action | Operational by year |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Subject | Kind | Finance |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| LITHUANIA | RAILWAYS | Corridor IX B IX D E – 75 (I) |  | 59 trains/day 50 trains/day 27 trains/day |  | Modernization of radio system, Increase in traffic loading to 73 trains/day on Corridor IXB, 62 trains/day on Corridor IXD, 34 trains/day on Corridor E-75(I) | Modernization of radio system | €52 million | 2005- 2008 |
|  |  |  |  |  |  | Hot boxes axles detector modernization, increase in traffic loading to 73 trains/day on Corridor IXB, 62 trains/day on Corridor IXD, 34 trains/day on Corridor E-75(I) | Hot boxes axles detector modernization | €12 million | 2004- 2006 |
|  |  | Corridor (Rail Baltica) | State border with Poland - Kaunas |  |  | Construction of new standard gauge | Construction of new standard gauge | €300 million | After 2010 |
|  |  | Corridor (Rail Baltica) | Kaunas – state border with Latvia |  |  | Construction of new standard gauge | Construction of new standard gauge | €500 million | After 2014 |

| State | Mode of transport | Route | Section | Traffic loading | Capacity | Extent of action | Operational by year |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Subject | Kind | Finance |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| LITHUANIA | RAILWAYS | Other lines | Stasylos – Vilnius Kužiai – Mažeikiai Klaipėda – Pagėgiai | 15 trains/day 19 trains/day 8 trains/day | 33 + 6/33 + 6 24 + 2/24 + 2 15 + 2/15 + 2 | Infrastructure renovation of main tracks links, Increase in traffic loading to 18 trains/day Infrastructures renovation of main tracks links, Increase in traffic loading to 23 trains/day Infrastructures renovation of main tracks links, Increase in traffic loading to 10 trains/day | Infrastructures renovation of main tracks links | €109 million | 2004- 2006 |
|  |  |  | Kaunas station | 45 trains/day | 97 + 21/134+ 21 | Reconstruction of Kaunas tunnel, Increase in traffic loading to 56 trains/day | Reconstruction of Kaunas tunnel (1.3 km length) | €3.2 million | 2004- 2005 |
|  |  |  | Kena station | 64 trains/day | 127 + 18/ 127 + 18 | Reconstruction of Kena border station | Reconstruction of Kena border station | €41 million | 1999- 2006 |
|  |  |  | Klaipėda node | 43 trains/day (Klaipėda station) | 76/76 (Klaipėda station) | Development of Klaipeda railway node | Development of Klaipeda railway node | €9 million | 2005- 2006 |
|  |  |  | Vilnius node | 140 trains/day (Vilnius station) | 152/173 (Vilnius station) | Development of Vilnius node | Development of Vilnius node | €11 million | 2004- 2006 |

Note : Line capacity breakdown:  odd freight trains plus passenger trains/even freight trains plus passenger trains

| State | Mode of transport | Route | Section | Traffic loading | Capacity | Extent of action | Operational by year |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Subject | Kind | Finance |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| LITHUANIA | INLAND WATERWAY TRANSPORT | E 41 Klaipėda – Curonian Lagoon-river Nemunas-Kaunas (277.9 km) | Klaipėda -Jurbarkas | _ | Boat’s draught-1.5m; width– 0 m, length-100 m | Navigation improvement through deepening and subsequent regulation, equalization of depth to 1.5 m. | – | approx. €22.6 million | 2005–2014 |
|  |  |  | Jurbarkas - Kaunas | – | Boat’s draught – 1.2 m; width – 8 m, length -100 m |  |  |  |  |

---------

# Text boxes

TRANS/WP.5/2005/16

page 12

TRANS/WP.5/2005/16
page 14

TRANS/WP.5/2005/16

page 14

TRANS/WP.5/2005/16

page 15

TRANS/WP.5/2005/16

page 16

TRANS/WP.5/2005/16

page 17

TRANS/WP.5/2005/16

page 8

Note:  The tables on the following pages will be in English only.

TRANS/WP.5/2005/16

page 13

TRANS/W.5/2005/16

page 7

TRANS/WP.5/2005/16

page 11

TRANS/WP.5/2005/16

page 10