#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2006/29

7 April 2006

Original: ENGLISH

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

## HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Twenty-ninth session

# Geneva, 3-12 (a.m.) July 2006

# Item 2 of the provisional agenda

TRANSPORT OF EXPLOSIVES

Carriage of signals and flares in Divisions 1.4G and 1.4S

Transmitted by the expert from the United Kingdom

Background

- The expert from the United Kingdom notes that the Dangerous Goods list, Chapter 3.2, has entries for the following signals and flares in Divisions 1.3G and 1.4G:

|  | 1.3G | 1.4G | 1.4S |
| --- | --- | --- | --- |
| Cartridges, signal | 0054 | 0312 | 0405 |
| Signal devices, hand | - | 0191 | 0373 |
| Signals, distress, ship | 0195 | - | - |
| Signals, smoke | 0487 | 0197 | - |
| Flares, aerial | 0093 | 0403 | 0404 |

However he has received a number of applications for approval of classifications for marine distress signals under UN 0432 1.4S "ARTICLES PYROTECHNIC, for technical purposes". An explanation of "ARTICLES PYROTECHNIC" is included in the glossary of terms in the Appendix but signals and flares listed in the above table are specifically excluded from this name and description.

- The requirements of 2.1.3.4.1 states Test Series 6 be used for the assignment of substances and articles to Divisions 1.1, 1.2, 1.3 and 1.4. Recent changes to the packaging for a number of signals, distress and smoke, has resulted in assignments of 1.4G and 1.4S in Test 6(c). Currently, there are no entries for "SIGNALS, smoke" in Division 1.4S, or 1.4G and 1.4S for "signals distress, ship" in the Dangerous Goods List.

Proposal

3.	To include the following entries into the Dangerous Goods List, in Chapter 3.2, to allow the transport of marine distress signals based on UN test results.

| UN No. | Name and description | Class or Division |  |  |  | Limited quantities | Packing Instruction |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) |
| 0xxx | Signals distress, ship | 1.4G |  |  |  | NONE | P135 |
| 0xxx | Signals distress, ship | 1.4S |  |  |  | NONE | P135 |
| 0xxx | Signals, smoke | 1.4S |  |  |  | NONE | P135 |

______________

# Text boxes

STSTE

Secretariat