#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2006/39

11 April 2006

Original: ENGLISH

## COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Twenty-ninth session

# Geneva, 3-12 (a.m.) July 2006

# Item 3 of the provisional agenda

TRANSPORT OF GASES

P200 Special Provision “d”

Transmitted by the expert from the United States of America

Introduction

1.	Special provision “d” of P200 specifies that when steel UN pressure receptacles are used, only those bearing an “H" mark are authorized.   The “H” mark signifies that the cylinders have been protected against hydrogen embrittlement.  However, special provision “d” is currently unnecessarily applied to Arsine, Germane, Phosphine, and Silane.  None of these gases are prone to hydrogen disassociating from the compounds and therefore no protection against hydrogen embrittlement is necessary.

Proposal

2.	In the special packing provision column of Packing Instruction P200, delete all references to special provision “d” from the entries for Arsine (UN2188), Germane (UN2192), Phosphine (UN2199), and Silane (UN2203).

______________

# Text boxes

STSTE

Secretariat