#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2006/68

1 September 2006

Original: ENGLISH

## COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirtieth session

# Geneva, 4-12 (a.m.) December 2006

# Item 2(c) of the provisional agenda

PROPOSALS OF AMENDMENTS TO THE RECOMMENDATIONS

ON THE TRANSPORT OF DANGEROUS GOODS

Provisions concerning radioactive material

Marking for carriage of radioactive material under "exclusive use"

Transmitted by the expert from Austria

Discussion

- The wording of the provision in 5.3.2.1.1 (e) regarding display of the UN number for carriage of radioactive material under "exclusive use" is not entirely clear and differs from the wording in 5.4.1.5.7.1 (i) requiring the relevant statement in the transport document:

- The current texts read as follows (differences highlighted):

5.3.2.1.1

(…. the UN number shall be displayed as required by this section on consignments of:)

…

- Packaged radioactive material with a single UN number under exclusive use in or on a vehicle, or in a freight container.

5.4.1.5.7.1

(The following information shall be included for each consignment of Class 7 material, as applicable, in the order given:)

- Where a consignment is required to be shipped under exclusive use, the statement “EXCLUSIVE USE SHIPMENT”;

- Monitoring the proper display of the UN-number is simple where the statement “EXCLUSIVE USE SHIPMENT” has to figure in the transport document whereas in all other cases it is very difficult and not likely that this was intended.

- Therefore the text in 5.3.2.1.1 (e) should be aligned to the wording in 5.4.1.5.7.1. (i).

IAEA aspects

- The corresponding provisions in IAEA TS-R1 are as follows:

548.

Where the consignment in the freight container or tank is unpackaged LSA-I or SCO-I or where an exclusive use consignment in a freight container is packaged radioactive material with a single United Nations number, the appropriate United Nations number for the consignment (see Table 8) shall also be displayed, ….

550.

(The consignor shall include in the transport documents with each consignment the identification of the consignor and consignee, including their names and addresses and the following information, as applicable in the order given:)

- Where a consignment is required to be shipped under exclusive use, the statement “EXCLUSIVE USE SHIPMENT”;

  - In the strict sense the term “exclusive use consignment” is not correct since exclusive use according to the definition does not regard the consignment but the conveyance or freight container wherein the consignment is carried. Therefore it is almost certain that the IAEA provision in 548 meant a consignment requiring exclusive use. Moreover there is the clear wording for the transport document in 550 (l).

  - In view of the text in the IAEA provision 550 (l) and the apparent meaning of the IAEA provision 548 there seems to be no need to wait for a change in the wording of the IAEA provisions and the text in the UN Model regulations should be changed anyway.

Proposal

  - 5.3.2.1.1 (e) shall read as follows (change underlined):

- Packaged radioactive material with a single UN number required to be shipped under exclusive use in or on a vehicle, or in a freight container.

____________________

# Text boxes

STSTE

Secretariat