| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/103 12 July 2006 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-fortieth session

Geneva, 14-17 November 2006

Item 4.2.36. of the provisional agenda

PROPOSAL FOR CORRIGENDUM 1 TO THE 01 SERIES OF AMENDMENTS

TO REGULATION No. 66

(Strength of superstructure)

Submitted by the Working Party on General Safety Provisions (GRSG)

Note:	The text reproduced below was adopted by GRSG at its ninetieth session. It is based on document ECE/TRANS/WP.29/GRSG/2006/17, adopted as reproduced in para. 5 of the report. It is submitted to WP.29 and to AC.1 for consideration (ECE/TRANS/WP.29/GRSG/69, para. 5).

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Paragraph 3.2.2.1., correct to read:

" ….

Mt	=	Mk + k · Mm, where k = 0.5 and Mm is the total mass of the restrained occupants (see paragraph 2.15.).

…. "

- - - - -