| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/107 14 July 2006 Original: ENGLISH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-fortieth session

Geneva, 14-17 November 2006

Item 4.2.49. of the provisional agenda

PROPOSAL FOR SUPPLEMENT 1 TO THE 02 SERIES OF AMENDMENTS TO REGULATION No. 107

(M2 and M3 vehicles)

Submitted by the Working Party on General Safety Provisions (GRSG)

Note:	The text reproduced below was adopted by GRSG at its ninetieth session. It is based on document ECE/TRANS/WP.29/GRSG/2006/5, as amended by Annex 2 to the report. It is submitted to WP.29 and to AC.1 for consideration (ECE/TRANS/WP.29/GRSG/69, para. 10).

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Paragraph 2.1.4., replace "Low floor bus" by "Low floor vehicle".

Insert a new paragraph 2.1.9., including a reference to a new footnote 2/ and the corresponding footnote 2/, to read :

"2.1.9.		"Vehicle without roof" 2/ means a vehicle without roof over all or part of its deck.  		In the case of a double-decked vehicle this shall be the upper deck.  Space for 		standing passengers shall not be provided on any deck without roof, 	independently of the class of vehicle.

__________________

2/	The use of these vehicles may be subject to rules established by National Administrations."

Paragraph 2.15.2., amend to read:

"2.15.2.	the space above the surface of any step or staircase (except where the surface of the 		step is contiguous with that of a gangway or access passageway), or"

Paragraph 2.16., amend to read:

"2.16.		"Access passage" means the space extending inwards into the vehicle from the 		service door up to the outermost edge of the upper step (edge of the gangway), 		intercommunication staircase or half-staircase.  Where there is no step at the door, 		the space to be considered as access passage shall be that which is measured 		according to Annex 3, paragraph 7.7.1. up to a distance of  300 mm from the 		starting position of the inner face of the test gauge."

Paragraph 4.4.1. the reference to footnote 2/ and footnote 2/, renumber as footnote 3/ and amend to read:

__________________

"3/	…. 49 for Cyprus, 50 for Malta, 51 for the Republic of Korea, 52 for Malaysia and 53 for Thailand.  Subsequent numbers shall be assigned .... "

Annex 3,

Insert a new paragraph 7.1.3., to read:

"7.1.3.		If the driver's compartment is without a roof, the driver should have some special 		protection against strong wind, sudden dust, heavy rain, etc."

Paragraph 7.2.2.2.5., amend to read:

"7.2.2.2.5.	the area 300 mm in front of all seats other than folding seats, except in the case of 		a sideways-facing seat, in which case this dimension may be reduced to 225 mm.  		In the case of variable seating arrangements, of any seat when considered to be in 		use, see paragraph 7.2.2.4."

Paragraph 7.2.3.2., amend to read:

"7.2.3.2.	(Reserved)."

Paragraph 7.6.1.5., amend to read:

"7.6.1.5.	Each rigid section of an articulated vehicle shall be treated as a separate vehicle 		for the purpose of determining the minimum number and the position of exits.  		The connecting passage between them shall not be considered as an exit.  Toilet 		compartments or galleys are not considered to be separate compartments for the 		purposes of defining the number of emergency exits.  The number of passengers 		shall  be  determined for  each rigid section.  The plane, which contains the		horizontal axis of the hinge between conjoined rigid sections of the vehicle, and 		perpendicular to the longitudinal axis of a vehicle, when it moves straight, shall 		be considered as the border between sections."

## Paragraph 7.6.1.7.2., amend to read:

"7.6.1.7.2.	One or two seats are permitted alongside the driver for additional people, in 		which case both of the exits referred to in paragraph 7.6.1.7.1. shall be doors.

The driver's door shall be accepted as the emergency door for the occupants of 		those seats, provided that it is possible to move a test gauge from the occupants' 		seats to  the exterior of  the vehicle through the driver's door (see Annex 4, 		figure 27).

Verification of the access to the driver's door shall be subject to the requirements 		of  paragraph  7.7.3.2.,  by using  the  test  gauge  having  a  dimension  of         	600 x 400 mm, as described in paragraph 7.7.3.3.

The door provided for the passengers shall be in the side of the vehicle opposite to 		that containing the driver's door and shall be accepted as the emergency door for 		the driver.

Up to five additional seats may be fitted in a compartment incorporating the 		driver's compartment, provided that the additional seats and the space for these 		seats comply with all requirements of this Regulation and at least one door giving 		access to the passenger compartment complies with the requirements of 	paragraph 7.6.3. for emergency doors."

### Paragraphs 7.6.1.9.1. and 7.6.1.9.2., amend to read:

"7.6.1.9.1.	it satisfies the requirements relating to the dimensions of emergency door indicated 		in paragraph 7.6.3.1.;

7.6.1.9.2.	it fulfils the requirements indicated in paragraph 7.6.1.7.2.;"

Insert a new paragraph 7.6.1.9.3., to read:

"7.6.1.9.3.	the space reserved for the driver's seat shall communicate with the main 	passengers' compartment through an appropriate passage; such requirement shall 	be deemed to be fulfilled if the test gauge described in paragraph 7.7.5.1. can 	move unobstructed from the gangway, until the front end of the gauge reaches the 	vertical plane tangential to the foremost point of the driver's seat back (this seat 	being situated in its rearmost longitudinal position) and, from this plane, the panel 	described in paragraph 7.6.1.7.2. could be moved to the emergency door in the 	direction established by such paragraph (see Annex 4, figure 28) with seat and 	steering wheel adjustment in their mid position."

Insert a new paragraph 7.6.1.15., to read:

"7.6.1.15.	In the case of a vehicle without a roof, the exits on the deck without a roof shall 		be such as to fulfil those prescriptions that are not incompatible with the absence 		of the roof."

Paragraph 7.6.2.1., amend to read (including new subparagraphs 7.6.2.1.1. to 7.6.2.1.4.):

"7.6.2.1.	.... half of the vehicle.  This does not preclude:

7.6.2.1.1.	the provision of a specially designed door in the rear or side faces of a vehicle for 		use in place of a service door by wheelchair passengers, or

7.6.2.1.2.	the provision of an additional service door in the rear face of a vehicle principally 		for loading/unloading of goods or luggage, but which could be used by passengers 		where circumstances so require, or

7.6.2.1.3.	the provision of one or more additional service doors on the opposite side of the 		vehicles in the case of vehicles designed for use in circumstances which require 		loading/unloading on both sides.  Examples of such circumstances include 		vehicles for airside use at airports, vehicles for use on multimodal transport 		systems using island platforms, or vehicles which cross borders to countries 		which do not drive on the same side of the road as the country in which the 		vehicle is to be licensed for operation.  Vehicles so equipped shall be provided 		with control(s) which allow the driver to inhibit normal operation of the doors 		which are not currently in use, or

7.6.2.1.4.	the provision of a service door in the rear face of a Class A or B vehicle."

Paragraph 7.6.2.3., amend to read:

"7.6.2.3.	.... of the vehicle is substantially the same.  (This shall not imply the need to 		provide additional exits over and above the number specified in paragraph 7.6.1.)."

Paragraph 7.6.2.4., amend to read:

"7.6.2.4.	At least one exit shall be situated either …. "

Paragraph 7.6.3.1., amend to read:

"7.6.3.1.	Vehicles of Class I, II or III shall meet the following requirements:

7.6.3.1.1.	A service door shall have an aperture creating an access in accordance with the 		requirements shown in paragraph 7.7.1. of this annex.

7.6.3.1.2.	An emergency door shall have a door aperture with a minimum height 	of 1,250 mm and a minimum width of 550 mm.

7.6.3.1.3.	An emergency window shall have a minimum area of 400,000 mm2.  It shall be 		possible to inscribe in this area a rectangle measuring 500 mm x 700 mm.

7.6.3.1.4.	In the case of an emergency window situated in the rear face of the vehicle, either 		it shall meet the requirements shown in paragraph 7.6.3.1.3., or it shall be possible 		to inscribe in the aperture of this emergency window a rectangle 350 mm high 		and 1,550 mm wide, the corners of which may be rounded to a radius of curvature 		not exceeding 250 mm.

7.6.3.1.5.	An escape hatch shall have a hatch aperture with a minimum area 	of 400,000 mm2.  It shall be possible to inscribe in this area a rectangle 	measuring 500 mm x 700 mm."

Paragraph 7.6.3.2., amend to read:

"7.6.3.2.	Vehicles of Class A or B may meet either the requirements shown in 	paragraph 7.6.3.1. (Class A meeting Class I requirements and Class B meeting 	Class II and III requirements) or those contained in Annex 7, paragraph 1.1."

Paragraph 7.6.4.6., amend to read:

"7.6.4.6.	If the direct view is not adequate, optical or other devices shall be installed to 		enable the driver to detect from his seat the presence of a passenger in the 	immediate interior and exterior vicinity of every side service door which is not an 	automatically-operated service door.

In the case of double-deck vehicles of Class I, this requirement also applies to the 		interior of all service doors and to the immediate vicinity of each 	intercommunication staircase on the upper deck.

In the case of a service door in the rear face of the vehicle not 	exceeding 22 passengers, this requirement is satisfied if the driver is able to detect 	the presence of a person 1.3 m tall standing 1 m behind the vehicle.

Driving mirrors may be used to meet the requirements of this paragraph provided 		that the field of view required for driving is still met."

In the case of doors situated behind the articulated section of an articulated vehicle, 		mirrors shall not be deemed to be a sufficient optical device.

## Paragraph 7.6.5.4., amend to read:

"7.6.5.4.	.... in the normal driving position in any normal ambient lighting condition, to warn 		.… "

Paragraph 7.6.10.7., amend to read:

"7.6.10.7.	(Reserved)"

Paragraph 7.6.10.9., amend to read:

"7.6.10.9.	when the passenger door is open, the retractable step shall be securely held in the 		extended position.  When a mass of 136 kg is placed in the centre of a single step 		or a mass of 272 kg is placed in the centre of a double step the deflection at any 		point on the step, measured relative to the body of vehicle, shall not 	exceed 10 mm."

Paragraph 7.6.11.1., amend to read:

"7.6.11.1.	Each emergency exit shall be marked, inside and outside the vehicle, by the 		symbol reproduced in Annex 4, figure 29.  An additional symbol (e.g. arrow), 		indicating where to find the emergency exit, may be added.”

Paragraphs 7.7.1.1. and 7.7.1.2., amend to read:

"7.7.1.1.	The free space extending inwards into the vehicle from the side wall in which the 		door is mounted shall permit the free passage of one test gauge having the 	dimensions of either test gauge 1 or test gauge 2 specified in Annex 4, figure 1.

The test gauge shall be maintained parallel with the door aperture as it is moved 		from the starting position, where the plane of the face nearest to the interior of the 		vehicle is tangential to the outermost edge of the aperture, to the position where it 		touches the first step, after which it shall be kept at right angles to the probable 		direction of motion of a person using the entrance.

7.7.1.2.		(Reserved)"

Paragraph 7.7.1.3., amend to read:

"7.7.1.3.	When the centre line of this test gauge has traversed a distance of 300 mm from its 		starting position and the test gauge is touching the surface of the step or floor, it 		shall be retained in that position."

Paragraph 7.7.1.6., amend to read:

"7.7.1.6.	The free passage clearance for this figure shall not include any space extending 		to 300 mm in front of any uncompressed seat cushion of a forward or rearward 		facing seat, or 225 mm in the case of sideways-facing seats, and to the height of 		the top of the seat cushion (see Annex 4, figure 25)."

Paragraph 7.7.1.8., amend to read:

"7.7.1.8.	However, one or more folding seat(s) for use by the crew may obstruct the access 		passage to a service door when in the position of use provided that:"

Paragraph 7.7.2.1., amend to read:

"7.7.2.1.	Except as provided for in paragraph 7.7.2.4., the free space between the gangway 		and the emergency door .... "

Paragraph 7.7.5.6., amend to read:

"7.7.5.6.	Folding seats allowing passengers to sit in the gangway shall not be permitted.  		Folding seats shall, however, be permitted in other areas of the vehicle so long as 		they do not obstruct the passage down the gangway of the gangway test gauge 		when in the open (seating) position."

Paragraph 7.7.7.2., amend to read:

"7.7.7.2.	The height of a step shall be measured at the centre of its width at the outer edge, 		the tyre equipment and pressure being as specified by the manufacturer for the 		technically permissible maximum laden mass (M)."

Paragraph 7.7.8.3., amend to read:

"7.7.8.3.	Height of seat cushion (dimension H, see Annex 4, figure 11a)"

The height of the …. less than 350 mm at the wheel arches (taking into account the 		allowances permitted in paragraph 7.7.8.5.2.) and at the engine/transmission 		compartment."

Paragraph 7.7.8.5.1., amend to read:

"7.7.8.5.1.	For a seat behind a partition or other rigid structure other than a seat, a minimum 		clear space in front of each required passenger seating space (as defined in 	paragraph 7.7.8.6.) shall be provided as shown in Annex 4, figure 13.  A partition 	whose contour corresponds approximately to that of the inclined seat back may 	intrude into this space.  In the case of seats alongside the driver's seat in vehicles 	of Class A or B, intrusion of the dashboard, instrument panel, gear change control, 	windscreen, sun visor, seat belts and seat belt anchorages shall be allowed."

Insert a new paragraph 7.7.8.5.2., to read:

"7.7.8.5.2.	For a seat behind a seat and/or a seat facing the gangway, a minimum clear foot 		space of at least 300 mm depth and a width according to paragraph 7.7.8.1.1., 		shall be provided as shown in Annex 4, figure 11b.  The local presence in this 		space of seat legs, passenger footrests and of intrusions as provided by 	paragraph 7.7.8.6. shall be permitted provided that adequate space remains for the 	passengers' feet.  This foot space may partly be situated in and/or above the 	gangway but shall not create any obstruction when measuring the minimum 	gangway-width in accordance with paragraph 7.7.5.  In the case of seats alongside 	the driver's seat in vehicles of Class A or B, intrusion of the seat belts and seat belt 	anchorages shall be allowed."

Paragraph 7.7.8.5.2. (former), renumber as paragraph 7.7.8.5.3. and amend to read:

"7.7.8.5.3.	However, at least two in Class I and Class II and one in Class A forward or 		rearward facing seats specifically intended and marked for passengers with 		reduced mobility other than wheelchair users shall be provided in that part of the 		bus which is most suitable for boarding.  These seats shall be designed for 	passengers with reduced mobility so as to provide enough space, shall have 	suitably designed and placed handholds to facilitate entry and exit of the seat and 	provide communication in accordance with paragraph 7.7.9. from the seated 	position."

Paragraph 7.7.8.5.2.1., renumber as paragraph 7.7.8.5.3.1.

Paragraph 7.7.8.6.1., amend to read:

"7.7.8.6.1.	In the case of single deck vehicles, over each seating position and, except in the 		case of the seat(s) alongside the driver in a vehicle of Class A or B, its associated 		foot space, there shall be measured a free space with a height of not less 	than 900 mm measured from the highest point of the uncompressed seat cushion 	and at least 1,350 mm from the mean level of the floor in the foot space.  In the case 	of vehicles to which paragraph 7.7.1.10. applies, and also for the seat(s) alongside 	the driver in a vehicle of Class A or B, these dimensions may be reduced 	to 1,200 mm measured from the floor and 800 mm measured from the highest point 	of the uncompressed seat cushion.

In the case of double deck vehicles, each …. "

Paragraph 7.7.8.6.3.2., amend to read:

"7.7.8.6.3.2.	in the case of the upper part of the outboard seating position, a zone with 	triangular cross-section whose apex is situated 700 mm from the top and whose 	base is 100 mm in width (see Annex 4, figure 15).  The space needed for safety 	belts and their anchorages and for the sun visor is also excluded;"

Paragraph 7.7.8.6.3.3., amend to read:

"7.7.8.6.3.3.	in the case of the foot well of an outboard seating position, a zone of a cross-		sectional area not exceeding, 0.02 m2 (0.03 m2 for low floor vehicles) and having a 		maximum width not exceeding 100 mm (150 mm for low floor vehicles) (see 		Annex 4, figure 16)."

Paragraph 7.7.9.1., replace the value "1200 mm" by "1,500 mm" and amend to read:

"…. have them on each deck.

The provisions of paragraph 7.6.11.4. apply to any textual markings used."

Insert a new paragraph 7.8.1.6., to read:

"7.8.1.6.	In the case of a double-decked vehicle without a roof, at least one lighting device 		shall be provided as near as practicable to the top of every staircase leading to the 		upper deck."

Insert a new paragraph 7.8.5., to read:

"7.8.5.		Control of the mandatory interior lighting shall be by manual switches under the 		control of the driver or automatically controlled."

Paragraph 7.11.1.4., amend to read:

"7.11.1.4.	The clearance between a hand-rail or hand-hold, along the majority of its length, 		and the adjacent part of the vehicle body or walls shall be at least 40 mm. However, 		in the case of a handrail on a door or a seat, or in the access passage of a vehicle of 		Class II, III or B, a minimum clearance of 35 mm shall be permitted."

Paragraph 7.11.2., amend to read:

"7.11.2.	Additional requirements for handrails and handholds for vehicles designed to carry 		standing passengers"

Paragraph 7.11.2.2., amend to read:

"7.11.2.2.	When applying the procedure described in paragraph 7.11.2.1., only such hand-		rails and handholds shall be considered which are not less than 800 mm and not 		more than 1,950 mm above the floor."

Paragraph 7.12.1., amend to read:

"7.12.1.	Where any seated passenger is likely to be thrown forward into a step well as a 		result of heavy braking, either a guard or, in the case of a vehicle of Class A or B, a 		seat belt shall be fitted.  Where fitted, the guard shall have a minimum height .... "

Insert new paragraphs 7.17. to 7.17.2., to read:

"7.17.		Passenger protection in vehicles without a roof

Every vehicle without a roof shall have:

7.17.1. 	a continuous front panel over the full width of that part of the vehicle that does 		not have a roof, with a height of not less than 1,400 mm from the general level of 		the floor adjacent to the front panel;

7.17.2.	a continuous protection around the side and rear of that part of the vehicle that 	does not have a roof, with a height of not less than 1,100 mm at the sides 	and 1,200 mm at the rear of the vehicle, measured from the general level of the 	floor adjacent to the panels.  The protection shall consist of continuous side and 	rear panels with a height of not less than 700 mm from the general level of the 	floor adjacent to the panels, combined with one or more continuous guard rail(s) 	that fulfils the following characteristics:

(a)	no dimension of its section must be less than 20 mm, or more than 45 mm;

(b)	the size of any aperture between a guard rail and any adjacent guard rail or 	panel shall not exceed 200 mm;

(c)	it shall be firmly attached to the structure of the vehicle;

(d)	doors at exits shall be considered to form part of this protection."

Insert a new paragraph 7.18., to read:

"7.18.		Vision and communication aid

In the case of a vehicle without a roof, the driver shall be provided with a visual 	means, such as a mirror, periscope or video camera/monitor, to enable the 	behaviour of passengers in the area without a roof to be observed.  In addition, 	an intercommunication system shall be provided to enable the driver to 	communicate with these passengers."

Annex 4,

Figure 1, amend to read:

"Figure 1

ACCESS TO SERVICE DOORS

(see Annex 3, paragraph 7.7.1.)

#### Test gauge 1                                                   Test gauge 2

| Vehicle class | Height of the upper panel (mm) (Dimension "A" figure 1) |
| --- | --- |
|  | Test gauge 1 | Test gauge 2 |
| Class A | 950 */ | 950 |
| Class B | 700 */ | 950 |
| Class I | 1,100 | 1,100 |
| Class II | 950 | 1,100 |
| Class III | 850 | 1,100 |

*/	For vehicles of Class A or B, the lower panel may be displaced horizontally relative to the upper panel provided that it is in the same direction."

Figure 11, renumber as Figure 11a.

Insert a new Figure 11b, to read:

"Figure 11b

SPACE FOR FEET OF SEATED PASSENGERS BEHIND A SEAT OR AT A SEAT FACING THE GANGWAY

(see Annex 3, paragraph 7.7.8.5.2.)

"

Figure 13, the title, amend to read:

"Figure 13

SPACE FOR SEATED PASSENGERS BEHIND A PARTITION OR OTHER RIGID STRUCTURE OTHER THAN A SEAT

(see Annex 3, paragraph 7.7.8.5.1.)"

Figure 16, the reference to "Class I", should be deleted (twice).

Figure 20, amend to read:

# "Figure 20

# TESTING DEVICE FOR SITING OF HANDHOLDS

# (see Annex 3, paragraph 7.11.2.1.)

# Thickness: 20 mm."

Figure 23, amend to read:

"Figure 23

ACCESSIBILITY SYMBOLS

(see Annex 8, paragraph 3.4.)

Figure 23 A

Pictogram for wheelchair users

or

Colour:		blue basis with white symbol

Size:		at least 130 mm diameter

Reference for the design principles of safety symbols: 	ISO 3864-1:2002

Figure 23 B

Pictogram for passengers with reduced mobility other than wheelchair users

Colour:	blue basis with white symbol

Size:		at least 130 mm diameter

Reference for the design principles of safety symbols: 	ISO 3864-1:2002"

Figure 24, amend to read:

"Figure 24

(Reserved)"

Insert new Figures 27 and 28, to read:

"Figure 27

### ACCESS TO DRIVER'S DOOR

(See Annex 3, paragraph 7.6.1.7.2.)

Figure 28

ACCESS TO DRIVER'S DOOR

(See Annex 3, paragraph 7.6.1.9.3.)

Insert a new figure 29, to read:								"

"Figure 29

EMERGENCY EXIT MARKING SYMBOL

(See Annex 3, paragraph 7.6.11.1.)

Colour:		green basis with white symbols

Size:		at least 130 mm wide and 50 mm high

Reference for safety symbols:	 			ISO 7010: 2003

Reference for the design principles of safety symbols:	ISO 3864-1: 2002"

Annex 7,

The title, amend to read:

"ALTERNATIVE REQUIREMENTS FOR VEHICLES OF CLASSES A AND B"

After the title, insert the following text to read:

"Vehicles of Classes A and B shall comply with the requirements of Annex 3 with 		the exception that:

-	in place of paragraph 7.6.3.1. of Annex 3, a vehicle may comply with paragraph 1.1. of this annex;

-	in place of paragraph 7.6.2. of Annex 3, a vehicle may comply with paragraph 1.2. of this annex."

Paragraph 1.1.1., amend to read (the table remains):

"1.1.1.	A vehicle to which paragraph 7.7.1.10. of Annex 3 applies shall meet the 	requirements of paragraph 7.6.3.1. of Annex 3 or paragraph 1.1. of this annex as 	regards emergency windows and escape hatches, and the following minimum 	requirements as regards service doors and emergency doors:

…. "

Annex 8,

Paragraph 3.1., amend to read:

"3.1.		Steps

The height of the first step from the ground of at least one service door shall not exceed 250 mm for vehicles of Class I and A and 320 mm for vehicles of Class II, III and B.  In the case where only one service door meets this requirement there must be no barrier or sign which prevents that door from being used as both an entrance and an exit.

As an alternative for vehicles of Class I and A, the first step from the ground shall not exceed 270 mm in two door openings, one entrance and one exit.

A kneeling system and/or retractable step may be engaged.

The height of steps in an access passage at the above-mentioned door(s), and in the gangway, shall be not more than 200 mm for vehicles of Class I and A 	and 250 mm for vehicles of Class II, III and B.

The transition from a sunken gangway to a seating area shall not be considered to be a step."

Paragraph 3.2.1., amend the reference to paragraph "7.7.8.5.2." to read "7.7.8.5.3."

Paragraph 3.2.3., amend to read:

"3.2.3.	Armrests shall be fitted on seats between the seating position and the gangway and shall be capable of being moved easily out of the way to permit clear access to the seat.  In the case of seats facing each other, one of the gangway seats may alternatively be fitted with a vertical stanchion.  This stanchion shall be positioned such that the seat occupant is kept securely on the seat and easy access to the seat is possible.

Handrails or handholds shall be fitted adjacent to priority seats in such a way as to allow the passenger to grasp them easily."

Paragraph 3.2.7., amend to read:

"3.2.7.	Each priority seating position shall have a free height of not less than 1,300 mm for vehicles of Class I and A and 900 mm for vehicles of Class II, measured from the highest point of the uncompressed seat cushion.  This free height shall extend over the vertical projection of the whole of the seat and the associated foot space.  Intrusion of a seat back or other object into this space shall be permitted provided that a minimum clear vertical space extending 230 mm in front of the seat cushion is maintained.  Where the priority seat is positioned facing a bulkhead more than 1,200 mm in height this space shall be 300 mm.  From the edges of the free space defined above, intrusions are permitted in accordance with paragraphs 7.7.8.6.3.1. to 7.7.8.6.3.4. of Annex 3 as if reference to the clear space in paragraphs 7.7.8.6.1. and 7.7.8.6.2. of Annex 3 is a reference to the clear space defined above.  The provisions of paragraph 7.7.8.1.4. of Annex 3 may apply.  Intrusions of handholds or handrails as mentioned in the second sub-paragraph of paragraph 3.2.3. may protrude by a maximum of 100 mm from the sidewall into the clear space over the vertical projection of the foot space."

Paragraph 3.3.4., amend to read:

"3.3.4.	If a vehicle is fitted with a ramp or lift, a means of communication with the driver shall be fitted outside, adjacent to the door, and at a height between 850 mm and 1,300 mm from the ground.  This requirement shall not apply to a door situated in the direct field of vision of the driver."

Paragraph 3.8.1., amend to read:

"3.8.1.	Wheelchair restraint system.  In vehicles required to have occupant restraint systems fitted, the wheelchair space shall be designed for the wheelchair user to travel facing forwards and shall be fitted with wheelchair and occupant restraint systems complying with paragraphs 3.8.1.2. or 3.8.2.

In vehicles not required to have occupant restraint systems fitted, the wheelchair space shall be fitted with restraint systems complying with paragraph 3.8.1.1. or 3.8.3."

Paragraph 3.9.1., amend to read:

"3.9.1.	If a door referred to in paragraph 3.6. is fitted with opening controls for use under normal circumstances, whether being outside or inside of the vehicle, these controls shall be adjacent to that door at a height between 850 mm and 1,300 mm from the ground (exterior controls) or the floor (interior controls)."

Paragraph 3.11.2.3., amend to read:

"3.11.2.3.	The lowering process shall be capable of being stopped and immediately reversed .… "

Paragraph 3.11.2.4., amend to read:

"3.11.2.4.	Any kneeling system that is fitted to a vehicle shall neither:

3.11.2.4.1.	allow the vehicle to be driven at a speed of more than 5 km/h when the vehicle is lower than the normal height of travel, nor

3.11.2.4.2.	allow the vehicle to be lowered when the operation of the service door is 	prevented for any reason."

Paragraph 3.11.4.3.3., amend to read:

"3.11.4.3.3.	These safety devices shall immediately stop the movement of the ramp when the ramp is subject to a reactive force not exceeding 150 N."

Paragraph 3.11.4.4.1., amend to read:

"3.11.4.4.1.	Where the driver has an adequate view of the ramp sufficient to monitor its deployment and use, to ensure the safety of passengers, the ramp may be operated by the driver when in the driver's seat.  This requirement may be met by using suitable indirect vision devices."

- - - - -

# Text boxes

Test gauge of 600 mm x 400 mm as described in Annex 3, paragraph 7.7.3.3.

Gangway test gauge

Test gauge of 60 cm x 40 cm as described in paragraph 5.7.3.3.

Gangway test gauge

Test gauge of 600 mm x 400mm as in Annex 3, paragraph 7.7.3.3.

15 cm min

70 cm min

30 ° max
– 8 ° min

30 cm min

60 cm max

550 mm

400 mm

700 mm

A

500 mm

30 o

30 o

A

400 mm

400 mm

20 mm

see Annex 3,

para 7.7.1.6.

700 mm

550 mm

400mm