| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/31/Add.1 24 March 2006 Original: ENGLISH |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-thirty-ninth session

Geneva, 20-23 June 2006,

Item 4.2.18. of the provisional agenda

PROPOSAL FOR SUPPLEMENT 4 TO THE 02 SERIES OF AMENDMENTS  TO REGULATION No. 51

(Noise emissions)

Addendum

Submitted by the representative of the European Community (EC)

Note:	The text reproduced below was prepared by the representative of the EC in order to complement its proposal.

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

GE.06-

Parragraph 5.1., amend to read:

"5.1.	Type approval shall only be granted if,

(a)	the vehicle type meets the requirements of paragraphs 6. and 7. below when tested according to measurement method A of annex 3, and

(b)	starting at 1 April 2007 and for a maximum period of two years, the results of the test run of that vehicle type in accordance with the measurement method B of annex 10 have been added to the communication form in annex 9 and communicated to all Contracting Parties to the Agreement applying this Regulation. This does not include any tests done in connection with the extension of existing approvals according to Regulation No. 51.  Furthermore, for the purpose of this monitoring procedure a vehicle is not considered to be a new type if the vehicle differs only in respect to paragraphs 2.2.1. and 2.2.2."

- - - - -