| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/32 24 March 2006 Original: ENGLISH |
| --- | --- | --- |

##### ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-thirty-ninth session

Geneva, 20-23 June 2006,

Item 4.2.8. of the provisional agenda

#### DRAFT CORRIGENDUM 5 TO SUPPLEMENT 15 TO THE 04 SERIES OF AMENDMENTS

#### TO REGULATION No. 16

(Safety-belts)

Submitted by the Working Party on Passive Safety (GRSP)

Note:  The text reproduced below was adopted by GRSP at its thirty-eighth session and is submitted for consideration to WP.29 and AC.1 (TRANS/WP.29/GRSP/38, para. 19).  It is based on the text of annex 2 to the report.

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Paragraph 8.3.5., amend to read:

"8.3.5.	In order to inform … of Regulation No. 14.

The first ISOFIX position shall allow at least the installation of one out of the three forward-facing fixtures as defined in appendix 2 of annex 17; the second ISOFIX position shall allow at least the installation …... of the vehicle."

Paragraph 15.1.3., add at the end:

"15.1.3.	............... in accordance with Supplement 15 to the 04 series of amendments to this Regulation.  However, existing approvals of the vehicle categories other than M1 and which are not affected by Supplement 15 to the 04 series of amendments to this Regulation shall remain valid and Contracting Parties applying this Regulation shall continue to accept them."

Annex 17, paragraph 1.1., item (c), amend to read:

"Provide a list of child restraint systems …"

- - - - -