| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/96 12 July 2006 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-fortieth session

Geneva, 14-17 November 2006

Item 4.2.10. of the provisional agenda

PROPOSAL FOR SUPPLEMENT 1 TO THE 03 SERIES AMENDMENTS

TO REGULATION No. 26

(Exterior projections)

Transmitted by the Working Party on General Safety Provisions (GRSG)

Note:	The text reproduced below was adopted by GRSG at its ninetieth session.  It is based on ECE/TRANS/WP.29/GRSG/2006/11, amended as reproduced on paragraph 26 of the report.  It is submitted to WP.29 and AC.1 for consideration (ECE/TRANS/WP.29/GRSG/69, para. 26).

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user.

Documents are also available via the INTERNET:

http://www.unece.org/trans/main/welcwp29.htm

Paragraph 6.8.1., amend to read:

"6.8.1.	Sheet-metal edges, such as gutter edges and the rails of sliding doors, shall not be 	permitted unless they are folded back or are fitted with a shield meeting the requirements 	of this Regulation which are applicable to it.

An unprotected edge shall be considered to be folded back either if it is folded back by 	approximately 180 º, or if it is folded towards the bodywork in such a manner that it 	cannot be contacted by a sphere having a diameter of 100 mm.

The requirements of paragraph 5.4. shall not apply to the following sheet metal edges: 	rear edge of bonnet and front edge of rear luggage boot."

- - - - -