| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/GRPE/2006/5 3 November 2005 Original: ENGLISH ENGLISH AND FRENCH ONLY |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Pollution and Energy (GRPE)

(Fifty-first session, 16-20 January 2006,

agenda item 10.1.)

PROPOSAL FOR AMENDMENTS TO REGULATIONS Nos. 24, 49, 67, 83 and 110

(Clarification of the scopes of the Regulations)

Transmitted by the expert from the European Commission (EC)

Note:		The text reproduced below was prepared by the expert from the EC in order to make the scope more precise.  It is based on a document without a symbol (informal document No. GRPE-49 12), distributed at the forty-ninth GRPE session.  The modifications to the current text of the Regulations are marked in bold characters.

A reference to the latest version of R.E.3 (TRANS/WP.29/78/Rev.1/Amend.4) shall be added for each of the scopes.

A.1.	PROPOSAL

REGULATION No. 24 – (Visible pollutants)

Paragraphs 1.1.1. to 1.1.3., amend to read:

"1.1.1.	PART I.	The emission of visible exhaust pollutants from C.I. engines which are intended for fitting to power-driven vehicles (vehicles of categories L, M, N, T and mobile machinery).

1.1.2.	PART II.	The installation into power-driven vehicles of C.I. engines that have been type approved to Part I of this Regulation.

1.1.3.	PART III.	The emission of visible exhaust pollutants from a power-driven vehicle that is fitted with an engine that has not been separately type approved to Part I of this Regulation."

B.1.	JUSTIFICATION

This Regulation shall apply to the mentioned vehicle categories falling under the Vienna Convention definition of "power-driven vehicle", but not to trailers and other vehicles that might be included in the definition "road vehicles".

A.2.	PROPOSAL

REGULATION No. 49 – (Emissions of C.I., NG, and P.I. (LPG) engines)

Paragraph 1., amend to read:

"1.	SCOPE

1.1.	This Regulation applies to vehicles of categories M and N and their engines, as shown by Table A, with regard to the tests foreseen for these engines in Table B.

Table A: APPLICABILITY

| Vehicle category | Max. mass | Positive-ignition engines | Compression-ignition engines |
| --- | --- | --- | --- |
|  |  | Petrol | NG 1/ | LPG 2/ | Diesel | Ethanol |
| M1 | ≤ 3.5 t | - | - | - | - | - |
|  | > 3.5 t | - | R49 | R49 | R49 | R49 |
| M2 | - | - | R49 | R49 | R49 or R83 3/ | R49 |
| M3 | - | - | R49 | R49 | R49 | R49 |
| N1 | - | - | R49 or R83 | R49 or R83 | R49 or R83 | R49 |
| N2 | - | - | R49 | R49 | R49 or R83 3/ | R49 |
| N3 | - | - | R49 | R49 | R49 | R49 |

1/	Natural Gas.

2/	Liquefied Petroleum Gas.

3/	Regulation No. 83 applies only for vehicles with a reference mass ≤  2,840 kg as an extension of an approval given for an engine used in vehicles of categories M1 or N1.

"R49 or R83" means that manufacturers can obtain type approval according to this Regulation or to Regulation No. 83, see paragraph 1.2.

Table B: REQUIREMENTS

|  | Positive-ignition engines | Compression-ignition engines |
| --- | --- | --- |
|  | Petrol | NG 1/ | LPG 2/ | Diesel | Ethanol |
| Gaseous pollutants | - | Yes | Yes | Yes | Yes |
| Particulates | - | - | - | Yes | - |

1.2.	Equivalent approvals

The following do not need to be approved according to this Regulation, if they are part of a vehicle approved according to Regulation No. 83:

- compression-ignition engines to be mounted in vehicles of categories N1, N2 and M2 fuelled with diesel;

-	positive-ignition engines fuelled with natural gas (NG) or liquefied petroleum gas (LPG) to be mounted in vehicles of category N1."

B.2.	JUSTIFICATION

Changes in the scope have been introduced several times in successive amendments.  The tables clarify the current scope of the Regulation.

A.3.	PROPOSAL

REGULATION No. 67 – (Equipment for liquefied petroleum gas)

Paragraph 1., amend to read:

"1.	SCOPE

This Regulation applies to:

1.1.	Part I.	Approval of specific equipment of vehicles of category M and N using liquefied petroleum gases in their propulsion system;

1.2.	Part II.	Approval of vehicles of category M and N fitted with specific equipment for the use of liquefied petroleum gases in their propulsion system with regard to the installation of such equipment."

B.3.	JUSTIFICATION

This Regulation shall not apply to motor vehicles other than those of categories M and N.

A.4.	PROPOSAL

REGULATION No. 83 – (Emissions of M1 and N1 categories of vehicles)

Paragraph 1., amend to read:

"1.	SCOPE

This Regulation applies to vehicles of categories M and N as shown by Table A, with regard to the tests foreseen for these vehicles in Table B.

Table A. APPLICABILITY

| Vehicle category |  | Positive-ignition engined vehicles including hybrid vehicles | Compression-ignition engined vehicles including hybrid vehicles |
| --- | --- | --- | --- |
|  | Max. mass | Petrol | NG 1/ | LPG 2/ | Diesel |
| M1 | ≤ 3.5 t | R83 | R83 | R83 | 83 |
|  | > 3.5 t | R83 | - | - | - |
| M2 | - | R83 | - | - | R49 or R83 3/ |
| M3 | - | R83 | - | - | - |
| N1 | - | R83 | R49 or R83 | R49 or R83 | R49 or R83 |
| N2 | - | R83 | - | - | R49 or R83 3/ |
| N3 | - | R83 | - | - | - |

1/	Natural Gas.

2/	Liquefied Petroleum Gas.

3/	Regulation No. 83 applies only for vehicles with a reference mass  ≤  2,840 kg as an extension of an approval given for an engine used in vehicles of categories M1 or N1.

"R49 or R83" means that manufacturers can obtain type approval according to this Regulation or to Regulation No. 49.

Table B. REQUIREMENTS

| Requirements | Positive-ignition engined vehicles of categories M and N including hybrid vehicles | Compression-ignition engined vehicles of categories M1 and N1 including hybrid vehicles |
| --- | --- | --- |
|  | petrol fuelled vehicle | bi-fuel vehicle | mono-fuel vehicle | Diesel fuelled vehicles |
| Gaseous pollutants | Yes (max. mass ( 3.5 t) | Yes (test with both fuel types) (max. mass ( 3.5 t) | Yes (max. mass ( 3.5 t) | Yes (max. mass ( 3.5 t) |
| Particulates | - | - | - | Yes (max. mass ( 3.5 t) |
| Idle emissions | Yes | Yes (test with both fuel types) | Yes | - |
| Crankcase emissions | Yes | Yes (test only with petrol) | Yes | - |
| Evaporative emissions | Yes (max. mass ( 3.5 t) | Yes (test only with petrol) (max. mass ( 3.5 t) | - | - |
| Durability | Yes (max. mass ( 3.5 t) | Yes (test only with petrol) (max. mass ( 3.5 t) | Yes (max. mass ( 3.5 t) | Yes (max. mass ( 3.5 t) |
| Low temperature emissions | Yes (max. mass ( 3.5 t) | Yes (test only with petrol) (max. mass ( 3.5 t) | - | - |
| In-use conformity | Yes (max. mass ( 3.5 t) | Yes (max. mass ( 3.5 t) | Yes. (max. mass ( 3.5 t) | Yes (max. mass ( 3.5 t) |
| On-board diagnostics | Yes (max. mass ( 3.5 t) | Yes (max. mass ( 3.5 t) | Yes (max. mass ( 3.5 t) | Yes (max. mass ( 3.5 t) |

B.4.	JUSTIFICATION

Changes in the scope have been introduced several times in successive amendments.  The tables clarify the current scope of the Regulation.

A.5.	PROPOSAL

REGULATION No. 110 – (Equipment for compressed natural gas)

Paragraph 1., amend to read:

"1.	SCOPE

This Regulation applies to:

1.1.	Part I.	Specific components for vehicles of category M and N using compressed natural gas (CNG) in their propulsion system;

1.2.	Part II.	Vehicles of category M and N with regard to the installation of specific components, for the use of compressed natural gas (CNG) for propulsion, of an approved type."

B.5.	JUSTIFICATION

This Regulation shall not apply to other motor vehicles than vehicles of category M and N.

- - - - -