| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/GRSG/2006/30 28 July 2006 Original: ENGLISH ENGLISH AND FRENCH ONLY |

###### ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on General Safety Provisions (GRSG)

Ninety-first session
Geneva, 17-20 October 2006
Agenda item 2.4

# PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 46

## (Devices for indirect vision)

## Transmitted by the expert from France

Note:  The text reproduced below was transmitted by the expert from France in order to clarify the installation requirements of Class I (interior) mirrors on vehicles of categories M1 and N1.  In addition, it proposes implementation conditions of optional mirrors on vehicles of categories M2 and M3.  It is based on and supersedes document ECE/TRANS/WP.29/GRSG/2006/18.  The modifications to the current text of the Regulation (up to the 02 series of amendments) are marked in bold characters.

_______________________

Note:  This document is distributed to the Experts on General Safety Provisions only.

GE.06-24478  (E)    200906    210906

A.	PROPOSAL

Paragraph 15.2.1.1.1, the table, the second column “Interior mirror Class I”, the cells corresponding to the M1 and N1 vehicle categories, amend to read:

“Compulsory

Unless the vehicle is fitted with safety glazing material in the field of vision stipulated in paragraph 15.2.4.1”

Paragraph 15.2.2.2, amend to read:

“ … shall not apply to:

(a)	exterior mirrors on the passenger side and optional exterior mirrors on the driver side of vehicles of categories M2 and M3;

(b)	Class VI mirrors.”

Paragraph 15.2.4.8.1, amend to read:

“15.2.4.8.1	Interior rear-view mirror (Class I)

The field of vision may be reduced by the presence of devices such as sun visors, windscreen wipers, heating elements and stop lamp of category S3, provided that all these devices together do not obscure more than 15% of the prescribed field of vision.  This requirement shall be tested by projection on to a vertical plane at right angles to the longitudinal centreplane of the vehicle.  The degree of obstruction shall be measured with the sun visors folded back.

The field of vision may also be reduced by components of framework or bodywork such as window columns of rear split doors, rear window frame, or headrests.”

B.	JUSTIFICATION

Reference to paragraph 15.2.1.1.1

This proposal aims to clarify mandatory installation requirements of the Class I (interior mirrors) mirrors on the vehicles of categories M1 and N1.  The mandatory installation of these mirrors is required because the driver can use such a mirror when driving or manoeuvring.  In order to comply with this requirement, the vehicle has to be equipped with a safety glazing material, installed in the driver’s indirect vision, as specified in Regulation No. 43.  The wording of paragraph 15.2.1.1.1 is in line with the definition of this glazing material.

Reference to paragraph 15.2.2.2

The requirement for exterior mirrors situated on the driver side to be visible through the portion of the windscreen swept by the windscreen wiper makes it very difficult, even impossible, for manufacturers to install optional wide-angle mirrors on vehicles of categories M2 and M3.  The proposal to modify paragraph 15.2.2.2 aims to allow this installation which improves the driver’s indirect vision conditions when driving or manoeuvring.

Reference to paragraph 15.2.4.8.1

Paragraph 15.2.1.1.1 provides that fields of vision shall be obtained from the minimum number of compulsory mirrors.  Vehicles of categories M1 and N1 must be equipped with two exterior mirrors, allowing a wider field of vision compared to the former requirements (01 series of amendments) of the Regulation.  Concerning the compulsory interior mirror installation requirements (see the reference to paragraph 15.2.1.1.1 above), the design and construction requirements of the vehicles might not be consistent with the dimensions of the field of vision.  The proposal to modify paragraph 15.2.4.8.1 confirms the mandatory presence of the interior mirror, enabling the rear transparent area of the vehicle to be visible even if the field of vision cannot be respected, and takes account of constraints imposed by the architecture of the vehicle and the optional installation of headrests on all rear seats.

-----