| Transmitted by the representative from Japan | Informal Document No. WP.29-142-13 142nd WP.29, 26-29 June 2007, agenda item 4.2.6. |
| --- | --- |

Proposal for the 01 series of amendments to Regulation No. 64

(Temporary use spare wheels/tyres)

The text reproduced below was adopted by GRRF at its sixty-first session.  It is based on ECE/TRANS/WP.29/GRRF/2002/17/Rev.7, as amended by Annex 2 to the report.  It is submitted to WP.29 and AC.1 for consideration (ECE/TRANS/WP.29/GRRF/61, para. 29).

A.	PROPOSAL

Insert new paragraphs 12.1 and 12.3-12.5.,

Paragraph 12.2., amend to read:

"12.	TRANSITIONAL PROVISIONS

12.1.	As from the official date of entry into force of the 01 series of amendments, no Contracting Party applying this Regulation shall refuse to grant approval under this Regulation as amended by the 01 series of amendments

12.2.	As from 36 months after the date of entry into force of the 01 series of amendments, Contracting Parties applying this Regulation with respect to the temporary use spare wheels/tyres, run flat tyres or a run flat system shall grant approvals only if the vehicle type to be approved meets the requirements of this Regulation as amended by the 01 series of amendments.

12.3.	Contracting Parties applying this Regulation shall not refuse to grant extensions of approval to the preceding series of amendments to this Regulation.

12.4.	Contracting Parties applying this Regulation shall continue to grant approvals to those types of vehicles which comply with the requirements of this Regulation as amended by the proceeding series during the 36 months' period which follows the date of entry into force of the 01 series of amendments.

12.5.	Notwithstanding the transitional provisions above, Contracting Parties whose application of this Regulation comes into force after the date of entry into force of the most recent series of amendments are not obliged to accept approvals which were granted in accordance with any of the preceding series of amendments to this Regulation.

B.	JUSTIFICATION

These paragraphs are editorial correction based on General guidelines for UNECE regulatory procedures and transitional provisions in UNECE Regulations, TRANS/WP29/1044 which was approved at WP.29 at its one-hundred-and-thirty-sixth session.

- - - - -