OICA PROPOSAL FOR A CORRIGENDUM RELATING TO

DOCUMENT ECE/TRANS/WP.29/2007/26

Annex 4A, Appendix 2, paragraph 5.4.1, amend to read:

" Alternatively, if the fuel composition is not known, the following stoichiometric factors may be used:

FS (diesel)	=	13.4

FS (LPG)	=	11.6

FS (NG)		=	9.5

FS (Ethanol)	=	12.3

JUSTIFICATION

The FS factor for ethanol-fueled engines was not carried over from Directive 2005/55/EC Annex VIII when aligning ECE R 49 with the Directive. All other calculation procedures for ethanol engines originally included in Annex VIII of the Directive are covered within the general calculation sections of document ECE/TRANS/WP.29/2007/26.

- - - - -