| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/GRRF/2007/17 13 July 2007 Original: ENGLISH ENGLISH AND FRENCH ONLY |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

Working Party on Brakes and Running Gear

Sixty-second session

Geneva, 25-28 September 2007

Item 7. of the provisional agenda

REGULATION No. 90 (Replacement brake linings)

#### Proposal for a draft corrigendum to Regulation No. 90

Submitted by the expert from the United Kingdom

#### The text reproduced below was prepared by the expert from United Kingdom in order to clarify the application of test speeds for the speed sensitivity test.  The modifications to the current text of the Regulation are marked in bold characters.

A.	PROPOSAL

Annex 3

Paragraph 2.1.2.1., amend to read:

"2.1.2.1.	Using the pedal force derived from paragraph 2.1.1.2. of this annex and with initial brake temperature ≤ 100 °C, make three brake applications from each of the following speeds:

(a) Front axle 65, 100 km/h and additionally 135 km/h where vmax exceeds 150 km/h.

(b) Rear axle 45, 65 km/h and additionally 90 km/h where vmax exceeds 150 km/h."

Paragraph 2.1.2.1., amend to read:

"2.2.4.1.	Using the line pressure derived from paragraph 2.2.3.2. and with initial brake temperature ≤ 100 °C make three brake applications from rotational speeds corresponding to vehicle linear speeds of:

(a) 75, 120 km/h and additionally 160 km/h where vmax exceeds 150 km/h."

B.	JUSTIFICATION

The United Kingdom wishes to put forward this proposal as a Corrigendum to the adopted 01 series of amendments to Regulation No. 90 in order to clarify the application of test speeds in relation to the maximum speed of the vehicle.

- - - - -