| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/GRSG/2007/6 1 February 2007 Original: ENGLISH ENGLISH AND FRENCH ONLY |

### ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

Working Party on General Safety Provisions

Ninety-second session

Geneva, 16-20 April 2007

Item 2.2.6. of the provisional agenda

BUSES AND COACHES

Regulation No. 107 (M2 and M3 vehicles)

Fire safety in buses

Proposal for draft amendments to Regulation No. 107

Submitted by the expert from Germany

The text reproduced below was prepared by the expert from Germany in order to improve the requirements for protection against the fire risks.  The text is based on informal document No. GRSG-91-29, distributed during the ninety-first session of the Working Party on General Safety Provisions (GRSG) (ECE/TRANS/WP.29/GRSG/70, para. 19), and takes into account the comments addressed at that session.  The modifications to the current text of the Regulation are marked in bold characters.

A.	PROPOSAL

Annex 3,

Insert a new paragraph 7.5.1.4., to read:

"7.5.1.4.	The engine compartment shall be equipped with a system providing the driver with an acoustic and/or visual signal in the event of fire."

Paragraph 7.5.1.4. (former), renumber as paragraph 7.5.1.5.

B.	JUSTIFICATION

This proposal is based on the results of research studies related to emergency exits and fire safety.  These studies were conducted by the German "Bundesanstalt für Straßenwesen" (Federal Highway Research Institute), which is a subordinate to the German Ministry of Transport, Building and Urban Affairs.

- - - - -