UN/SCETDG/34/INF. 64

COMMITTEE OF EXPERTS ON THE TRANSPORT OF DANGEROUS GOODS AND ON THE GLOBALLY HARMONIZED SYSTEM OF CLASSIFICATION AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the Transport of Dangerous Goods

Thirty-fourth session Geneva, 1-9 December 2008 Item 4 of the provisional agenda

LISTING, CLASSIFICATION AND PACKING

Proposed revision to UN3028 - Transport of Nickel-Metal Hydride Batteries

Submitted by the United Kingdom and International Vessel Operators Hazardous Materials Association, Inc. (VOHMA)

- Recognising that at DSC12 in September 2007, after discussing the consequences of a serious incident, IMO took the decision to refer the issue to the Committee to achieve a harmonised approach.

- Listening to the debate, the following is proposed as a workable multi modal approach for inclusion into the Model Regulations.

Amend entry in Dangerous Goods List as follows, new – underline deleted – strike-through

| 3028 | BATTERIES, DRY, N.O.S. CONTAINING POTASSIUM HYDROXIDE SOLID, electric storage | 8 |  |  | 295 304 274 | 2 kg | E0 | P801 |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Delete text as indicated to make the entry generic and add S.P. 274 to include the technical name of hazardous components.

Revise special provision 304 as follows

Using text from ICAO technical instructions attachment 2 add (a), (b) is existing text and (c) text from INF 10 and ST/SG/AC.10/C.3/2008/97

- Batteries filled with potassium hydroxide, solid which are shipped from the factory in their original dry state and filled with the dry alkali are subject to the provisions of these Regulations.

- Batteries, dry, containing corrosive electrolyte which will not flow out of the battery if the battery case is cracked are not subject to these Regulations provided the batteries are securely packed and protected against short-circuits. Examples of such batteries are: alkali-manganese, zinc-carbon, nickel-metal hydride and nickel-cadmium batteries.

- Nevertheless, in the case of application of this exemption to sea transport of nickel-metal hydride batteries, other than button cells, the following requirements apply:

  - The consignment shall be accompanied by a document describing the batteries as “nickel-metal hydride batteries” including a declaration signed by the consignor that the batteries are securely packed and protected against short-circuits and that stowage away from sources of heat is required;

  - Unit loads and cargo transport units shall be marked “STOW AWAY FROM SOURCES OF HEAT” in capital letters not less than 65 mm high.".

________________