OICA PROPOSAL FOR AMENDMENTS TO REGULATIONS Nos. 83 and 101

In order to harmonize the test procedures between future EU-regulation and current UN/ECE-Regulations, especially with respect to the use in countries outside Europe, the introduction of E5 petrol and B5 diesel as alternative reference fuel is proposed for the Type I and Type VI tests.

The modifications to the text of the Regulation are marked in bold characters.

A.	PROPOSAL

REGULATION No. 83

List of contents, annexes,

Items 2.4., 2.18 amend to read:

2.4. 	“Gaseous pollutants” means the exhaust gas emissions of carbon monoxide, oxides of nitrogen, expressed of:

- C1H1,85 for petrol (E0),

- C1H1,86 for diesel (B0),

- C1H2.525 for LPG,

- C1H4 for NG,

- C1H1.89O0.016 for petrol (E5),

- C1H1.86O0.005 for diesel (B5)

2.18. 	“Fuel requirement by the engine” means the type of fuel normally used by the engine:
- petrol (E0 or E5),

- LPG (liquefied petroleum gas),

- NG (natural gas),

- either petrol or LPG,

- either petrol or NG,

- diesel fuel (B0 or B5).

Annex 4, Item 8.2.; amend to read:

ANNEX 4

TYPE I TEST

…

8. 	DETERMINATION OF THE QUANTITY OF GASEOUS AND PARTICULATE POLLUTANTS EMITTED

  - The volume considered

The volume to be considered shall be corrected to conform to the conditions of 101.33 kPa and 273.2 K.

  - Total mass of gaseous and particulate pollutants emitted

The mass M of each pollutant emitted by the vehicle during the test shall be determined by obtaining the product of the volumetric concentration and the volume of the gas in question, with due regard for the following densities under above-mentioned reference conditions:

In the case of carbon monoxide (CO): d = 1.25 g/l

In the case of hydrocarbons:

- for E0 petrol (CH1.85) d = 0.619 g/l

- for B0 diesel (CH1.86) d = 0.619 g/l

- for LPG (CH2.525) d = 0.649 g/l

- for NG (CH4) d = 0.714 g/l

- for E5 petrol (C1H1.89O0.016) d = 0.631 g/

- for B5 diesel (C1H1.86O0.005) d = 0.622 g/l

Annex 4, Appendix 8

The second subparagraph of paragraph 1.3. of Appendix 8 to Annex 4 shall be amended to read:

“......The dilution factor is calculated as follows:

For each reference fuel:

For a fuel of composition CxHyOz the general formula is:

For the reference fuels contained Annex IX, the values of ‘X’ are as follows.

| Fuel | X |
| --- | --- |
| Petrol (E0) | 13.4 |
| Diesel (B0) | 13.4 |
| LPG | 11.9 |
| NG | 9.5 |
| Petrol (E5) | 13.4 |
| Diesel (B5) | 13.5 |

Annex 10, amend to read:

ANNEX 10

2.	 SPECIFICATIONS OF REFERENCE FUELS FOR TESTING VEHICLES TO THE EMISSION LIMITS GIVEN IN ROW B OF THE TABLE IN PARAGRAPH 5.3.1.4. - TYPE I TEST

2.1. 	TECHNICAL DATA ON THE REFERENCE FUEL TO BE USED FOR TESTING VEHICLES EQUIPPED WITH POSITIVE-IGNITION ENGINES

(1) 	The values quoted in the specifications are “true values”. In establishment of their limit values

the terms of ISO 4259 “Petroleum products – Determination and application of precision data

in relation to methods of test” have been applied and in fixing a minimum value, a minimum

difference of 2R above zero has been taken into account; in fixing a maximum and minimum

value, the minimum difference is 4R (R = reproducibility).

Notwithstanding this measure, which is necessary for technical reasons, the manufacturer of

fuels should nevertheless aim at a zero value where the stipulated maximum value is 2R and

at the mean value in the case of quotations of maximum and minimum limits. Should it be

necessary to clarify the questions as to whether a fuel meets the requirements of the specifications,

the terms of ISO 4259 should be applied.

(2)	The fuel may contain oxidation inhibitors and metal deactivators normally used to stabilise refinery

gasoline streams, but detergent/dispersive additives and solvent oils must not be added.

(3) 	The actual sulphur content of the fuel used for the Type I test shall be reported.

ALTERNATIVELY

Type: Petrol (E5)

| Parameter | Unit | Limits1 | Test method |
| --- | --- | --- | --- |
|  |  | Minimum | Maximum |  |
| Research octane number, RON |  | 95,0 | — | EN 25164 prEN ISO 5164 |
| Motor octane number, MON |  | 85,0 | — | EN 25163 prEN ISO 5163 |
| Density at 15 °C | kg/m3 | 743 | 756 | EN ISO 3675 EN ISO 12185 |
| Vapour pressure | kPa | 56,0 | 60,0 | EN ISO 13016-1 (DVPE) |
| Water content | % v/v |  | 0.015 | ASTM E 1064 |
| Distillation: |  |  |  |  |
| – evaporated at 70 °C | % v/v | 24,0 | 44,0 | EN-ISO 3405 |
| – evaporated at 100 °C | % v/v | 48,0 | 60,0 | EN-ISO 3405 |
| – evaporated at 150 °C | % v/v | 82,0 | 90,0 | EN-ISO 3405 |
| – final boiling point | °C | 190 | 210 | EN-ISO 3405 |
| Residue | % v/v | — | 2,0 | EN-ISO 3405 |
| Hydrocarbon analysis: |  |  |  |  |
| – olefins | % v/v | 3,0 | 13,0 | ASTM D 1319 |
| – aromatics | % v/v | 29,0 | 35,0 | ASTM D 1319 |
| – benzene | % v/v | — | 1,0 | EN 12177 |
| – saturates | % v/v | Report | ASTM 1319 |
| Carbon/hydrogen ratio |  | Report |  |
| Carbon/oxygen ratio |  | Report |  |
| Induction period2 | minutes | 480 | — | EN-ISO 7536 |
| Oxygen content4 | % m/m | Report | EN 1601 |
| Existent gum | mg/ml | — | 0,04 | EN-ISO 6246 |
| Sulphur content3 | mg/kg | — | 10 | EN ISO 20846 EN ISO 20884 |
| Copper corrosion |  | — | Class 1 | EN-ISO 2160 |
| Lead content | mg/l | — | 5 | EN 237 |
| Phosphorus content | mg/l | — | 1,3 | ASTM D 3231 |
| Ethanol4 | % v/v | 4,7 | 5,3 | EN 1601 EN 13132 |
| 1 The values quoted in the specifications are ‘true values’. In establishment of their limit values the terms of ISO 4259 Petroleum products - Determination and application of precision data in relation to methods of test have been applied and in fixing a minimum value, a minimum difference of 2R above zero has been taken into account; in fixing a maximum and minimum value, the minimum difference is 4R (R = reproducibility). Notwithstanding this measure, which is necessary for technical reasons, the manufacturer of fuels shall nevertheless aim at a zero value where the stipulated maximum value is 2R and at the mean value in the case of quotations of maximum and minimum limits. Should it be necessary to clarify whether a fuel meets the requirements of the specifications, the terms of ISO 4259 shall be applied. 2 The fuel may contain oxidation inhibitors and metal deactivators normally used to stabilise refinery gasoline streams, but detergent/dispersive additives and solvent oils shall not be added. 3 The actual sulphur content of the fuel used for the Type 1 test shall be reported. 4 Ethanol meeting the specification of prEN 15376 is the only oxygenate that shall be intentionally added to the reference fuel. 5 There shall be no intentional addition of compounds containing phosphorus, iron, manganese, or lead to this reference fuel. |

ALTERNATIVELY

| Parameter | Unit | Limits1 | Test method |
| --- | --- | --- | --- |
|  |  | Minimum | Maximum |  |
| Cetane number2 |  | 52,0 | 54,0 | EN-ISO 5165 |
| Density at 15 °C | kg/m3 | 833 | 837 | EN-ISO 3675 |
| Distillation: |  |  |  |  |
| - 50 % point | °C | 245 | — | EN-ISO 3405 |
| - 95 % point | °C | 345 | 350 | EN-ISO 3405 |
| - final boiling point | °C | — | 370 | EN-ISO 3405 |
| Flash point | °C | 55 | — | EN 22719 |
| CFPP | °C | — | – 5 | EN 116 |
| Viscosity at 40 °C | mm2/s | 2,3 | 3,3 | EN-ISO 3104 |
| Polycyclic aromatic hydrocarbons | % m/m | 2,0 | 6,0 | EN 12916 |
| Sulphur content3 | mg/kg | — | 10 | EN ISO 20846 / EN ISO 20884 |
| Copper corrosion |  | — | Class 1 | EN-ISO 2160 |
| Conradson carbon residue (10 % DR) | % m/m | — | 0,2 | EN-ISO 10370 |
| Ash content | % m/m | — | 0,01 | EN-ISO 6245 |
| Water content | % m/m | — | 0,02 | EN-ISO 12937 |
| Neutralisation (strong acid) number | mg KOH/g | — | 0,02 | ASTM D 974 |
| Oxidation stability4 | mg/ml | — | 0,025 | EN-ISO 12205 |
| Lubricity (HFRR wear scan diameter at 60 °C) | μm | — | 400 | EN ISO 12156 |
| Oxidation stability @ 110 °C4, 6 | h | 20,0 |  | EN 14112 |
| FAME5 | % v/v | 4,5 | 5,5 | EN 14078 |
| 1 The values quoted in the specifications are ‘true values’. In establishment of their limit values the terms of ISO 4259 Petroleum products – Determination and application of precision data in relation to methods of test have been applied and in fixing a minimum value, a minimum difference of 2R above zero has been taken into account; in fixing a maximum and minimum value, the minimum difference is 4R (R = reproducibility). Notwithstanding this measure, which is necessary for technical reasons, the manufacturer of fuels shall nevertheless aim at a zero value where the stipulated maximum value is 2R and at the mean value in the case of quotations of maximum and minimum limits. Should it be necessary to clarify whether a fuel meets the requirements of the specifications, the terms of ISO 4259 shall be applied. 2 The range for cetane number is not in accordance with the requirements of a minimum range of 4R. However, in the case of a dispute between fuel supplier and fuel user, the terms of ISO 4259 may be used to resolve such disputes provided replicate measurements, of sufficient number to archive the necessary precision, are made in preference to single determinations. 3 The actual sulphur content of the fuel used for the Type 1 test shall be reported. 4 Even though oxidation stability is controlled, it is likely that shelf life will be limited. Advice shall be sought from the supplier as to storage conditions and life. 5 FAME content to meet the specification of EN 14214 6 Oxidation stability can be demonstrated by EN-ISO 12205 or by EN 14112. This requirement shall be reviewed based on CEN/TC19 evaluations of oxidative stability performance and test limits |

ALTERNATIVELY

Type: Petrol (E5)

| Parameter | Unit | Limits1 | Test method |
| --- | --- | --- | --- |
|  |  | Minimum | Maximum |  |
| Research octane number, RON |  | 95,0 | — | EN 25164 prEN ISO 5164 |
| Motor octane number, MON |  | 85,0 | — | EN 25163 prEN ISO 5163 |
| Density at 15 °C | kg/m3 | 743 | 756 | EN ISO 3675 EN ISO 12185 |
| Vapour pressure | kPa | 56,0 | 95,0 | EN ISO 13016-1 (DVPE) |
| Water content | % v/v |  | 0.015 | ASTM E 1064 |
| Distillation: |  |  |  |  |
| – evaporated at 70 °C | % v/v | 24,0 | 44,0 | EN-ISO 3405 |
| – evaporated at 100 °C | % v/v | 50,0 | 60,0 | EN-ISO 3405 |
| – evaporated at 150 °C | % v/v | 82,0 | 90,0 | EN-ISO 3405 |
| – final boiling point | °C | 190 | 210 | EN-ISO 3405 |
| Residue | % v/v | — | 2,0 | EN-ISO 3405 |
| Hydrocarbon analysis: |  |  |  |  |
| – olefins | % v/v | 3,0 | 13,0 | ASTM D 1319 |
| – aromatics | % v/v | 29,0 | 35,0 | ASTM D 1319 |
| – benzene | % v/v | — | 1,0 | EN 12177 |
| – saturates | % v/v | Report | ASTM 1319 |
| Carbon/hydrogen ratio |  | Report |  |
| Carbon/oxygen ratio |  | Report |  |
| Induction period2 | minutes | 480 | — | EN-ISO 7536 |
| Oxygen content4 | % m/m | Report | EN 1601 |
| Existent gum | mg/ml | — | 0,04 | EN-ISO 6246 |
| Sulphur content3 | mg/kg | — | 10 | EN ISO 20846 EN ISO 20884 |
| Copper corrosion |  | — | Class 1 | EN-ISO 2160 |
| Lead content | mg/l | — | 5 | EN 237 |
| Phosphorus content | mg/l | — | 1,3 | ASTM D 3231 |
| Ethanol4 | % v/v | 4,7 | 5,3 | EN 1601 EN 13132 |
| 1 The values quoted in the specifications are ‘true values’. In establishment of their limit values the terms of ISO 4259 Petroleum products - Determination and application of precision data in relation to methods of test have been applied and in fixing a minimum value, a minimum difference of 2R above zero has been taken into account; in fixing a maximum and minimum value, the minimum difference is 4R (R = reproducibility). Notwithstanding this measure, which is necessary for technical reasons, the manufacturer of fuels shall nevertheless aim at a zero value where the stipulated maximum value is 2R and at the mean value in the case of quotations of maximum and minimum limits. Should it be necessary to clarify whether a fuel meets the requirements of the specifications, the terms of ISO 4259 shall be applied. 2 The fuel may contain oxidation inhibitors and metal deactivators normally used to stabilise refinery gasoline streams, but detergent/dispersive additives and solvent oils shall not be added. 3 The actual sulphur content of the fuel used for the Type 1 test shall be reported. 4 Ethanol meeting the specification of prEN 15376 is the only oxygenate that shall be intentionally added to the reference fuel. 5 There shall be no intentional addition of compounds containing phosphorus, iron, manganese, or lead to this reference fuel. |

REGULATION No. 101

Paragraph 5.2.4. amend to read:

5.2.4. 	The appropriate reference fuels as defined in annex 10 to Regulation No. 83 must be used for testing.

For LPG and natural gas (NG) that reference fuel must be used which is chosen by the manufacturer for the measurement of the net power in accordance with Regulations No. 85. The chosen fuel must be specified in the communication document as defined in annex 3 to this Regulation.

For the purpose of calculation mentioned in paragraph 5.2.3., the fuel consumption shall be expressed in appropriate units and the following fuel characteristics shall be used:

(a) density: measured on the test fuel according to ISO 3675 or an equivalent method. For petrol and diesel fuel the density measured at 15 °C will be used; for LPG and natural gas a reference density will be used, as follows:

0.538 kg/litre for LPG

0.654 kg/m3 for NG *)

(b) hydrogen-carbon ratio: fixed values will be used which are:

C1H1.85 for petrol (E0)

C1H1.86 for diesel fuel (B0)

C1H2.525 for LPG

C1H4.00 for NG.

C1H1.89O0.016 for petrol (E5)

C1H1.86O0.005 for diesel fuel (B5)

Annex 6,

Item 1.4.3. amend to read:

ANNEX 6

METHOD OF MEASURING EMISSIONS OF CARBON DIOXIDE AND FUEL CONSUMPTION OF VEHICLES POWERED BY AN INTERNAL COMBUSTION ENGINE ONLY

- SPECIFICATION OF THE TEST

1.4. 	Calculation of CO2 and fuel consumption values

1.4.3.	The fuel consumption, expressed in litres per 100 km (in the case of petrol, LPG or diesel) or in m3 per 100 km (in the case of NG) is calculated by means of the following formulae:

(a) 	for vehicles with a positive ignition engine fuelled with petrol (E0):

FC = (0.1154 / D) · [(0.866 · HC) + (0.429 · CO) + (0.273 · CO2)]

(b) 	for vehicles with a positive ignition engine fuelled with LPG:

FCnorm = (0.1212 / 0.538) · [(0.825 · HC) + (0.429 · CO) + (0.273 · CO2)]

If the composition of the fuel used for the test differs from the composition

that is assumed for the calculation of the normalised consumption,

on the manufacturer's request a correction factor cf may be applied, as follows:

FCnorm = (0.1212 / 0.538) · (cf) · [(0.825 · HC) + (0.429 · CO) + (0.273 CO2)]

The correction factor cf, which may be applied, is determined as follows:

cf = 0.825 + 0.0693 · nactual

where:

nactual = the actual H/C ratio of the fuel used

(c) 	for vehicles with a positive ignition engine fuelled with NG:

FCnorm = (0.1336 / 0.654) · [(0.749 · HC) + (0.429 · CO) + (0.273 · CO2)]

(d) 	for vehicles with a compression ignition engine diesel (B0):

FC = (0.1155 / D) · [(0.866 · HC) + (0.429 · CO) + (0.273 · CO2)]

(e)	for vehicles with a positive ignition engine fuelled with petrol (E5):

FC = (0.118 / D) · [(0.848 · HC) + (0.429 · CO) + (0.273 · CO2)]

(f)	for vehicles with a compression ignition engine fuelled with diesel (B5):

FC = (0.116 / D) · [(0.861 · HC) + (0.429 · CO) + (0.273 · CO2)]

In these formulae:

FC	=	the fuel consumption in litre per 100 km (in the case of

petrol, LPG or diesel) or in m3 per 100 km (in the case of natural gas)

HC	=	the measured emission of hydrocarbons in g/km

CO	=	the measured emission of carbon monoxide in g/km

CO2	=	the measured emission of carbon dioxide in g/km

D	=	the density of the test fuel

In the case of gaseous fuels this is the density at 15 °C.

# * * *

B.	JUSTIFICATION

Regulations 83 and 101 do not allow any biodiesel or ethanol content in the specification of the reference fuel for Type I and Type VI testing.

The specific procedures, tests and requirements for type approval, which are now under discussion in the European Community, will define future reference fuels, such as petrol, diesel, gaseous fuels and biofuels, such as bioethanol, biodiesel and biogas The current commitology proposal (version of September 2007) allows only B5 and E5 fuel as reference fuel for Type I and Type VI testing of mono-fuel vehicles.

It is reasonable to allow the use of the proposed B5 and E5 reference fuel as an alternative in Regulations 83 and 101 to avoid double testing of Type I and Type VI testing and to .allow easier export of modern Euro 5 concepts to countries outside the European Community, which apply the UN/ECE Regulations.

- - - - -