| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2009/11 17 December 2008 Original: ENGLISH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

One-hundred-and-forty-seventh session

Geneva, 10 - 13 March 2009

Item 4.2.1 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for to Supplement 11 to the 02 series of amendments to Regulation No. 3

(Retro-reflecting devices)

Submitted by the Working Party on Lighting and Light-Signalling (GRE) (/

The text reproduced below was adopted by GRE at its sixtieth session.  It is based on ECE/TRANS/WP.29/GRE/2008/31, as amended by Annex III to the report.  It is submitted to WP.29 and AC.1 for consideration (ECE/TRANS/WP.29/GRE/60, para. 22).

Insert a new paragraph 2.15., to read:

"2.15.	"Colour of the reflected light of the device" The definitions of the colour of the reflected light are given in paragraph 2.30. of Regulation No. 48."

Paragraph 5.2., amend to read:

"5.2.	If the approval granted in respect of a retro-reflecting device is extended to other such devices differing only in colour, the two samples in any other colour submitted in conformity with paragraph 3.1.4. of this Regulation shall be required to meet only the colorimetric specifications, the other tests ...."

Annex 4,

Paragraph 2., amend to read:

"2.	After verification of the general specifications (paragraph 6 of the Regulation) and the specifications of shape and dimensions (Annex 5), the ten samples shall be subjected to the heat resistance test described in Annex 10 to this Regulation and at least one hour after this test examined as to their colorimetric characteristics and CIL..."

Paragraph 3.1., amend to read:

"3.1.	a colour which satisfies the conditions laid down in paragraph 2.30. of Regulation No. 48 for clear, red or amber retro-reflecting devices. This shall be ..."

Annex 6,

Insert new paragraph 2., to read:

"2.	For checking the colorimetric characteristics, paragraph 2.30. of Regulation No. 48 applies."

Paragraphs 2. and 3. (former), to be deleted.

Annex 14,

Paragraph 2., amend to read:

"2.	… and one hour minimum after this test examined as to their colorimetric
characteristics  and CIL ..."

Paragraph 4.1., amend to read:

"4.1.	A colour which satisfies the conditions laid down in Regulation No. 48, paragraph 2.30.  This shall be ..."

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.