| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2009/13 17 December 2008 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-seventh session

Geneva, 10 - 13 March 2009

Item 4.2.3 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Supplement 18 to the 01 series of amendments to Regulation No. 6

(Direction indicators)

Submitted by the Working Party on Lighting and Light-Signalling (GRE) (/

The text reproduced below was adopted by GRE at its sixtieth session.  It is based on ECE/TRANS/WP.29/GRE/2008/51, not amended.  It is submitted to WP.29 and AC.1 for consideration (ECE/TRANS/WP.29/GRE/60, para. 26).

Annex 1, amend to read:

"……..

(ii)	direction indicator lamps of Category 6, for which they are 30( above and 5( below the horizontal.

Minimum horizontal visibility angles

Direction indicators for the front of the vehicle

Category 1: 	for use at a distance not less than 40 mm from the headlamp;

Category 1a:	for use at a distance greater than 20 mm but less than 40 mm from the headlamp;

Category 1b: 	for use at a distance less than 20 mm from the headlamp.

H plane : "horizontal plane going

through the reference centre

of the lamp"

Categories 2a and 2b:  direction indicator…."

Annex 2,

Item 9, amend to read:

"9	Concise description

……..

Light source module specific identification code:.........................................................

Only for installation on M1 and/or N1 category vehicles: yes/ no 2/

Only for limited mounting height of equal to or less than 750 mm above the ground: yes/ no 2/

..........."

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.

# Text boxes

Vehicle

Reference axis

Driving

direction

Reference axis

45°

80°

20°

iving

direction

Reference axis

80°

Vehicle

s to be mounted on the right side of the vehicle. The

Vehicle

Driving

direction

Reference axis

45°

80°

20°

Reference axis

80°

Vehicle

Vehicle

Driving

direction

Reference axis

45°

80°

45°

On and above the H plane for all lamps.

Under the H plane for

lamps intended for M2, M3 or N2 category of vehicles

80°

Driving

direction

Vehicle

Reference axis

Reference axis

Under the H plane for

M1 and N1 category of vehicles

20°

20°

80°

80°

Driving

direction

Vehicle

Vehicle

H plane: "horizontal plane going through the reference centre of the lamp"