| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2009/99 23 July 2009 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-ninth session

Geneva, 10-13 November 2009

Item 4.2.11 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Corrigendum 1 to Supplement 4 to the 02 series of amendments to Regulation No. 46 (Devices for indirect vision)

Submitted by the Working Party on General Safety (/

The text reproduced below was adopted by the Working Party on General Safety (GRSG) at its ninety-sixth session.  It is based on ECE/TRANS/WP.29/GRSG/2009/4, not amended.  It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRSG/75, para. 25).  The proposal will be revised by GRSG at its October 2009 session.

Amend paragraph 1., to read:

"1.	SCOPE

This Regulation applies:

(a)	to compulsory and optional devices for indirect vision, set out in the table under paragraph 15.2.1.1.1. for vehicles of category M and N 1/ and to compulsory and optional devices for indirect vision mentioned in paragraphs 15.2.1.1.3 and 15.2.1.1.4 for vehicles of category L 1/with bodywork at least partly enclosing the driver,

(b)	to the installation of devices for indirect visions on vehicles of categories M and N and on vehicles of category L 1/ with bodywork at least partly enclosing the driver.

______________

1/  As defined in Annex 7 to the Consolidated Resolution on the Construction of Vehicles (R.E.3) (TRANS/WP.29/78/Rev.1/Amend.2 as last amended by Amend.4)

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.